## Slide 1: AP223 conformace classes
Len Slovensky

## Slide 2: Cast parts Architecture
STEP
Translator
CC1-Design
engineering
drawing
Native
CAD
drawing
Order
Manager
STEP
Validator
CC4-
Customer
to
foundry
Reference
Customer
Foundry
STEP
Translator
Foundry
Process
Planning
CC2-Cast
part design
(cast shape,
casting
requirements)
CC5 -
Metal caster
to
tooling shop
Reference
Tooling shop
STEP
Translator
CC3-Cast part
tooling
(near net shape+
gating system+
Pattern features)
Simulation
Simulation
CC8 –
Metal caster
to
simulation
Inspection
Inspection
CC6 –
Metal caster
to
inspection
Reference
Tooling
Manager
AP219
(dimensional
inspection)
Machining
CC7 –
Metal caster
to
machining
Process
Planning

## Slide 3: Conformance class 1
CC1 – Design engineering drawing
    Geometry
      B-rep
    Material
      And alternate material
    Machining features
      Boss, pocket, hole,
    Tolerances
      geometric and dimensional
    Properties
      Surface, part property, material
Design
engineering
drawing

## Slide 4: #1 capture design drawing
Convert native CAD drawing to AP223 design engineering drawing
STEP
Translator
Native CAD drawing
CC1-Design
engineering
drawing

## Slide 5: #2 validate design drawing
Validate accuracy of STEP file
CC1-Design
engineering
drawing
STEP
Validation
Validation report

## Slide 6: Conformance class 2
CC2 – Cast part design
  Near net shape
    Casting a part very close to the required end shape so that it requires almost no machining.
  Draft for Patterns & Castings
    Pattern Draft is the taper allowed on the vertical surface of a pattern to permit withdrawal of the casting from the mold. Casting draft is the actual draft angle on the casting.
  Parting Line and Parting Line Tolerances
    The mark or line on a casting formed at the junction of cope and drag section where the mold parts. Its location and draft are determined during the design process.
  Cast features
    Features of a casting formed by the pattern, mold and cores rather than machined as a post-casting operation. Typical cast in features include walls, fillets, ribs and bosses.
  Cored out features
    Features formed by cores inserted into a mold. Typically they are hollowed-out interior or cavity features in a casting which could not be formed using a pattern or by machining.
  Metal inserts, cast in part
    Metal inserts may be cast into parts by placing the inserts into the mold before pouring the alloy.
  Finish Allowance
    Additional cast on material (machine stock) that is to be machined away from the surface of the casting.
  Surface finish “as cast”
    "As cast” finish is depending on alloy, size of part, molding process and tooling quality.
Cast part design
(cast shape, casting requirements)

## Slide 7: #3 capture design drawing
Convert native CAD drawing to AP223 cast part drawing
STEP
Translator
CC2-Cast part design
(cast shape, casting requirements)
Native CAD drawing

## Slide 8: #4 validate design drawing
Validate accuracy of STEP file
STEP
Validation
Validation report
CC2-Cast part design
(cast shape, casting requirements)

## Slide 9: Conformance class 3
CC3 – Cast part tooling
  Cope - Top half of a horizontally parted flask, mold, or pattern.
  Drag - Bottom half of a horizontally parted flask, mold, or pattern.
  Cope/Drag plates - The cope (top) half of the pattern is mounted to the cope plate. The drag (bottom) half of the pattern is mounted to the drag plate.
  Flask - A rigid metal or wood frame used to hold sand from which a mold is formed.
  Master pattern - A pattern constructed with double shrinkage allowance, from which cast production patterns are made.
  Match plate - A plate made from a master pattern that forms both the cope and drag parts of the mold.
  Mold - The form shaped by a pattern, made of sand, metal, or refractory material, which contains the cavity into which molten metal is poured to produce a casting of the desired shape.
  Mold cavity - The impression in the mold produced by removal of the pattern.
  Pattern - A form made of metal, plastic, wood, or other material, around which molding material is placed to make a mold for casting metal.
  Loose pattern - A pattern not affixed to a plate, used to make molds for castings.
  Pattern plate - Pattern affixed to a plate to make both the cope and drag halves of a mold.
  Permanent mold - the mold used to produce castings in the permanent mold process.
  Runner - The portion of the gate feature in the mold that connects the down sprue with the casting, ingate, or riser.
  Riser - the gating system that forms the reservoir of molten metal necessary to compensate for losses due to shrinkage as the metal solidifies.
  Sprue - A vertical cut or hole into the mold that allows molten metal to flow into the mold.
  Ingate - The portion of the gate system that introduces metal into the casting cavity.
  Vent - Small opening or passage in the mold or core to facilitate the escape of gases when the mold is poured.
  Chills - A metal insert in the sand mold used to produce localized chilling and control the rate of casting solidification.
Cast part tooling
(AP224+gating system+
Pattern features)

## Slide 10: #5 capture cast part tooling
Convert native CAD drawing to AP223 design engineering drawing
STEP
Translator
Native CAD drawing
CC3-Cast part tooling
(near net shape+gating system+
Pattern features)

## Slide 11: #6 validate cast part tooling drawing
Validate accuracy of STEP file
STEP
Validation
Validation report
CC3-Cast part tooling
(near net shape+gating system+
Pattern features)

## Slide 12: Conformance class 4
CC4 – Customer to foundry request for bid (RFQ)
  Bidding information
  Buyer/ company information
  Part/casting identification
  Delivery schedule
  Casting/molding process
  Alloy requirement
  Drawing
Customer to
foundry

## Slide 13: #7 customer send RFQ
Customer order manager
CC4-Customer to
foundry
CC1-Design
engineering
drawing
Reference
Reference

## Slide 14: Conformance class 4
CC4 – Customer to bid winning foundry for additional customer requirements
  Customer service data
    Mechanical stress requirements
    Wear or abrasion
    Corrosion service
    Elevated temperature service
    Machining operations
    Finishing operations
  Casting production and quality requirments
  Specifications
  Mechanical testing and chemical analysis
  Heat treatment
  Tolerances
  Special inspection requirements
Customer to
foundry

## Slide 15: #8 customer to foundry who won bid
Customer order manager
CC4-Customer to
foundry
CC1-Design
engineering
drawing
Reference
CC3-Cast part tooling
(near net shape+gating system+
Pattern features)

## Slide 16: Conformance class 5
CC5 – defines the exchange between the Metal caster to tooling shop
  Part design
    Data not in CC5 but is a reference to CC1
  Cast part pattern
    Data not in CC5 but is a reference to CC3
  Cast part
    Data not in CC5 but is a reference to CC2
  Customer casting requirements
  Tooling requirements
    Type of tooling, cores to be made, required gating, type of casting process
CC5-Metal caster to
tooling shop

## Slide 17: #9 foundry to tooling shop
Foundry order manager
CC1-Design
engineering
drawing
Reference
CC3-Cast part tooling
(near net shape+gating system+
Pattern features)
CC5-Metal caster to
tooling shop
CC2-Cast part design
(cast shape, casting requirements)

## Slide 18: #10 - Metal caster to inspection
AP224
Reference
AP219
(dimensional inspection)
CC6-Metal caster
to inspection
Cast part
(AP224+gating system+
Casting requirements)

## Slide 19: #11 - Metal caster to machining
AP224
Reference
CC7-Metal caster
to machining
Cast part
(AP224+gating system+
Casting requirements)

## Slide 20: #12 - Metal caster to simulation
Reference
Cast part
(AP224+gating system+
Casting requirements)
CC8-Metal caster
to simulation

## Slide 21: #13 - Metal caster to other operations
AP224
External
Reference
Cast part
(AP224+gating system+
Casting requirements)
CC9-Metal caster
to Other operations

## Slide 22: #14- Casting process planning
AP224
External
Reference
AP219
(dimensional inspection)
CC10-Casting
Process
Plan
Cast part
(AP224+gating system+
Casting requirements)
Cast part tooling
(AP224+gating system+
Pattern features)

## Slide 23: Cast parts Architecture
STEP
Translator
CC1-Design
engineering
drawing
Native
CAD
drawing
Order
Manager
STEP
Validator
CC4-
Customer
to
foundry
Reference
Customer
Foundry
STEP
Translator
Foundry
Process
Planning
CC2-Cast
part design
(cast shape,
casting
requirements)
CC5 -
Metal caster
to
tooling shop
Reference
Tooling shop
STEP
Translator
CC3-Cast part
tooling
(near net shape+
gating system+
Pattern features)
Simulation
Simulation
CC8 –
Metal caster
to
simulation
Inspection
Inspection
CC6 –
Metal caster
to
inspection
Reference
Tooling
Manager
AP219
(dimensional
inspection)
Machining
CC7 –
Metal caster
to
machining
Process
Planning