## Slide 1
LSC Demonstration Environments
discussion document
Toulouse June 2006
Alan Crawford
alc@lsc.co.uk
7th March 2006

## Slide 4: Main Alternative ~ 28th Feb
Use existing feature method
  Only use geometry within scope of ShopMill
    Simplify geometry of part
    Or only machine simple elements of part
  Request and use ShopMill from Siemens
    on the 840D controller
Option advantages / disadvantages
  Feature based –benefit for a product range
  Not a comprehensive approach
  Demonstrates the potential advantages for the use of higher conformance classes – later development
  Retains STEP based production approach

## Slide 6: Milestones (1)
demonstration scenario validation STEP meeting
  Cc3 & cc2 rough and finish for Airbus
  Cc2 for Boeing part – manufactured @ Airbus
  Simple feature based legacy 2D drawn part
demonstration scenario validation (including Boeing review) - 17th March
Select site for machining – end of march
Airbus design manufacturing input – end of march
    Tooling used, number of set-ups
    Cutting sequence constraints
    Drawings/designs available
Prepare – end of march
  Rough/removal feature – outline process
  Prepare – rough/removal feature – example format

## Slide 7: Milestones (2)
first version of the
  roughing AP238 cc3 file generation
  roughing profile ??28th April??
first version of the finishing program
  15th May
final demonstration scenario and final version of the programs
  15th June

## Slide 8: To confirm
Location of machining task
  University or at Airbus
  Identify Airbus machining expert to be involved
Demonstration suggestion
  Rough using feature based
  Finish using cutter path
Will the Boeing part be made in demonstration?
Availability of software & converters

## Slide 9: Actions
Distribute AP203 version of the part?
  ALC
Can an AP224 file be produced by the Japanese machining model?
Check on method of holding part
Prepare in-stage machined components
For simple part – can the CL data be output by EdgeCAM in APT CL ASCII? ALC

## Slide 10: Information required from Airbus
Manufacture process
    Billet shape [AB common aluminium, material 400 * 400 * 50]
    Device holding (clamp oversize material)
    Tooling used, number of set-ups
    Cutting sequence constraints
Machine configuration
  Tools
  Table tilt or 5 axis (B & C table tilt) [tbc]
  Huron KX50

## Slide 11: Confirmed limits for demonstration
Limits on a non-perfect part
  Single set-up
  No tolerance considerations
  Roughing technique different from finishing