## Slide 1
Proposal for an Harmonized Traceability-enabled AP238.
Julio Garrido Campos
jgarri@uvigo.es
E.T.S. Ingenieros Industriales de Vigo
Departamento de Ingeniería de Sistemas y Automatica
SC4 Technical Forum,
Italy, March 2006
AP 238 Traceability Proposals

## Slide 2: Document Purpose.
How to Implement Traceability?
  Which Activity Model Scope?
    Traceability configuration into design STEP APs?
  Traceability Automation.
    AP-238 traceability workingsteps or instruction codes?
    AP-238 traceability data collection. Machine Traceability Capabilities?
Which Information (Harmonization)?
  Information Requirements (Harmonized and new requirements)?
    Which Characteristics?
    Which Static Data Type?
      materials, tools, other generic resources?
    Which Dynamic Data Type?
      Process timeStamps, Controller Events?
Questions to be answered and decissions to be taken

## Slide 3: Document Index.
Part 1: Purpose and Objectives.
  Traceability Background & Questions Intro.
    Traceability Activity Model.
    Traceability data in AP238.
  Activity Model Questions.
  Data Model Questions (Traceability Harmonization).
    STEP Traceability Approaches & Harmonization.
    “Static Data Type Information”
      Product characteristics.
      Generic manufacturing resources.
        Materials Harmonization.
        Other manufacturing resources.
    “Dynamic Data Type Information”
      Traceability Automation.
      Workingsteps Data.
Part 2: Questions Summary and Decisions to Make.
  Questions Summary.
  Decisions.

## Slide 4: Part 1: Traceability Activity Model (1)
Questions:
  1 Where and How to Integrate Traceability Processes (ACTIVITIES) into AP238 scenario ?
  2 Which traceability requirements?.
Trace the
manufacturing
of a product
A0
STEP Product Data
(AP238????)
CNC Controllers &
Machine Tools
Machine
Operators
Raw
Materials
Customer
Requirements
Standard Regulations
for Traceability
NC Machines
Traceability Capabilities
Collected Traceability Manufacturing Data
Collected Characteristics Part Manufacturing Data
Manufacturing process Analysis/Audit/Check
Part 1: Purpose and Objectives.
   Questions Introduction.
   Manufacturing Traceability
   Traceability Activity Model.
   Traceability Data in AP328.

## Slide 5: Part 1: Traceability Activity Model (2)
Questions:
  1 Where and How to Integrate Traceability Processes (ACTIVITIES) into AP238 scenario?
  2 Which traceability requirements?.
Configure
Traceability
A01
Execute
Traceability
A02
Analyze
Traceability
A03
Traceability Specifications
Product
Data
Workpiece
Manufacturing
Data (AP238)
Traceability
Instruction
Codes (into AP238 ?)
AP-238
Traceability
Scope
Traceability Data
Traceability Audit
Traceability
Collected
Data
Workpiece
Data
Manufacturing
Process Data
(Other)
Part 1: Purpose and Objectives.
   Questions Introduction.
   Manufacturing Traceability
   Traceability Activity Model.
   Traceability Data in AP328.
Statistical
Quality Control
(after manufacturing)
CLIENT manufacturing Prerequits
Casting Prerequisits
(AP223)

## Slide 6: Part 1:Traceability Data in AP238 (1)
STATIC DATA ?
Questions:
  1 Where and How to Integrate Traceability Processes into AP238?
  2 Which traceability data (requirements)?
WorkPiece RESOURCES:
Materials, Machine, Workers:
Identification, origin, storage …
WorkingStep RESOURCES:
Selected Tools identification,
Worker identifiaction …
DYNAMIC DATA ?
WorkingStep Execution Results:
TimeStamps,
Controller Events: (Alarms,
Manual & Automatic mode Changes
CHARACTERISTICS DATA ?
WorkPiece Characteristics &
Feature Oriented Data.
Tolerances, Well Defined
Process and Workpiece Characteristics
PROPERTIES
Part 1: Purpose and Objectives.
   Auestions Introduction.
   Manufacturing Traceability
   Traceability Activity Model.
   Traceability Data in AP328.

## Slide 7: Document Index.
Part 1: Purpose and Objectives.
  Questions Introduction.
    Traceability Activity Model.
    Traceability data in AP238.
  Activity Model Questions.
  Data Model Questions (Traceability Harmonization).
    STEP Traceability Approaches & Harmonization.
    “Static Data Type Information”
      Product characteristics.
      Generic manufacturing resources.
        Materials Harmonization.
        Other manufacturing resources.
    “Dynamic Data Type Information”
      Traceability Automation.
      Workingsteps Data.
Part 2: Questions Summary and Decisions to Make.
  Questions Summary.
  Decisions.

## Slide 8: Part 1: Activity Model Questions (1)
Traceability Processes need BIDIRECTIONAL exchange data flow.
  () Requirements or “TO BE” data, from DESIGN to MANUFACTURE.
  () Collected Data or “AS IS” data, from MANUFACTURE to DESIGN.
Design
Detailing
Path Planning
Manufacturing
CAD
CADD
CAM
CNC CONTROL
Integrated CAD/CAM
AP203
AP224
AP203 Ed2
AP238
“TO BE” data
[traceability requirements]
“AS IS” data
[collected data]
INPUT
OUTPUT
Part 1: Purpose and Objectives.
   Questions Introduction.
  Activity Model Questions
   Data Model Questions.

## Slide 9: Part 1: Activity Model Questions (2)
“To be”
Traceability data
requirements
Question:
  “STEP integrated Traceability” in STEP-enabled Manufacturing Scenarios?
Why Yes?:
    Traceability Data as another “view” of product is to be integrated with common product data.
    Traceability Exchange Paths in extended enterprises are the same as other STEP product data.
    Traceability Configuration will allow customers to explicit its traceability requirements.
    Traceability data Collection will allow traceability automation during machining.
Customer
Product design
requirements
Manufacturer
PRODUCT DATA EXCHANGE IN STEP FORMAT
“AS IS”
Traceability
collected data
NC- Machines &
Controllers
Enterprise Data
Management Tools
PROPOSED DATA EXCHANGE IN STEP FORMAT
Part 1: Purpose and Objectives.
   Questions Introduction.
  Activity Model Questions
   Data Model Questions.

## Slide 10: Part 1: Activity Model Questions (3)
NC- Machines
& Controllers
Questions: TRACEABILITY PROCESS CONFIGURATION:
  NC Traceability-ENABLED MACHINES (Machine Capabilities )?
AP238 Manufacturer
“AS IS”
Traceability
collected data
AP238 data
traceability
configuration
data in AP238 ?
Part 1: Purpose and Objectives.
   Questions Introductin.
  Activity Model Questions
   Data Model Questions.
T-CC1
T-CC2
T-CC3
T-CC4
T-CC5
“TO BE”
Traceability
configuration data
Traceability Configuration:
1-Traceablity Configured
Conformance Classes:
T-CC1: no traceability
T-CC2: characteristics
T-CC3: static data
T-CC4: dynamic data
T-CC5: full
T-CC6: …
2-Selection in STEP AP designs
3-Hybrid Solution.
    Information to perform Traceability operations (tolerances?)?
        1- Selection in STEP AP designs (Properties)

## Slide 11: Part 1: Activity Model Questions (4)
Questions: TRACEABILITY INPUT PROCESSES: AUTOMATIC PROCESS!!!!!!
    1. WHERE TO MAKE EXPLICIT these REQUIREMENTS ?
    2. HOW TO COMMUNICATE & UNDERSTAND these requirements ?
Requirements in the extended enterprise.
  configuration data flow from design to manufacturing at diferent product life cycle stages.
    (I) Customer (design: Ap203Ed2/AP224) .
    (II) Subcontractor (planning AP240/AP224).
    (III) Manufacturer (machinning AP238).
Virtual Enterprise
possible INPUT points for Traceability Requirements
AP203
AP224
“To be”
Traceability data
requirements
Product design
requirements
Enterprise Data
Management Tools
Main Customer
“To be”
Traceability
data
requirements
Macro design
requirements
Enterprise Data
Management Tools
Macro Planning
“To be”
Traceability
data
requirements
Micro design
requirements
Micro Planning
AP224
AP240
“As IS”
Traceability
data
Collected
Machining
AP238
Part 1: Purpose and Objectives.
   Question Introduction.
  Activity Model Questions
   Data Model Questions.

## Slide 12: Part 1: Activity Model Questions (5)
Questions: TRACEABILITY OUTPUT PROCESSES.
  Traceability DATA PLACE HOLDERS?.
  AP238 Scope to be Extended to include traceability Data?.
  AP238 as AP to communicate back collected traceability Data?.
AP238 Manufacturer
“AS IS”
Traceability
collected data
NC- Machines &
Controllers
Well Defined
Output Point
AP238 ?
How to comunicate back these traceability data ?
Part 1: Purpose and Objectives.
   Questions Introductin.
  Activity Model Questions
   Data Model Questions.
“TO BE”
Traceability
data
Product design
requirements
Enterprise Data
Management Tools
Main Customer
Traceability DATA PLACE HOLDERS:
1-INCLUSIVE AP238:
- Specific entities for “AS IS”
2- “AS IS” data as non step files
“AS IS”
Traceability
data

## Slide 13: Document Index.
Part 1: Purpose and Objectives.
  Questions Introduction.
    Traceability Activity Model.
    Traceability data in AP238.
  Activity Model Questions.
  Data Model Questions (Traceability Harmonization).
    STEP Traceability Approaches & Harmonization.
    “Static Data Type Information”
      Product characteristics.
      Generic manufacturing resources.
        Materials Harmonization.
        Other manufacturing resources.
    “Dynamic Data Type Information”
      Workingsteps.
      Traceability Automation.
Part 2: Questions Summary and Decisions to Make.
  Questions Summary.
  Decisions.

## Slide 14: Part 1: STEP Traceability Approaches & Harmonization. (1)
Approaches to traceability in STEP.
  AP223 for Casting.
  AP238 Traceability Purpose ad Objectives:
    STEP-EXPRESS information model for automation of traceability processes in AP-238 manufacturing processes. (including assembled products)
    Enable “Traceability Applications and processes” to communicate with manufacturing, design and process planning applications and processes.
    Machine interpretable electronic exchange of traceability requirements and traceability collected data, ensuring fast traceability process response (understandability and avaliability).
Mold Design
Cast Process Simulation
Quality Control Records & Documents
Process Plan & Process Activities
Administrative Data
Casting Requeriments
Materials & composition
Tolerances
Properties
Features
Shape Representation
Part Model
AP223
Part 1: Purpose and Objectives.
   Question Introduction.
   Activity Model Questions.
   Data Model Questions.
   STEP Traceability Approaches
  & Harmonization.

## Slide 15: Part 1: STEP Traceability Approaches & Harmonization. (2)
Some Harmonized Functional Units across STEP APs
  AP224, 240 & 238.
AP224 |  | 
Part Model | Shape Representation | Features
Properties | Tolerances | Materials
Process Control | Administrative Data | Requisitions
Process requirement Documents |  | 
AP240 |  | 
Part Model | Shape Representation | Features
Properties | Tolerances | Materials
Machine tool Resources | Administrative Data | Process Plan & Process Activities
Process requirement Documents |  | 
AP238 |  | 
 |  | Features
 | Tolerances | 
 | Administrative Data (Management UOF) | 
 | Milling, Turning & EDM Processes (ISO 14649) | 
Part 1: Purpose and Objectives.
   Questions Introduction.
   Activity Model Questions.
   Data Model Questions.
   STEP Traceability Approaches
  & Harmonization.

## Slide 16: Part 1: STEP Traceability Approaches & Harmonization. (3)
Milling, Turning & EDM Processes (ISO 14649)
Administrative Data (Management UOF)
Tolerances
Features
AP238
Some Harmonized Functional Units across STEP APs
  Proposed extended Ap238 (scope) with Harmonized UOF addressing traceability information requirements.
Process requirement Documents
Requisitions
Administrative Data
Process Control
Materials
Tolerances
Properties
Features
Shape Representation
Part Model
AP224
Process requirement Documents
Process Plan & Process Activities
Administrative Data
Machine tool Resources
Materials
Tolerances
Properties
Features
Shape Representation
Part Model
AP240
Traceability Data Records
Properties (Characteristics Data)
Part 1: Purpose and Objectives.
   Questions Introduction.
   Activity Model Questions.
   Data Model Questions.
   STEP Traceability Approaches
  & Harmonization.

## Slide 17: Part 1: STEP Traceability Approaches & Harmonization. (4)
Some Harmonized Functional Units across STEP APs
  Proposed extended Ap238 (scope) with Harmonized UOF addressing traceability information requirements.
  If Properties, Characteristics, or traceability data are “to BE” specified in AP224,AP240, and recorded during machining, DATA PLACEHOLDERS are necessary to collect this data.
CAD/CAM
System
CAD/CAM
Translator
AP-238
File
AP-203/224/240
CNC
System
Customer
Shop
Manufacturing
+ traceability configuration
+ traceability
AP203/224/240
“TO BE” data ?
AP-238 code
(sample traceability)
#probing operations
#get_controller_data
#get_workingstep_time
………..
AP-238 “AS IS”
collected data ?
Properties
Traceability data
Part 1: Purpose and Objectives.
   Questions Introduction.
   Activity Model Questions.
   Data Model Questions.
   STEP Traceability Approaches
  & Harmonization.
Properties
Traceability data
Properties
Traceability data

## Slide 18: Document Index.
Part 1: Purpose and Objectives.
  Questions Introduction.
    Traceability Activity Model.
    Traceability data in AP238.
  Activity Model Questions.
  Data Model Questions (Traceability Harmonization).
    STEP Traceability Approaches & Harmonization.
    “Static Data Type Information”
      Product characteristics.
      Generic manufacturing resources.
        Materials Harmonization.
        Other manufacturing resources.
    “Dynamic Data Type Information”
      Traceability Automation.
      WorkingStep Data.
Part 2: Questions Summary and Decissions to Make.
  Questions Summary.
  Decisions.

## Slide 19: Part 1: Product Characteristics. (Data Model Questions - 1)
AP 238: Static Data: Recording Product Characteristics.
  Part properties are defined in APs (223,224,240), if interpreted as requirements and specifications used to control manufacturing conditions, in terms of AP238, there is no data placeholder for collecting specified characteristics. There is no way to integrate data generated when the product will be manufactured, or characteristics as “as is” data.
  Proposal:
material_property S[0:?]
material_identifier
standard_identifier
clamping_positions S[0:?]
its_material
its_id
global_tolerance
its_geometry
1,66(40,40,29,5,5,2)
Workpiece
(AP238)
Material
(AP238)
Property (AP224)
Part 1: Purpose and Objectives.
   Questions Introduction.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Product Characteristics

## Slide 20: Part 1: Product Characteristics. (Data Model Questions - 2)
Property
(AP224)
SPECIFICATION
(AP223/223/240)
property_name
STRING
property_characteristic S[0:?]
Shape_aspect/Shape_element
material_characteristic S[0:?]
Material_
property (AP224)
material_characteristic S[0:?]
Material
(AP224)
part_property_ characteristic S[0:?]
process_ characteristic S[0:?]
surface_ characteristic S[0:?]
feature_ characteristic S[0:?]
workingstep _ characteristic S[0:?]
property_
characteristic S[0:?]
Property_parameter (AP224)
Part_
property (AP224)
Process_
property (AP224)
property_
characteristic S[0:?]
Workpiece (AP238 Part)
Workpiece.its_traceable_characteristic
(INV) applied_to
Surface_
property (AP224)
property_
characteristic S[0:?]
Feature_
property (AP238)
property_
characteristic S[0:?]
(ABS) manufacturing_feature (AP238)
its_feature
WorkingStep_
property (AP238)
Property_parameter (AP224)
(ABS) workingstep (AP238)
its_workingstep
property_
characteristic S[0:?]
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Product Characteristics

## Slide 21: Part 1: Materials. (Data Model Questions - 3)
AP 238: Static Data: Recording Material Data.
  Material properties, can be regarded as an “special” kind of product characteristics, AP238, cover material properties, with the “material_property” attribute of the “material” entity included in the “workpiece” UOF, but in a limited fashion, as these are modeled as set of “property parameter”. Data related to materials covers both characteristics and some traceability information needed, so it is also interested to harmonize the concept of materials between APs and to add some extra information requirements needed for traceability processes.
material_property S[0:?]
material_identifier
standard_identifier
clamping_positions S[0:?]
its_material
its_id
global_tolerance
its_geometry
1,66(40,40,29,5,5,2)
Workpiece
(AP238)
Material
(AP238)
property_parameter
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Chatacteristics
     Materials.

## Slide 22: Part 1: Materials. (Data Model Questions - 4)
AP 238: Static Data: Recording Material Data.
  Proposal: It is important to note also here the distinction between material_identifier and standard (they identified the type of material used: as example in AP223: “The material_id specifies a word or group of words that make up the unique designation of the material.”), and added LOT/ITEM identifiers needed for traceability purposes, identifying the batch of used material and possible the concrete unit in this material lot.
material_hardness S[0:?]
Hardness
material_property S[0:?] (AP223/224/240
material_characteristics S[0:?])
material_identifier (AP224 material_id)
standard_identifier (AP238)
Material
(AP224)
label
label
Material_
_property
(AP223/
AP224/
AP240)
STRING
stock_size (AP224)
property_parameter
property_characteristics S[0:?]
SPECIFICATION
(AP223/223/240)
material_specification S[0:?]
LOT
(AP223)
traced_lot
production_date (AP223)
lot_id
label
date
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Chatacteristics
     Materials.

## Slide 23: Part 1: Generic Manufacturing Resources. (Data Model Questions - 5)
AP 238: GENERIC Static Traceability Data. (Traced workPiece)
  Traceability should be as per MANUFACTURED PRODUCT basis (workPiece).
  Traceability configuration is “TO BE” data, Traceability Data is “AS IS” collected data.
clamping_positions S[0:?]
its_id
global_tolerance
its_geometry
1,66(40,40,29,5,5,2)
Workpiece
(AP238)
its_workpiece
(“AS IS” data placeholders)
Traced_Workpiece
material_identifier (AP224 material_id)
standard_identifier (AP238)
Material
(AP224)
label
label
STRING
stock_size (AP224)
traced_lot (traceability UOF)
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Chatacteristics
     Materials.
     Generic Resources.
LOT
(AP223)

## Slide 24: Part 1: Generic Manufacturing Resources. (Data Model Questions - 6)
AP 238: Static Traceability Data: Traced WorkPiece
  Traceability configuration is “TO BE” data, Traceability Data is “AS IS” collected data.
Management HARMONIZED UOF
traced_item (traceability UOF)
Traced_Workpiece
its_workpiece
requirements_specified_by L[1:?]
(ABS)
Traced_WorkingStep
requirements_documented_by L[1:?]
STRING
Specification
(ABS) Document_file
LOT
(AP223)
label
date
traced_lot (traceability UOF)
description
lot_id
Machine AP240 HARMONIZED UOF
Machine
(AP240)
id
comapny_model
comapny_name
Controller
controlled_by
controller_model
controller_name
controller_specification
used_machine
Approval
Traceability_authorization L[1:?]
Traced_Operations S[0:?]
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Chatacteristics
     Materials.
     Generic Resources.

## Slide 25: Document Index.
Part 1: Purpose and Objectives.
  Questions Introduction.
    Traceability Activity Model.
    Traceability data in AP238.
  Activity Model Questions.
  Data Model Questions (Traceability Harmonization).
    STEP Traceability Approaches & Harmonization.
    “Static Data Type Information”
      Product characteristics.
      Generic manufacturing resources.
        Materials Harmonization.
        Other manufacturing resources.
    “Dynamic Data Type Information”
      Automation.
      WorkingSteps Data.
Part 2: Questions Summary and Decisions to Make.
  Questions Summary.
  Decisions.

## Slide 26: Part 1: Dynamic Data Type. (Automation 1)
AP 238: Adding Traceability Capabilities to NC-Machines ?
  Some Data collecting operations for both traceability and characteristics could be performed through “Touch_Probing” workingsteps.
  These data collecting operations (1) would include all kind of operations which imply machine axis movement.
  However there are other set of operations that could be performed by the NC-controller, (which don’t imply machine axis movements), and can be group under the NC-functions.
executable
PROGRAM STRUCTURE
NC_functions (2)
WorkingSteps
Machinning_workingsteps
Touch_probing (1)
WORKPLAN
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 27: Part 1: Dynamic Data Type. (Automation 3)
AP 238: Adding Traceability Capabilities to NC-Machines ?
  Proposal and Work ?
ABS(nc_function) executable
get _Non_Machinning_data
program_stop
exchange_pallet
optional_stop
set_mark
wait_for_mark
index_pallet
index_table
display_message
load_tool
unload_tool
nc_legacy_fucntion
(ABS)Data_
placeHolder
Its_recorded
_data
get_tool_data
get_time
Date
Its_recorded
_data
Its_recorded
_time
(ABS)Data_
placeHolder
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 28: Part 1: Dynamic Data Type. (Automation 2)
AP 238: Adding Traceability Capabilities to NC-Machines ?
  (Proposal) Enhancing NC functions, with “generic” instructions code for data collection. Sample:
    get_time : get current time for the selected operation. This code should be used for registering starting and ending times for traced operations (workingstep).
    get_tool_data : traceability information necessary for identifying the tool. This could be the right point to collect this data as traceability recorded tool data, should identify the concrete tool used, not it’s characteristics. (14649 PARTS 111)
    more to_be_defined… ?
WS #10
WS #11
WS #20
Instructions for AP 238
traced Workingstep
#get_time_WS(&Start_time)
#axis_movement(………...)
………………………………
#load tool(…………………)
………………………………
………………………………
………………………………
……………………………… ………………………………
………………………………
………………………………
#get_time_WS(&End_time)
Program flow
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 29: Part 1: Dynamic Data Type. (Automation 4)
AP 238: Dynamic Traceability Data: Traced WorkingSteps.
  AP-238 is to be executed by NC machines.
  Traceability data should include Knowledge about controller-asociated events when executing a workingstep (example, a warning an alarm).
Controller Traceable Status
& Events
Resume
AUTO
STOP
MANUAL
WARNING
Change to Auto
Change to
Manual
Alarm
No Error
ABS(nc_function) executable
program_stop
optional_stop
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 30: Part 1: Dynamic Data Type. (Working Step Data 1)
AP 238: Tracing Controller Events (Workingstep Execution).
- dynamic data samples (1)-
Execution samples
0s 5s
START
END
(ABS)
Traced_WorkingStep
TimeStamp
workingstep_time
Event
execution_events S[0:?]
0
5
END
Event
execution_events S[0:?]
0s 1…..2 5s
START
WARNINGS
WARNING
1
WARNING
1.5
WARNING
2
1. NORMAL EXECUTION
2. EXECUTION with WARNINGS (no stop)
(ABS)
Traced_WorkingStep
TimeStamp
workingstep_time
0
5
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 31: Part 1: Dynamic Data Type. (Working Step Data 2)
END
Event
execution_events S[0:?]
0s 1 3 8s
START
ALARM
STOP
ALARM
1
STOP
1
GO ON
3
3. EXECUTION with ALARM (stop & resume)
(ABS)
Traced_WorkingStep
TimeStamp
workingstep_time
0
8
GO ON
AP 238: Tracing Controller Events (Workingstep Execution).
- dynamic data samples (2)-
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 32: Part 1: Dynamic Data Type. (Working Step Data 5)
Event
execution_events S[0:?]
0s 1 5 6 10s
START
ALARM
STOP
& RESTART
ALARM
1
STOP
1
RESTART
1
4. FAILED EXECUTION & WITH WORKINGSTEP RESTART
(ABS)
Traced_WorkingStep
TimeStamp
workingstep_time
0
??
WorkingStep Restart
1s 6s
START
END
(ABS)
Traced_WorkingStep
TimeStamp
workingstep_time
Event
execution_events S[0:?]
1
6
AP 238: Tracing Controller Events (Workingstep Execution).
- dynamic data samples (5)-
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 33: Part 1: Dynamic Data Type. (Working Step Data 3)
END
Event
execution_events S[0:?]
0s 1 5 6 10s
START
ALARM
STOP
ALARM
1
STOP
1
MANUAL
5
4. EXECUTION with MANUAL GO TRHOUGH
(ABS)
Traced_WorkingStep
TimeStamp
workingstep_time
0
10
GO ON
MANUAL
GO ON
6
operations
AP 238: Tracing Controller Events (Workingstep Execution).
- dynamic data samples (3)-
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 34: Part 1: Dynamic Data Type. (Working Step Data 4)
Event
execution_events S[0:?]
0s 1 5 6 10s
START
ALARM
STOP
EXIT & JUMP
ALARM
1
STOP
1
EXIT
1
4. FAILED EXECUTION.
(stop & exit)
(ABS)
Traced_WorkingStep
TimeStamp
workingstep_time
0
??
JUMP POINT
AP 238: Tracing Controller Events (Workingstep Execution).
- dynamic data samples (4)-
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Dynamic Data Type Information.
     Automation
     WorkingStep Data

## Slide 35: Part 1: Generic Manufacturing Resources. (Data Model Questions - 6)
AP 238: Static Traceability Data: Traced WorkPiece
  Traceability configuration is “TO BE” data, Traceability Data is “AS IS” collected data.
Management HARMONIZED UOF
traced_item (traceability UOF)
Traced_Workpiece
its_workpiece
requirements_specified_by L[1:?]
(ABS)
Traced_WorkingStep
requirements_documented_by L[1:?]
STRING
Specification
(ABS) Document_file
LOT
(AP223)
label
date
traced_lot (traceability UOF)
description
lot_id
Machine AP240 HARMONIZED UOF
Machine
(AP240)
id
comapny_model
comapny_name
Controller
controlled_by
controller_model
controller_name
controller_specification
used_machine
Approval
Traceability_authorization L[1:?]
Traced_Operations S[0:?]
Part 1: Purpose and Objectives.
   Q.I.
   Activity Model Questions.
   Data Model Questions.
     STEP Traceability Approaches.
     Static Data Type Information
     Chatacteristics
     Materials.
     Generic Resources.

## Slide 36: Part 1: Dynamic Data Type. (Working Step Data 6)
AP 238: Tracing WorkingSteps.
tool_item_data (traceability UOF)
Workingstep_data
(ABS)
Traced_WorkingStep
TimeStamp
Date
start time
end_time
ABS(PlaceHolder Subtype)
ToolData
used_tools
S[0:?]
STRING
STRING
working_step_description
Traceability_remarks
TimeStamp
Date
start time
workingstep_time
LOT
(AP223)
Date
Label
Label
Item_identification
traced_lot
lot_id
date
Event
end_time
Date
event_time
STRING
event_description
execution_events S[0:?]
event_operations
STRING
event_break_point
STRING
STRING
event_return_point
event_type
(WARNING, ALARM, MANUAL/AUTO CHANGE, HARD/SOFT RESTAR, ERROR ..)
Controller_event

## Slide 37: Document Index.
Part 1: Purpose and Objectives.
  Questions Introduction.
  Traceability Activity Model.
  Traceability Harmonization.
    STEP Traceability Approaches.
    “Static Data Type Information”
      Product characteritics.
      Generic manufacturing resources.
        Materials Harmonization.
        Other manufacturing resources.
    “Dynamic Data Type Information”
      Workingsteps.
      Traceability Automation.
Part 2: Questions Summary and Decisions to Make.
  Questions Summary.
  Decisions

## Slide 38: Part 2: Questions Summary (1).
(1)Traceability CONFIGURATION Strategy in AP238?
  (1.1) Machine Conformance Classes
      CC1 (no trace-enabled)
      CC2 (trace-enabled characteristics/probing-enabled)
      CC3 (trace-enabled static type)
      CC4 (trace-enabled dynamic type)
      CC5 (full trace-enabled machine)
  (1.2) Specific configuration based on AP ?
  (1.3) Both
Virtual Enterprise
possible INPUT points for Traceability Requirements
AP203
AP224
“To be”
Traceability data
requirements
Product design
requirements
Enterprise Data
Management Tools
Main Customer
“To be”
Traceability
data
requirements
Macro design
requirements
Enterprise Data
Management Tools
Macro Planning
“To be”
Traceability
data
requirements
Micro design
requirements
Micro Planning
AP224
AP240
“As IS”
Traceability
data
Collected
Machining
AP238
Part 2: Questions & Decisions to Make.
   Questions Summary
   Decisions.

## Slide 39: Part 2: Questions Summary (2).
(2)Traceability Data PLACE HOLDERS?
  Inclusive strategy
    Specific place holders.
  Other strategy (“TO BE” data as non STEP file)
AP238 Manufacturer
“AS IS”
Traceability
collected data
NC- Machines &
Controllers (CC)
Traceability Data
Part 2: Questions & Decisions to Make.
   Questions Summary
   Decisions.
Traceability DATA PLACE HOLDERS:
1-INCLUSIVE AP238:
- Reuse “AS IS” for “TO BE”
data.
- Specific entities for “TO BE”
2- “TO BE” data as non step files
“TO BE”
Traceability
data
Enterprise Data
Management Tools
“AS IS”
Traceability
data

## Slide 40: Part 2: Questions Summary (3).
(3) AP 238 TRACEABILITY DATA AUTOMATION FUNCTIOS?
ABS(nc_function) executable (2)
program_stop
exchange_pallet
optional_stop
index_pallet
index_table
display_message
load_tool
unload_tool
nc_legacy_fucntion
get_tool_data
get_time
Date
Its_recorded
_data
Its_recorded
_time
(ABS)Data_
placeHolder
Part 2: Questions & Decisions to Make.
   Questions Summary
   Decisions.
executable
PROGRAM STRUCTURE
WorkingSteps
Machinning_workingsteps
Touch_probing (1)

## Slide 41: Part 2: Questions Summary(4).
(4) AP 238 TRACEABILITY DATA SCOPE ?
  (4.1) STATIC DATA & CHARACTERISTICS DATA ?
  (4.2) DYNAMIC DATA?
  (4.3) CONTROLLER EVENT DATA for MANUFACTURING SIMULATION?
clamping_positions S[0:?]
its_material
its_id
global_tolerance
its_geometry
Workpiece
(AP238)
(Characterisitcs)
(Harmonized AP224 Properties)
its_workpiece
(as is data placeholders)
Traced_Workpiece
material_identifier (AP224 material_id)
standard_identifier (AP238)
Material
(AP224 Harmonized)
label
label
STRING
stock_size (AP224)
traced_lot (traceability UOF)
Traced_WorkingSteps
(Dynamic Data
WorkPiece Generic_ Resources & Data
event
execution_events S[0:?]
Part 2: Questions & Decisions to Make.
   Questions summary
   Decisions.
LOT
(AP223)

## Slide 42: Part 2: DECISIONS
(1)Traceability Configuration Strategy in AP238?
  (1.1) Machine Conformance Classes?
    CC1 (no trace-enabled)
    CC2 (trace-enabled characteristics/probing-enabled)
    CC3 (trace-enabled static type)
    CC4 (trace-enabled dynamic type)
    CC5 (full trace-enabled machine)
  (1.2) Specific Configuration.
  (1.3) Both
(2) AP 238 DATA PLACE HOLDERS?
  INCLUSIVE ?
  DATA EXCHANGE MODEL BETWEEN TRACEABILITY PLANT SYSTEMS & CAx SYSTEMS ?
(3) AP 238 TRACEABILITY AUTOMATION FUNCTIONS?
(4) AP 238 TRACEABILITY DATA SCOPE?
  (4.1) STATIC DATA & CHARACTERISTICS DATA ?
  (4.2) DYNAMIC DATA?
  (4.3) CONTROLLER EVENT DATA for MANUFACTURING SIMULATION?
Part 2: Questions & Decisions to Make.
   Questions summary.
   Decisions.