## Slide 1: State of STEP-NC AP-238
Martin Hardwick
David Loffredo
info@steptools.com
STEP-NC Manufacturing Center
Watervliet Arsenal, Building 20
Metal Processing Manufacturing Division
Watervliet, New York 12189
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: STEP-NC AP-238
STEP-NC defines an object model for:
  Workingsteps – e.g. sequence of operations WS 1, WS2 etc
  Operations – e.g WS1 is Rough milling of pocket
  Features – e.g. Dimensions of pocket
  Tooling – e.g. Machining attributes for rough milling the pocket
  Toolpath – e.g. Path, speeds and feeds to mill the pocket
Using Three Conformance Classes
  CC1 = CNC independent tool paths
  CC2 = CC1 + CAD geometry
  CC3 = CC2 + CAD features and tolerances

## Slide 3: Aerospace Implementation
CAD
CAM
Viewer
CNC
CATIA
UGS
Pro/E
AP-238 CC1
AP-203 CC6
Fanuc
Siemens
Okuma
AP-238 CC2
Visual CNC

## Slide 4: Army Implementation
CC3 demonstration
  Export tolerance and feature data from CAD
  Add toolpath data from CAM
  Intelligent application uses tolerances for in-process measurements
CAD
CAM
CNC
AP-224
AP-238 CC4
Mastercam
UGS
STEP
Plan
???