## Slide 1: SEDS issues
AP224, AP240
ISO/SC4/TC184/WG3/T24
Toulouse, France
June 2006
Mr. Len Slovensky
(513) 383-8311
slovensky@scra.org

## Slide 2: AP224 e3 SEDS #1
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates:
5.1.9.6 Compound_datum
5.1.9.6.1 compound_datum to datum_feature (as element)
5.2 AIM EXPRESS short listing
Annex A (normative) AIM EXPRESS expanded listing
Annex B (normative) AIM short names
Other Parts Affected by the Issue: AP203e2, AP240, AP238, AP223, AP229, AP219, AP214
Related Issues:
Summary/Abstract/Keywords: datum, compound_datum

## Slide 3: AP224 e3 SEDS #1
Problem Description: Mapping of ARM entity Compound_datum maps to AIM entity common_datum, but defined incorrectly in AP224e3.
5.1.9.6 Compound_datume, souce for common_datum is stated as 10303-47, this is incorrect. also the note is incorrect, it was written for AP224 1st edition without common_datum, needs to be changed.
5.1.9.6.1 compound_datum to datum_feature (as element) mapping is correct for datum to
datum_feature, but incorrect for common_datum.
5.2 AIM EXPRESS short listing - common_datum missing from USE FROM for aic_geometric_tolerances, 10303-519
Annex A (normative) AIM EXPRESS expanded listing - common_datum entity definition missing.
Annex B (normative) AIM short names - common_datum entity AIM element missing
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3

## Slide 4: AP224 e3 SEDS #1
Proposed Solution (Optional):
5.1.9.6 Compound_datum - Chance source to 10303-519, update note to reflect the use of composite_shape_aspect
5.1.9.6.1 compound_datum to datum_feature (as element) change to:
Reference Path: common_datum
composite_shape_aspect
composite_shape_aspect.component_relationships [i] ->
shape_aspect_relationship
shape_aspect_relationship.related_shape_aspect ->
shape_aspect =>
datum
5.2 AIM EXPRESS short listing - add common_datum to USE FROM for aic_geometric_tolerances, 10303-519
Annex A (normative) AIM EXPRESS expanded listing - add common_datum entity definition.
Annex B (normative) AIM short names - add common_datum entity AIM element.

## Slide 5: AP224 e3 SEDS #2
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates:
5.1.9.15 Dimensional_tolerance
5.1.9.15.1 dimension_description
Other Parts Affected by the Issue: AP203e2, AP240, AP238, AP223, AP229, AP219, AP214
Related Issues:
Summary/Abstract/Keywords: dimensional tolerance, dimensional size

## Slide 6: AP224 e3 SEDS #2
Problem Description:
5.1.9.15 Dimensional_tolerance has two subtypes: size_tolerance and
location_tolerance. size_tolerance maps to the part 47 entity dimensional_size, and location_tolerance maps to the part 47 entity dimensional_location. However the mapping for Dimensaion_tolerance maps to part 47 shape_dimension_representation. The mapping to the subtypes is incomplete.
5.1.9.15.1 dimension_description - the mapping is incorrect size_tolerance and all of the size_tolerance subtypes. The size tolerance subtypes use dimensional_size.name as a part of the entity mapping.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3

## Slide 7: AP224 e3 SEDS #2
Proposed Solution (Optional):
5.1.9.15 Dimensional_tolerance
#1: Dimensional_tolerance as Dimensional_size
AIM element: shape_dimension_representation
Source: ISO 10303-47
Reference Path: shape_dimension_representation <-
dimensional_characteristic_representation.representation
dimensional_characteristic_representation
dimensional_characteristic_representation.dimension ->
dimensional_characteristic
dimensional_characteristic = dimensional_size
dimensional_size
#2: Dimensional_tolerance as Dimensional_location
AIM element: shape_dimension_representation
Source: ISO 10303-47
Reference Path: shape_dimension_representation <-
dimensional_characteristic_representation.representation
dimensional_characteristic_representation
dimensional_characteristic_representation.dimension ->
dimensional_characteristic
dimensional_characteristic = dimensional_location
dimensional_location

## Slide 8: AP224 e3 SEDS #2
5.1.9.15.1 dimension_description
#1: Dimensional_tolerance as Dimensional_size
AIM element: (dimensional_size.name)
Source: ISO 10303-47
ISO 10303-41
Reference Path: shape_dimension_representation <=
shape_representation<=
representation<-
description_attribute_select=representation
description_attribute_select<-
description_attribute.described_item
description_attribute
description_attribute.attribute_value
#2: Dimensional_tolerance as Dimensional_location
AIM element: (shape_aspect_relationship.description)
Source: ISO 10303-47
ISO 10303-41
Reference Path: shape_dimension_representation <-
dimensional_characteristic_representation.representation
dimensional_characteristic_representation
dimensional_characteristic_representation.dimension ->
dimensional_characteristic
dimensional_characteristic = dimensional_location
dimensional_location <=
shape_aspect_relationship
shape_aspect_relationship.description

## Slide 9: AP224 e3 SEDS #3
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates:
5.3.218 Position_tolerance to Datum
Annex G Figure G.28
Other Parts Affected by the Issue: AP203e2, AP240, AP238, AP223, AP229, AP219
Related Issues:
Summary/Abstract/Keywords: Positional tolerance, datum

## Slide 10: AP224 e3 SEDS #3
Problem Description:
We've hit a part with a true position tolerance that didn't have any datum references associated with it.
We looked in the ANSI standard and a few other places to see if this is allowed. From what we've found,
it is possible to tolerance a feature in this manner (our case was a hole in a circular pattern where the diameter
of the pattern was basic and the position tolerance meant that the location of the hole is true relative to its own
location on the diameter).
Anyway, AP224v(all) requires that a true position tolerance needs from 1 to 3 datum references.
ARM diagram 28 shows a position-tolerance having from 1 to 3 datums. In AIM express diagram 27,
the mapped entity for referenced tolerances, geometric_tolerance_with_datum_reference has a
datum_system attribute that is a set of 1 to many.
Can this be changed to allow 0 to 3 datum references?
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3

## Slide 11: AP224 e3 SEDS #3
Proposed Solution (Optional): AP224 and the other APs using Positional_tolerance use AIC519 to define Positional_tolerance for the AIM and it already has a local rule of 0 to 3 datum references. Therefore the AP224 ARM should be changed to match the AIM, this is upward compatible.

## Slide 12: AP224 e3 SEDS #4
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates: AP224e3 4.2.143 Numeric_parameter, 5.1.6.6 Numeric_parameter
Other Parts Affected by the Issue: AP240, AP238, AP223, AP229, AP219
Related Issues: none
Summary/Abstract/Keywords:

## Slide 13: AP224 e3 SEDS #4
Problem Description:
For Dimension Tolerance I can add a note or description to help clarify the dimensions usage (make it BASIC or whatever).
This dimension maps to a measure-rep-item that has an item that is a descriptive-rep-item where the value is stored.
For features, all the dimensions that make it up are numeric-parameters.
These are also measure-rep-items. Is it possible to put a note or clarification onto a numeric-parameter in a similar manner as
Dimension Tolerance?
Also add significant digits and description.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 14: AP224 e3 SEDS #4
Proposed Solution (Optional):
4.2.143 Numeric_parameter
The data associated with a Numeric_parameter are the following:
— parameter_description;
— parameter_note;
— parameter_units;
— parameter_value;
— significant_digits.

## Slide 15: AP224 e3 SEDS #4
5.1.6.6 Numeric_parameter
AIM element: measure_representation_item
Source: ISO 10303-45
5.1.6.6.1 Numeric_parameter to measure_qualification (as parameter_description)
AIM element: (measure_qualification.description)
Source: ISO 10303-41
Reference Path: measure_representation_item<=
measure_with_unit<-
measure_qualification.qualified_measure
measure_qualification
measure_qualification.name=’numeric parameter clarification’
measure_qualification.description
5.1.6.6.2 Numeric_parameter to measure_qualification (as parameter_note)
AIM element: (type_qualifier.name)
Source: ISO 10303-41
Reference Path: measure_representation_item<=
measure_with_unit<-
measure_qualification.qualified_measure
measure_qualification
measure_qualification.name=’numeric parameter clarification’
measure_qualification.qualifiers[i]->
value_qualifier=type_qualifier
type_qualifier
type_qualifier.name
5.1.6.6.2 Numeric_parameter to measure_qualification (as parameter_note)
AIM element: (precision_qualifier.precision_valu)
Source: ISO 10303-41
Reference Path: measure_representation_item<=
measure_with_unit<-
measure_qualification.qualified_measure
measure_qualification
measure_qualification.name=’numeric parameter clarification’
measure_qualification.qualifiers[i]->
value_qualifier=precision_qualifier
precision_qualifier
precision_qualifier.precision_value

## Slide 16: AP224 e3 SEDS #5
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates: AP224e3 Figure 112 Square_U_profile
Other Parts Affected by the Issue: AP240, AP238, AP223, AP229, AP219
Related Issues: none
Summary/Abstract/Keywords:

## Slide 17: AP224 e3 SEDS #5
Problem Description:
I am working with square-u-profiles for grooves. In 4.2.231.2 and 4.2.231.4, the side angles are defined as a measure
between the side and the base. The associated figure 111 indicates that the measures are from base line on the outside of
the profile to the sides. I thought at one time we had said to define it from inside the profile instead?
This goes back quite a ways, it was like this in ap224v1 as well.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 18: AP224 e3 SEDS #5
Proposed Solution (Optional):
Modify the figure so it shows the angles measured on the inside.
AP224e3
Proposed

## Slide 19: AP224 e3 SEDS #6
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates: AP224e3 4.2.3 Angular_dimension_tolerance
Other Parts Affected by the Issue: AP203e2, AP240, AP238, AP223, AP229, AP219, AP214
Related Issues: none
Summary/Abstract/Keywords:

## Slide 20: AP224 e3 SEDS #6
Problem Description:
The angular-dimension-tolerance ARM definition changed between v2 and v3 in 224.
The major-angle attribute was removed. In the express file, angular_location still has an
angle-selection (as an angle-relator) included. Is that suppose to be used for something or just left blank?
The angular-dimension-tolerance ARM definition changed between v2 and v3 in 224.
The major-angle attribute was removed. In the express file, angular_location still has an angle-selection
(as an angle-relator) included. Is that suppose to be used for something or just left blank?
I think we need the major-angle still. How are we suppose to indicate which angle we are measuring between 2 lines:
/
/ angle1
---------------
/ angle2
/
Angle2 = supplement of angle1. If we pick these 2 lines or planes, how do we tell which angle we are after and in which quadrant?
Is there any way to indicate the reflex of angle1? (reflex = 360 - angle1).

## Slide 21: AP224 e3 SEDS #6
      Angular_dimension_tolerance
#1: if directed = true
AIM element: (directed_dimensional_location)
(angular_location)
Source: ISO 10303-224
Rules:
Reference Path: (directed_dimensional_location<=)
(angular_location <=)
dimensional_location
#2: if directed = false
AIM element: (angular_location)
Source: ISO 10303-47
Rules:shape_representation_subtype_exclusiveness – (See 5.2.4.35)

## Slide 22: AP224 e3 SEDS #6
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240
Proposed Solution (Optional): Change back to AP224e2
ENTITY Angular_dimension_tolerance
SUBTYPE OF(Location_tolerance);
major_angle : BOOLEAN;
mirror_origin : BOOLEAN;
mirror_termination : BOOLEAN;
END_ENTITY;

## Slide 23: AP240 SEDS #1
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates: 4.2.55 Geometric_tolerance, 4.3.65 Geometric_tolerance to Shape_aspect,
5.1.7.8 Geometric_tolerance, 5.1.7.8.1 geometric_tolerance to shape_aspect (as applied_shape),
Annex G diagram G14
Other Parts Affected by the Issue:
Related Issues:
Summary/Abstract/Keywords: geometric tolerances GD&T

## Slide 24: AP240 SEDS #1
Problem Description: The intent of the Geometric_tolerance entity was to create one entity that would define the need for geometric tolerances, and to use AP224 as a reference, saying that the Geometric _tolerance entity represents all of the entities defined in AP224 for geometric tolerances, and mapped to AIC 519. The problem is this does not bring into AP240 all of the datum requirements or tolerance zone requirements.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 25: AP240 SEDS #1

## Slide 26: AP240 SEDS #1

## Slide 27: AP240 SEDS #2
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates: 4.2.83 Machining_process_feature,
Annex G diagram G14
Other Parts Affected by the Issue:
Related Issues:
Summary/Abstract/Keywords: machining features

## Slide 28: AP240 SEDS #2
Problem Description: The intent of the Machining_process_feature entity was to create one entity that would define the need for machining features, and to use AP224 as a reference, saying that the Machining_process_feature entity represents all of the entities defined in AP224 for machining features, and mapped to AIC 522. The problem is this does not bring into AP240 all of the machining feature requirements.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 29: AP240 SEDS #2

## Slide 30: AP240 SEDS #3
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates: 5.2.3.2.20 document_file
Other Parts Affected by the Issue: none
Related Issues: none
Summary/Abstract/Keywords: document

## Slide 31: AP240 SEDS #3
Problem Description: The definition of the entity documen_file defines it as a subtype of characterized_object and document. This is backwords from AP224 which defines a document_file as a document and characterized_object, this effects inheritance.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 32: AP240 SEDS #3
Proposed Solution (Optional): switch characterized_object and document
ENTITY document_file
SUBTYPE OF (characterized_object, document);

## Slide 33: AP240 SEDS #4
Author: Len Slovensky
Email Address: Slovensky@scra.org
Part and Clause where Issue Originates: AP240
Clause 5.1.7.2.1 full_or_half
Other Parts Affected by the Issue: none
Related Issues: none
Summary/Abstract/Keywords: angular size dimension, dimensinal tolerances

## Slide 34: AP240 SEDS #4
Problem Description:
Ap224v3 changed the mapping (5.1.9.2.1) for the full-or-half attribute to a descriptive-rep-item.description.
AP240 has it like AP224v2, mapped to a representation-item.name.
Is Ap240 going to be made consistant with ap224v3?
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 35: AP240 SEDS #4
Proposed Solution (Optional): Make the same as AP224e3
5.1.9.2.1 full_or_half
AIM element: descriptive_representation_item.description
Source: ISO 10303-43
Reference Path: angular_¬size <=
dimensional_size
dimensional_characteristic = dimensional_size
dimensional_characteristic <-
dimensional_characteristic_representation.dimension
dimensional_characteristic_representation
dimensional_characteristic_representation.representation ->
shape_dimension_representation <=
shape_representation <=
representation
representation.items[i] ->
representation_item
descriptive_representation_item
descriptive_representation_item.description
{(descriptive_representation_item.description= 'full angle')
(descriptive_representation_item.description= 'half angle')}