## Slide 1: Status of STEP Manufacturing
AP219, AP223, AP224, AP229, AP240, AIC522
ISO/SC4/TC184/WG3/T24
Toulouse, France
June 2006
Dr. Bill Freeman
(843) 760-3791
freeman@scra.org
Mr. Len Slovensky
(513) 383-8311
slovensky@scra.org
Mr. Jesse Crusey
(717) 264-2716
jcrusey@aol.com

## Slide 2: STEP-Manufacturing Suite status
10303-219 - Dimensional inspection information exchange
10303-223 - Exchange of design and manufacturing product information for casting parts
10303-224 - Mechanical product definition for process planning using machining features
10303-229 - Exchange of design and manufacturing product information for forged parts
10303-240 - Process plans for machined product
10303-522 - Application interpreted construct: Machining features

## Slide 3: Integrated Manufacturing Architecture using Manufacturing features
Dimensional Inspection Information Exchange
Geometry,
Manufacturing
Features,
Tolerances,
Properties
Exchange of Design and Manufacturing Product Information for Cast Parts
AP219
AP224
Mechanical product definition for process planning
using machining features
Process plans for
machined parts
AP240
CMM
Application interpreted model for computerized numerical controllers
CNC
AP238
AP223
CAD
Exchange of Design
and Manufacturing
Product Information
for Forged Parts
AP229

## Slide 4: What is a Machining Feature ?
Definition of an aspect of shape on a part.
Terminology in terms of Manufacturing users
Defines explicit definition of shape:
  Geometry
Defines implicit definition of shape:
  Parametric attributes

## Slide 5: Explicit and Implicit feature information
Example: Slot
  Boundary Representation Geometry defines Slot Feature
  Face Topology defines Slot floor and side walls
Faces
Example: Slot
  Parameters defines Slot
    Slot depth
    Slot width
    Slot height
    Corner radius

## Slide 6: Feature relationships
Feature
Geometric
Tolerance
Geometric
Shape
Position tolerance references Countersunk hole
Countersunk hole references cylindrical face
Explicit feature related

## Slide 7: Feature relationships
Implicit feature related
Feature
Dimensional
Tolerance
Feature
Attribute
For hole
depth
Plus minus
tolerance

## Slide 8: Manufacturing Feature Example
Planar_face
Planar_face
(Rough)
Planar_face
(Rough)
Clamping Direction
Planar_face
Planar_face
Planar_face
Compound_feature
[Round_hole + Counterbore_hole]
General_outside_profile
Step
Slot
Countersunk_hole
Countersunk_hole
Thread
Countersunk_hole
Slot
Compound_feature
[Round_hole + Counterbore_hole]
Countersunk_hole
Slot
General_cutout
Rectangular_open_pocket
Rectangular_boss
Planar_face
Countersunk_hole
General_outside_profile
Planar_face
Countersunk_hole
Countersunk_hole
Groove
Clamping Direction
[Slot_D1]
Slot
[Hole_D1] 2 times
Countersunk_hole
[Thread_D1]
2 times Thread
[Head_D1]
Planar_face
（Finish)
[Head_E1]
Planar_face
（Finish)
[Slot_E1] Slot
[Hole_E1]2 times
Countersunk_hole
[Thread_E1] 2 times
Thread
Clamping Direction
Notes: The AP224 IS standard has defined some 18 different machining features, however these features are further defined into many different variations. For example the Hole feature can be defined as a round hole, counterbore countersunk through hole, a blined hole with several different bottom conditions, and all of these hole feature types can be defined with tapers. Therefore the 18 different machining features are used to define a large number machining feature variations.
After AP224 was published as an IS standard in1999, it was determined that these machining features could be used in many other STEP standards. Therefore the machining feature portion was removed from AP224 and a new ISO standard was created called Application Integrated Construct (AIC) 522. This AIC is a standalone construct that can be used by any AP to include the AP224 machining features in directly into the AP definition.

## Slide 9: AP224
Dimensions
Tolerances
Geometry with Topology
Features
Major component for AP
Drawing notes
Material property
Surface finish
Process property
Hardness
Part information
Security
Approvals
Materials
CORE DATA
Notes: AP224 contains the following information, which is necessary to manufacture the required part.
• Necessary CAD geometry and topology in a neutral format.
• Machining feature information such as hole, boss, slot, groove, pocket, chamfer and fillet.
• Dimensional and geometric tolerance information.
• Material properties, process properties and material hardness.
• Administrative information such as approval, part name and ID, delivery date and quantity.

## Slide 10: STEP-Manufacturing Suite status
10303-224 - Mechanical product definition for process planning using machining features
  3rd edition published 2006
  A few issues will be discussed in Toulouse to determine if SEDS should be submitted.
10303-522 - Application interpreted construct: Machining features
  2nd edition published together with AP224 3rd edition.
  No current issues to discuss for this part.

## Slide 11: AP240-Process plans for machined parts
work instructions for the tasks required to manufacture a part,
which include:
  references to the resources required to perform the work
  the sequences of the work instructions
  relationships of the work to the part geometry
technical data for and/or out of the process planning
for machined pats which includes:
  machining features for defining shapes necessary for manufacturing
  machining feature classification structure
  geometric and dimensional tolerances of the parts being manufactured
  materials, and properties of the parts being manufactured
information contained in the process plans
for machined parts which includes:
  numerical controlled machines
  manual operations
CORE DATA
Notes: AP240 defines the macro process planning for machining parts. This AP captures part shape, tolerances properties from AP224 and adds additional information contained in the process plans for machined parts which includes: numerical controlled machines, and manual operations. AP240 adds information on work instructions for the tasks required to manufacture a part, using which include: references to the resources required to perform the work the sequences of the work instructions relationships of the work to the part geometry. And AP240 has information on technical data for and/or out of the process planning for machined pats which includes: machining features for defining shapes necessary for manufacturing, machining feature classification structure, geometric and dimensional tolerances of the parts being manufactured and materials, and properties of the parts being manufactured.

## Slide 12: Process plan defines resources
Defines:
  Machines
  Tools
  Fixtures
  Workstation
  Work cell
  Controller
Notes: Ap240 defines all of the resources necessary to manufacture a part. This would include
Machines
Cutting tools, and holders
In stock fixtures, or special to be designed fixtures
The facility or facilities where the part is to be processed
A Work cell which is an area within the enterprise, consisting of one or more machines.
Generic resources – examples are Durable products such as marking dies, and consumable products such as dye penetrate, coolants,and lubricants

## Slide 13: Develop Manufacturing Process (Macro Process Planning)
Manufacturing process defines:
  sequential manufacturing operations
  machine,
  type of setup,
  Machining processes
    Assign process to features
Notes: The AP240 process plan incorporates a sequential list of manufacturing process. Each machining process:
Identifies the Machine required for the operation
  Example: 5 axis mill, turning center, etc.
Identifies the type of setup necessary for that machine
  Example: place part on machining pallet with clamps,
  Place fixture on machine pallet and place part in fixture,
Identifies machining operations, these operations may be non-NC operations like heat treat, or de-burr or may be a volume removal operation identified by a manufacturing feature.
In this example of a process plan, there are 3 sequential manufacturing processes, each has a machine identified, a setup with positioning of clamps defined, and identified features.
Each of these 3 manufacturing processes will have several machining operations defined.

## Slide 14: AP240 Machining operations
[Slot_D1]
Slot
[Hole_D1] 2 times
Countersunk_hole
[Thread_D1]
2 times Thread
[Head_D1]
Planar_face
（Finish)
[Head_E1]
Planar_face
（Finish)
[Slot_E1] Slot
[Hole_E1]2 times
Countersunk_hole
[Thread_E1] 2 times
Thread
Clamping Direction
Machining operations defines:
  Sequence of features for Manufacturing activity
Notes: AP240 also used machining features in defining in planning manufacturing activities and operations. A part will require multiple machine setups in order to machine each and every side of the part. Each setup activity definition contains a list of machining features that can are eligible for material removal. Also any other manufacturing activity that removes material from the part will have a list of machining features that pertain to that specific activity. Manufacturing activities are further subdivided into separate operations per that activity. For example there may be a manufacturing activity defined to drill all holes and thread some of the holes on the part. This activity would contain a list of hole and thread features. This activity would be subdivided into operations for drilling counter sinking, and tapping. Each of these operations would contain a subset of the manufacturing activity features. Adding the AP224 machining features has greatly enhanced the AP240 macro process planning information.

## Slide 15: AP240 Manufacturing activity
Manufacturing activity are defined to process the feature
Operations are defined for the manufacturing activity

## Slide 16: STEP-Manufacturing Suite status
10303-240 - Process plans for machined product
  1st edition published 2005
  A few issues will be discussed in Toulouse to determine if SEDS should be submitted.
  Some of the issues are about geometric and dimensional tolerances which effects other manufacturing suite APs.

## Slide 17: AP219 Scope
This project will specify information requirements for analyzing the data and reporting the results of dimensional inspections of solid parts or assemblies.
Certain information used for administering, planning, and executing dimensional inspection as well as archiving the results is also required in the analysis activity.
Dimensional inspection can occur at any stage of the life cycle of a product where checking for conformance with a design specification is required.
Excluded from the scope are the dimensional inspection of liquid surfaces, the materials properties of parts, manufacturing activities, and mathematical algorithms to perform the dimensional inspection analysis.

## Slide 18: AP219 - Dimensional Inspection Information Exchange
Analysis
Feature analysis mode
Feature tolerance mode
Parameter analysis mode
Dimensional Measurement features
Circle, arc, sphere
Geometric surface
Lines, planes
Pattern
Measurement execution
Execution result
Execution result measurement
Data acquisition software
Result parameter
Program run
Program identification
Run administrator
Measurement location
Program Run
Tolerances
Geometric tolerances
Dimension tolerances
Material condition modifier
Tolerance range
Part Properties
Calculated value
Parametric calculated value
Parameters
  Property
  Numeric
  Descriptive
Part
Part
Manufacturing features
Shape representation
  Brep model
  Explicit base shape
  Implicit base shape
Measurement parameters
Dimensional parameter
Point parameter
Vector parameter
Parameter value limits
Administration data
Person and Organization
Date and time
Time offset
CORE DATA

## Slide 19: Harmonization: Mapping and integration
Harmonization through mapping between requirements specifications
Harmonization through integration of requirements specifications
AP219
View
AP224
View
integration
mapping
AP219
View
DMIS
View

## Slide 20: AP219 - Dimensional Inspection with tolerances
Manufacturing view
Dimensional
measurement
view
15mm + .25
25mm + .5
Hole 2
Hole 1
-
-
Circle 2
Circle 1
Circle 4
Circle 3
AP219 defines
  Dimensional Tolerances
  Geometric Tolerances
Instances: Counterbore_hole measurement

## Slide 21: Manufacturing and dimensional measurement views
Dimensional
Measurement view
Manufacturing view
Manufacturing
feature
Parameter
nominal
Parameter
tolerance
Manufacturing info
Part
Dimensional
measurement
feature
Dimensional
Measurements
Points
Measurement data
Dimensional
measurement
parameter
Calculated
value
Measurement results
DMIS Feature actual
DMIS Feature nominal
specification

## Slide 22: STEP-Manufacturing Suite status
10303-219 - Dimensional inspection information exchange
  CD ballot passed – Feb. 10, 2005, ballot issues submitted by China, Japan and USA
  DIS ballot closes – August 7, 2006

## Slide 23: AP223 - Exchange of Design and Manufacturing Product Information for Cast Parts
Casting process simulation
Shape representation
Process design parameters
Simulation results
Quality Control Records
Processes of building a sand mold, of building a die assembly, and of building an investment pattern assembly.
Processes of melting, pouring, cooling, shaking out, extracting, and knocking out a casting
Melting processing and resulting metal composition
Inspection and testing results of the cast part.
Process Plan
Process_plan harmonized with AP240
Melting, pouring, cooling, shakeout, extracting, and gate removal of a casting
Process used to produce a casting
Metal alloys used to produce a casting.
Equipment used to produce a casting.
Mold Design
Shapes of sand mold, die assembly, and investment pattern assembly
Materials used in the casting processes
Building a sand mold, a die assembly, and an investment pattern assembly
Data Supported
Shapes of cast parts
Materials of cast parts
Tolerances and surface finish
Physical and mechanical properties
Harmonized with AP224 features, tolerances, properties
CORE DATA
Notes: AP223 brings together all of the information contained in AP224 and AP240. This AP defines the “as designed” AP224 type of data and the process planning information for cast part. However AP223 has unique requirements specific for castings. For example the AP224 machining features need draft angles to define cast features. The AP240 process plan needs activities and operations defined to support the casting foundry. Besides this overlap with existing APs,

## Slide 24: AP223- Cast parts Architecture
STEP
Translator
CC1-Design
engineering
drawing
Native
CAD
drawing
Order
Manager
STEP
Validator
CC4-
Customer
to
foundry
Reference
Customer
Foundry
STEP
Translator
Foundry
Process
Planning
CC2-Cast
part design
(cast shape,
casting
requirements)
CC5 -
Metal caster
to
tooling shop
Reference
Tooling shop
STEP
Translator
CC3-Cast part
tooling
(near net shape+
gating system+
Pattern features)
Simulation
Simulation
CC8 –
Metal caster
to
simulation
Inspection
Inspection
CC6 –
Metal caster
to
inspection
Reference
Tooling
Manager
AP219
(dimensional
inspection)
Machining
CC7 –
Metal caster
to
machining
Process
Planning
Notes: AP223 also has additional requirements for simulation data, to simulate pouring molten medal into a mold and analyzing metal flow, cool spots, and poor mold design. This AP also support design information for the mold used to make the cast part. Casting molds contain a varied of features unique to the casting process like cope, drag, sprue basin, runners. Parting lines, etc. The machining features become an integral part of castings in defining the cast shape and in developing the mold information.

## Slide 25: STEP-Manufacturing Suite status
10303-223 - Exchange of design and manufacturing product information for casting parts
  CD ballot passed – Dec. 19, 2005, ballot issues submitted by Japan and USA
  DIS ballot in development
    EXPRESS-G ARM to be reviewed in Toulouse
    DIS ballot expected in 3rd quarter 2006

## Slide 26: AP223 - Exchange of Design and Manufacturing Product Information for Cast Parts
Data Supported
Shapes of forged parts
Materials of forged parts
Tolerances and surface finish
Physical and mechanical properties
Harmonized with AP224 features, tolerances, properties
Process Plan
Process_plan harmonized with AP240
Process used to produce a forging
Metal alloys used to produce a forging.
Equipment used to produce a forging.
Forging process simulation
Shape representation
Process design parameters
Simulation results
CORE DATA
Die Design
Shapes of die assembly
Materials used in the die design processes
Building a die assembly
Quality Control Records
Processes of building a die assembly.
Inspection and testing results of the cast part.

## Slide 27: AP223 Architecture
Design engineering drawing
Forged part design (forged shape, forging requirements)
Forged part tooling (near net shape, dies, parting surface, draft, shrinkage)
Customer requirements

## Slide 28: STEP-Manufacturing Suite status
10303-229 - Exchange of design and manufacturing product information for forged parts
  NWI ballot passed – Nov 4, 2005
  CD document currently under development
    Meetings are being held with industry to develop requirements model.
  DIS ballot expected 1st quarter 2007

## Slide 29: AP238 Application interpreted model for computerized numerical controllers
Manufacturing Features
Slot
Hole
Planar face
Thread
Outer Round
Chamfer
Workpiece
Workpiece
Material
Parameters
  Property
  Numeric
  Descriptive
Project
Project
Person and address
Tool path
Tool path
Feed stop
Parameterized path
Cutter contact and location trajectory
Measure
Limits and fits
Plus minus value
Tolerance length measure
Operation
Machine functions
Machining operation
Tool direction
Tool path list
Executable
Working step
Working plan
Setup
Cutting tool
If and While statement
Program structure
Process data for milling
Boring
Drilling
Reaming
Tapping
Cutting tools
Drill
Tap
Reamer
Boring tool
CORE DATA
Notes: AP238 is the next step in manufacturing after AP240; this AP defines the micro process planning. Where AP240 defined the high level details for manufacturing a part, this AP defines the specific information for a specific machine. This AP defines specific process information like boring, drilling, reaming or tapping. AP238 defines the setup, sequential working steps, cutting tool specifications for tools like drills, taps, boring tools, and reamers. AP238 describes how to make geometry from a piece of stock by removing AP224 machining features in a sequential order with specific tolerances with tools that meet all of these requirements.

## Slide 30: AP238 – Machining operation
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
L[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Machining features

## Slide 31: STEP-Manufacturing Suite status
AP238 - Application interpreted model for computerized numerical controllers
  STEP Tools Inc. has status

## Slide 32: Conceptual Basis -- SMS
Function
Defense
C4 Data
Standards
Org
STEP
Product Data Generation
AP224/AP203
DESIGN or Legacy Data Capture
AP224
AP240
Macro Process Planning
AP240
w/ AP224
Features
AP238
AP238
FACTORY
Part
Fab
Finished Part
Micro Process Planning/NC Coding
Inspection
AP219
CMM
AP238
AP240
Classic Work Tasks | Design or Capture Part Features Dim. & Tol. Material Notes & Spec’s Translate to STEP AP224 Validate AP224 file against design | Define Route steps and Sequence Select Resource for each step Apply Operation Standard Times Material/BOM Cost Est. Input Order Tools/ Fixtures Inspection Instructions | Setup Graphics Develop Cutter paths Post Process NC Program Operator instructions Finalize Tool List | Download NC Program Load Preset Tools Set Offsets Load Part Machine Part Optimize NC Program Inspection Unload Part Move part to next Route Step
Prototype Facility
Or FACTORY
Prototype Facility
Or FACTORY
AP223/AP229
Notes: SMS – Step Manufacturing Suite – STEP In – STEP Out – STEP Throughout

## Slide 33: Questions?