## Slide 1: AP-238 IS Walkthrough
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Toulouse SC4 Meeting
July 2006

## Slide 2: AP-238 Status
Final AP238 ready for ISO publication
  Updated with resolutions for all DIS comments, as developed at Valencia June 2005 meeting (see wg3n2095)
  Finishing up a couple of things in informative annexes
    Regenerating ARM & AIM EXPRESS-G diagrams.
    Adding CC1 and CC2 P21 examples to Annex K
  SC4 checklists, send to ISO for publication ~2 weeks after Toulouse meeting.
AP238 IS Documents
  wg3n2101 AP-238 document
  wg3n2096 EXPRESS short form schema
  wg3n2097 EXPRESS long form schema
  wg3n2099 Issue log
  wg3n2098 AP validation report
  wg3n2100 SEDS on ISO 14649 parts to SC1/WG7

## Slide 3: Document Update
Document updated with resolutions to all DIS ballot comments
  Held DIS ballot workshop, Valencia June 2005, developed resolutions for all comments
  See resolution discussion slides (wg3n2095) and issue log (wg3n2099) for all details
Comments categories
  Relationship between AP-238, ISO 14649, the STEP manufacturing suite APs and others
  Harmonization of information requirements
  General document wording and structure
  Missing information requirements
  Usage clarifications needed
  Mapping and EXPRESS bugs
  Editorial bugs

## Slide 4: Comment Resolution (1)
Relationship between AP-238, ISO 14649, STEP manufacturing suite APs, and others
  Clarified wording where possible, added many NOTEs, under the following constraints
    SC4 boilerplate text could not be changed without SC4 resolutions
    The normative scope that was approved could not be changed without another DIS ballot cycle.

## Slide 5: Comment Resolution (2)
Harmonization of information requirements
  Updated to published versions of ISO 14649-10, 11, 12, 111, and 121 documents.
    Final tool model in 111/121 had changed quite a bit from FDIS versions used in AP238 DIS
    Updated mappings to match new model, but the AIM representation remained similar.
    Confusion between Aachen and Geneva over P111?
  All ISO 14649 issues discovered during testing and AP development have been documented as SEDS report for SC1/WG7 (see wg3n2100) Issue resolutions included in AP238 for publication in this edition.
  When added to future editions of ISO 14649, future editions of AP238 can just reference instead of maintaining two copies of the definition (as we did with AIC522)

## Slide 6: Comment Resolution (3)
General document wording and structure
  Added all AOs to clause 4.2 to make the contents of the document easier to grasp.
  Imported AOs have a normative reference to the ISO 14649 document and an informative note with express description.
  Annex K has been reworked with annotated AIM examples for the 14649 P11 and P12 examples, CC1 and CC2 examples.

## Slide 7: Comment Resolution (4)
Missing information requirements
  Documented as SEDS report for SC1/WG7 for inclusion into ISO 14649 (see wg3n2100).
  Added roughing and finishing for freeform milling
  Added assumed machine tool characteristics based on machine_parameters from AP240
  Added tool_usage to link tool requirements to actual tool. Based on AP240 with carousel id, and tool position, reference to product or PLIB entries for tool.
    Eliminated DIS tool_holder_profile as redundant
  Added AP224/240 general surface, part, etc properties
  Added workpiece PDM fields and toolpath ID field.
  Added volume, area, mass measures to support the CAD geometric validation properties.
  Added support for full range of shape representations

## Slide 8: Comment Resolution (5)
Usage clarifications needed
  Expanded “Fundamental Concepts and Operation” section with additional discussion and examples for all measures, contexts, toolpath geometry details, and additional feature discussions.
  Doubled the number of diagrams in the main body (21->49)
Mapping and EXPRESS bugs
  Updated AIM to latest IRs (p41e3 and aic522e2)
  Running mapping paths through checking tools
  Work with AP224 and AP203 data sets identified several small mapping issues with features, pdm, and shapes.
Editorial bugs
  Many fixes to the text
  Regenerating EXPRESS-G

## Slide 9: Walkthrough of AP-238
From ISO 14649-10
Measures
Project
Workpiece
Features
Milling Process Operations From ISO 14649-11
Milling Cutting Tools From ISO 14649-111
Turning Process Operations From ISO 14649-12
Turning Cutting Tools From ISO 14649-121
Executable
Operation
Toolpath
AP-238 pulls together machining process, tool requirement, geometry, tolerances, and PDM.
  Start with process and tools described by ISO 14649 parts
  Add STEP PDM, Geometry, and Tolerances, and integrate so that features and all other data can be shared across APs
Dimensions and Tolerances STEP GD&T
PDM and Product Geometry Common to all APs

## Slide 10: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 11: Workpiece, Shape, and PDM
Workpiece is a STEP product description
Has owner information, approvals, dates and times.
Material and material properties
Workpiece uses the same STEP shape representations as AP203, AP214, AP224 and other STEP APs.
Produced by any CAD system that supports STEP.

## Slide 12: Machining Features
round hole
counterbore hole
compound feature
pocket with
through bottom
condition
pocket with
flat bottom
condition
slot with
radius
ends
2.5D milling features
  Hole, pocket, slot, step, etc
Transition features
  Edge round and chamfer
Replicate feature
  Patterns of repeated features
Region features
  Surfaces for freeform milling
Turning features
  Outer round, knurl, groove
Notes: This slide represents the highlights of AP224.
The list of items in each box represents a sample of what AP224 contains.
To summarize - AP224 contains everything found on a drawing of a part

## Slide 13: Machining Features
Features can have implicit and explicit shape
  Implicit feature shape is a parametric description using profiles and paths
    The parameters may have plus/minus, limits and fits, max/min limitations.
  Explicit feature shape links geometry faces to features for visualization, etc.
Implicit description
A round_hole is defined by a complete circular profile and a linear path
Explicit description
Refers to the B-REP faces on the geometry that describe the hole

## Slide 14: Process and Final Features
An AP-238 model can document both final feature and process feature
  Final feature is on final part, from upstream, possibly from an AP-224 or AP-240 application. As such, some features might only define a volume when combined with the stock.
  Process features are the features pointed to by workingstep. Specific to a workplan, needs full volume limits.
  Workingstep can also point to one or more final features that it contributes to. Many workingsteps and process features may contribute to one final feature.
Final feature in red (POCKET)
Process features to:
- Drill the corners (HOLE)
- Mill out center with large tool (POCKET)
- Mill remaining material
with smaller tool (FINAL POCKET)

## Slide 15: Dimensions and Geometric Tolerances
Dimensions defining location
  Location defined by a linear distance
  Location defined by a distance along a curve
  Location defined by an angle
Dimensions defining size
  Curves, angle, diameter, radius, thickness, length, width, height
Geometric characteristics with datums as needed.
  angularity, circular runout, coaxiality, concentricity, cylindricity, flatness, line profile, parallelism, perpendicularity, position, roundness, straightness, surface profile, symmetry, total runout
0.01
0.01
A
0.01
A

## Slide 16: GD&T and Measures
The GD&T definitions are harmonized across all design and manufacturing APs.
  Harmonized across AP-214, AP-224, AP-240, and AP-203e2, which uses Modules 1050 and 1051. Will also be going into AP-219 and other APs.
AP238 measure values and units
  Geometric shape and measure parameters can specify their units, as in all other APs.
  Parameter tolerances can be used for any quantity, not just lengths. Now available for angles, speeds, etc.
  ISO 14649 did not allow choice of units. (mm, deg, m/s only) and parameter tolerances limited to lengths.

## Slide 17: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 18: Machining Programs
The heart of the STEP-NC model
  Workplans containing a sequence of workingsteps.
  Each workingstep associates an operation with a feature somewhere on the workpiece.
  Each operation describes what to do (mill/drill/turn, toolpaths), tool requirements, strategies and parameter settings to use.
More information than M and G codes. Linked with geometric and technological information.
  Parameters can be grouped and shared, e. g. tools, feeds, etc.
  Toolpaths specified in STEP geometry in part space.
  Part shape and feature descriptions could be used by intelligent NC controllers for collision detection or even to calculate some tool movements.

## Slide 19: Machining Programs
Project
  Starting place, defines setup and main workplan
Executables
  Describes control flow and sequencing.
  Workingstep associates an operation and a feature.
  Technology independent
Operations
  Describes what a workingstep does — plane mill, center drill, contour turning, etc.
  The basis for all technology-specific extensions.
  Specifies details like
    spindle, feedrate and other technology parameters
    coolant & other machine functions
    tool paths, plunge strategies, etc.

## Slide 20: Control Flow and Sequencing
executable
nc function
program
structure
workingstep
machining workingstep
rapid movement
touch probing
STEP-NC Executables
Program steps that do not move any machine axes
(display message, etc.)
Control flow for the machining program
workplan
parallel
if_statement
while_statement
Program steps that move
the machine axes

## Slide 21: Toolpaths
Diagram WZL RWTH Aachen
Used for explicit control of the tool motion for an operation.
  Can use splines or other curves to describe motion and feedrates.
  Can describe path as machine independent motion of tool center point or tool contact point.
  Can also describe path using old-style machine dependent motion of individual axis.

## Slide 22: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 23: Milling Process Operations
Drilling Operations
  Drilling, boring, back boring, tapping/threading
  Tool moves in the Z axis only
  Many strategy parameters
2.5D Machining Operations
  Plane and side milling, roughing and finishing
  Tool can move XY or along Z, but not at the same time.
  Set of strategies
Freeform Machining Operations
  For sculpted surfaces
  3, 4, and 5axis motion
  Set of strategies

## Slide 24: Turning Process Operations
Turning Operations
  Contouring, facing, grooving, threading and knurling.
  Roughing and finishing for each
  Set of strategies
Possible Future Operations
  Work underway in SC1 to describe operations for EDM, contour cutting of wood and glass, grinding.
  Add to future AP-238 editions when mature.

## Slide 25: Milling and Turning Cutting Tools
Every operation can have a tool associated.
  Represents tool requirements, not a physical tool on a machine.
  Potential for some optimization by the controller.
G&M codes just referenced tool #1, #2, etc.
  Human must make sure that #1 corresponds to the right thing.
  Controller not able to add any value to the process.

## Slide 26: Milling and Turning Cutting Tools
Call out characteristic tool parameters
  Endmills, facemill, ball endmill, bullnose endmill, side mill, tslot, tapered, dovetail, thread mills
  Drills, centerdrill, twist, tapered, or spade drills, combined drill and reamer or tap
  Boring and reaming tools, tapered reamer, counterbore, countersink
  Turning, grooving and knurling tools, taps and threading tools

## Slide 27: Summary
Yet to do:
  Finish updating ARM & AIM EXPRESS-G diagrams.
  Add CC1 and CC2 examples for Annex K
  Run through checklists and WG3 signoffs
Send to ISO for publication ~2 weeks after Toulouse meeting.

## Slide 28: AP-238 OMAC Testing Forums
Running AP-238 testing activities in conjunction with OMAC STEP-NC working group.
  January 2005 forum in Orlando focused on 5axis testing with cutter location paths, four data sources and two controls configured for different machine geometry
  May 2005 Eastec demonstration of closed-loop tests with cutter contact paths
AP-238
AB Tool Tilt
BC Table Tilt

## Slide 29: AP-238 OMAC Testing Forums
Produced test articles in 5-axis machining tests at Boeing and NIST using AP-238
  NAS 979 circle/diamond/square with inverted cone
  Representative aerospace part with 1-2degree inclines and tightly constrained positioning holes

## Slide 30: AP-238 Demonstrations
June 2006 Industry Day Demonstration
  Live demonstration of 5-axis milling of aerospace test parts provided by Airbus.

## Slide 31: AP-238 Test Sets
Created archive of AP-238 machining test data sets for distribution to future testers.
  Currently ~100 data sets spanning a variety of machining programs with STP files, screen dumps, reports and such.
  CC1 and CC2 files, simple 2.5D as well as multi-axis paths, surfacing and high-speed paths