## Slide 1: Describing Toolpaths in an AP-238 CC1 file
Martin Hardwick
hardwick@steptools.com
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax

## Slide 2: This Walkthrough
This walkthru describes the AP-238 entities required to define a toolpath
  It shows what values are
    Required by the AP-238 standard (underlined in red)
    Suggested to help debugging by showing the workingstep or tool path uses the entity.
    Suggested values can be ignored if you have a better debugging method.
Other walkthru’s describe.
  How to represent other APT information in an AP-238 CC1 file
  How to add the entities necessary to conform to the standard

## Slide 3: Syntax conventions
The boxes represent entities
  The text attributes of the entity are described in the box
  If a value is required by the ISO standard it is underlined and shown in red
The arrows represent attributes that are implemented as addresses in the Part 21 file
  The direction is important
  The label on the arrow is the name of the EXPRESS attribute
Entities are described
  If an entity is not described on this page then it will have a box
  If an entity is described on another page then it will be shown in bold case
  If an entity is a constant value then it is shown in green. See the end of this slide set for a description of these values

## Slide 4: Basic organization of the AP-238 CC1 file
Per file
  One Project
  One Workplan
Per Tool change
  One Workingstep
  One Freeform_milling operation
Per Feed, Speed or Coolant change
  One Machining_toolpath
Workplan
Workingstep
1
n
Freeform_milling
1
1
Machining_toolpath
1
n
LOADTL
COOLNT
FEDRAT
SPINDL
RAPID

## Slide 5: The Project – name and version data
#40=application_
protocol_
definition
product_definition
id = machining_project.name
description = ’machining project’
machining_project
id = formal program name
name = informal program name
description = ’’
product_definition _formation
id = version number
description = ‘machining project’
of_product
process_product_association
name = machining_project.id
description = ’’
product_definition_process
name= ‘machining’
description = ’’
Identification = ’’
machining_workplan
#10=product_context
#30=product_definition_context
frame_of_reference
formation
frame_of_reference
defined_product
process
chosen_method
#20=application_context

## Slide 6: The Workplan – one per file
machining_workingstep
machining_workplan
name = ‘AP-238 CC1’
description = ‘main workplan’
consequence = ‘’
purpose = ‘’
machining_process_sequence_relationship
name = machining_workingstep.name
description = ‘’
sequence_position = 1.0 for 1st, 2.0 for 2nd etc.
relating_method
related_method
machining_process_sequence_relationship
name = machining_workingstep.name
description = ‘’
sequence_position = 1.0 for 1st, 2.0 for 2nd etc.
relating_method
related_method
product_definition_process
process
machining_workingstep
name = ‘WS 1’, ’WS 2’, ‘WS 3’ etc.
description = ‘machining’
consequence = ‘’
purpose = ‘’
freeform_milling_operation
relating_method
related_method
machining_operation_relationship
name = machining_workingstep.name
description = ‘’
related_method

## Slide 7: Freeform_milling – one per LOADTL
freeform_milling_operation
name = machining_workingstep.name
description = ‘AP-238 CC1’
consequence = ‘’
purpose = ‘’
related_method
machining_operation_relationship
machining_toolpath_sequence_relationship
name = machining_toolpath.name
description = ‘AP-238 CC1’
sequence_position = 1.0 for 1st, 2.0 for 2nd etc.
relating_method
machining_toolpath
related_method
usage
machining_tool
name = ‘milling cutting tool’
description = user name for tool
action_resource_type
kind
machining_toolpath_sequence_relationship
relating_method
“Consider also creating a new operation for each change of spindle speed”

## Slide 8: Machining_toolpath – one per FEDRAT
machining_toolpath
name = machining_workingstep.name + ‘TP 1’ or ‘TP 2’ etc.
description = ‘cutter location trajectory’
consequence = ‘’
purpose = ‘’
related_method
machining_toolpath_sequence_relationship
machining_technology_relationship
relating_method
action_property
name = ‘basic curve’
definition
action_property
name = ‘tool axis’
definition
machining_functions_relationship
relating_method
“Also need a new machining_toolpath for each COOLNT change”
“Coolant”
“feed and speed”
“x, y,z”
“i, j, k”

## Slide 9: Basic curve and tool axis representations
representation
name = ‘basic curve’
representation
polyline
name = machining_toolpath.name
property
action_property
name = ‘basic curve’
description=machining_toolpath.name
action_property_representation
name = action_property.name
description=action_property.description
#110= representation_context
items[1:1]
cartesian_point
name = user data
coordinates=X, Y,Z
points
representation
name = ‘tool axis’
representation
polyline
name = machining_toolpath.name
property
action_property
name = ‘tool axis’
description=machining_toolpath.name
action_property_representation
name = action_property.name
description=action_property.description
items[1:1]
cartesian_point
name = user data
coordinates=I, J, K
points
#120=representation_context
machining_toolpath
definition
definition
“Same number of points
required in both curves”
“If MULTAX on”

## Slide 10: Machining_technology (feed and speed)
machining_technology
name = ‘AP-238 CC1’
description= ‘milling’
consequence = ‘’
purpose = ‘’
definition
related_method
action_property
name = ‘feedrate’
description=machining_toolpath.name
relating_method
action_property_representation
property
machining_toolpath
definition
action_property
name = ‘spindle speed’
description=machining_toolpath.name
action_property_representation
property
Machining_technology_relationship
name = machining_toolpath.name
description=‘coolant value’

## Slide 11: Feedrate representation
machining_feed_speed_representation
name = ‘feed speed’
representation
measure_representation_item
name = ‘feed speed’’
value_component = value
unit_component = inches per minute
property
action_property
action_property_representation
name = action_property.name
description = ‘’
#120=representation_context
items[1:1]

## Slide 12: Spindle speed representation
machining_spindle_speed_representation
name = ‘spindle speed’
representation
measure_representation_item
name = ‘rotational speed’’
value_component = value
unit_component = revolutions per minute
property
action_property
action_property_representation
name = action_property.name
description = ‘’
#120=representation_context
items[1:1]

## Slide 13: Machining_functions (coolant)
machining_functions
name = ‘AP-238 CC1’
description = ‘milling’
consequence = ‘’
purpose = ‘’
definition
related_method
action_property
name = ‘coolant’
description = machining_workingstep.name
machining_toolpath
relating_method
action_property_representation
property
Machining_functions_relationship
name = machining_toolpath.name
description = ‘coolant value’

## Slide 14: Coolant representation
representation
name = ‘coolant’
representation
descriptive_representation_item
name = ‘shared constant’
description = ‘coolant on’
property
action_property
action_property_representation
name = action_property.name
description = action_property.description
#120=representation_context
Items[1:1]
Or description = ‘coolant off’

## Slide 15: RAPID
action_property
name = ‘speed profile’
description = machining_toolpath.name
machining_toolpath
definition
“Other speeds are ignored if the path has this property”
“Toolpath that is to be RAPID”
representation
name = ‘rapid’
representation
descriptive_representation_item
name = ‘constant’
description = ‘rapid’
#120=representation_context
Items[1:1]
property
action_property_representation
name = ‘rapid’
description = ‘’