## Slide 1: Lifecycle data model of machine tool products
2006. 10.
Suk-Hwan Suh
Center for Ubiquitous Manufacturing
POSTECH, Korea
shs@postech.ac.kr

## Slide 2: Background
ISO 14649 Part 110, Machine tool data model is under development by ISO TC184/SC1/WG7
Harmonized with Machine Tool data model under development by ISO TC39
Joint work necessary between ISO TC184 and TC39
Joint Meeting between ISO TC184/SC1/WG7 and ISO TC39/SC2 held in Busan Korea, May 11, 2006
Proposal for developing machine tool product model is represented in Toulouse, June 29, 2006

## Slide 3: Scope
Goal:
  General and comprehensive data model covering the whole product life cycle of machine tools and supporting activities related to machine tools
The scope of machine tools data model from the perspectives of ;
  MTB (Machine Tool Builder):
    Covering the whole manufacturing process such as design, manufacturing, test & evaluation, distribution, and guarantee service (maintenance), recycle & reuse.
    Supporting the transaction among MTBs, sub contractors, and customer
  Collaborative Product Commerce (CPC):
    Supporting the realization of the e-Manufacturing.
    Covering the data which is required in the collaborative manufacturing process
  Customer support and environment:
    Supporting sales of new machine tools and used machine tools

## Slide 4: Application of product lifecycle data model for machine tools
Product Life Cycle Support
SCM (MTB & sub contractor)
e-Commerce (B2B, B2C)
Digital manufacturing (STEP-Manufacturing)
  Process planning / Machine programming
  Virtual machining
  Virtual NC
  Factory flow simulation
  Workspace design
Performance verification and tracking/process variability/quality control
Plug-and-play machine installation, self-identification
Machine intelligence (self-knowledge)
Maintenance
Environment (Recycle/Refurbish, …)
CRM (Customer Relationship Management)

## Slide 5: Considerations for data model
Comprehensiveness
  Data model can represent the general properties of machine tools with regardless of the machine tool type.
Specification
  Data model can represent some special properties of machine tool product as individual product.
Throughout the entire lifecycle
  Data model can include the whole product life cycle of machine tools and supporting activities related to machine tools
  Also data model can represent the historical data of machine tool product as individual product.
Extensibility
  Data model can represent a new type of machine tools without adding or modifying existing data model.
Interoperability
  Data model can be interoperable with existing standards such as STEP, STEP-NC and so on.

## Slide 6: Related International Standards to be referenced for the Machine tools data model
ISO TC39
  The standards for interchangeability between components
    Headstock, spindle, column, base, table, rotary table, etc.
  The standards for testing machine tools
    Test method, Test code, Test condition, etc.
ASME B5
  Draft B5.59-1: “Data Specification for Machine Tool Performance Tests”
  Draft B5.59-2: “Data Specification for Properties of Machine Tools for Milling and Turning”
ISO 14649 Part 110
  Under development by ISO TC184/SC1/WG7
  Functional requirement data model for machine tools
(POSTECH model)
  Developed for TurnSTEP, Type 3 STEP-NC system for turning developed by POSTECH
  Mainly for configuration (structure, kinematics) of machine tools

## Slide 7: Related International Standards to be referenced for the Lifecycle & Business
STEP AP 239 PLCS
  PLCS specifies the information requirements for product lifecycle support and the integrated resources necessary to satisfy those requirements
  Categories
    Product assembly
    Through life product
    Specification and planning of activities
    Activity history
    Product history
MANDATE (ISO 15531)
  ISO 15531 is an International Standard for the computer-interpretable representation and exchange of industrial manufacturing management data.
  Manufacturing management data includes the flow of materials and products through the whole production chain, from suppliers, through manufacturers, assemblers, to distributors and sometimes customers
  Categories
    information related to the external exchanges, e.g., between main plant and suppliers;
    information related to the management of the resources used during the manufacturing processes;
    information related to the management of the manufacturing flows.
Other STEP Standard such as STEP AP203, STEP AP224 and STEP-NC (ISO 14649)

## Slide 8: Activities and data required in BOL
Production Planning
  Brief spec. of machine tools ( executable operation, capacity, etc)
  Business data (due date, production volume, etc)
Design
  2D Drawing, 3D Solid Model, spec. for each components
  Machine tools spec. and performance.
  Design BOM
Procurement from sub contractor
  Drawing and 3D solid model of components
  The spec. (Performance & Quality) of components
  Business data (due date, the volume of order, etc)
Manufacturing
  Manufacturing BOM
  Assembly data
Test & Evaluation
  Test item, Test method, Test procedure
Sales & installation
  Catalogue, installation guide
  Manuals: usage manual, NC manual, application manual (CAP, CAM, etc), etc.
Machine tool product data model
MANDATE
Machine tool product data model
ASME B5.59-2
PLCS (STEP-PDM)
Machine tool product data model
MANDATE
Machine tool product data model
PLCS
ISO TC39 Work
ASME B5.59-1
Machine tool product data model

## Slide 9: Activities and data required in MOL
Client data
  Usage data
    Machining history data
    Operating conditions (Environment)
  Traceability data
  Customer requirement
Maintenance data
  Manual
  Diagnosis and evaluation
    Machine tools error: yaw, roll, pitch of each axis, and angularity, backlash error, etc
    Diagnosis history: Diagnosis data, result, action, …
    Compensation history: pitch error compensation, backlash error compensation
  Repair and replacement
    Failure history: breakage components, data, reason, maintainer, maintaining time
    Replacement of the components
  Preventive Maintenance
    Preventive maintenance history: date, components, …
    Tool life management
Business data
  Purchase data
  Inventory data
PLCS
Machine tool product data model
PLCS
Machine tool product data model
MANDATE

## Slide 10: Activities and data required in EOL
Processes in EOL
  Repair
  Remanufacturing
  Recycling & Reuse
  Disposal
Required data
  Design data
    Physical structure : size, shape, weight, etc
    Material composition
  Reliability
    Expected life of components
  Disassembly
    Disassembly instructions
    Disassembly process plan
  Production information
    Design changes
    Material and structural changes
  Lifecycle information
    Operating conditions
    Maintenance data
    Part replacement information
Generated data
  Condition of the product
  Life of the product & components
  Recycle/reuse information
  …
Machine tool product data model
PLCS
Machine tool product data model

## Slide 11: Overall data model for machine tools (Ver. 1: presented in the Busan Meeting, 2006.05)

## Slide 12: Revised Overall Data model Structure (Ver. 2, Hershey, 2006.10)
Static Data:
In general, these data are generated in BOL and are not changed.
Dynamic Data:
- In general, these dare are generated in MOL and EOL
These data are changed every constant time interval, irregularly, or in real time.
Not developed yet. Detail data modeling is necessary
Not developed yet. Detail data modeling is necessary

## Slide 13: Revision summary (Ver.1 vs Ver.2)
Data model are grouped according to the product life cycle
  BOL data for engineering and business data
  MOL data for maintenance, breakdown, history, and so on
  EOL data for recycle, remanufacturing, reuse, and so on
Data model is harmonized with existing international standard
  Many data are referenced from existing ISO standard such as PLCS
    BOL data such as product structure, product assembly, product identification, and so on
    Through life product data such as activity, history, breakdown, and so on
  Machine tool product and part will be harmonized with ASME B5.59-2

## Slide 14: Overall structure from the perspective of related international standard
: Company own standard
and Need to be developed
: Draft version by ASME B5
: STEP and STEP-NC
ASME B5.59-2
PLCS (STEP-PDM)
PLCS
ASME B5.59-2
ASME B5.59-1
ISO 14649 Part 110 will be developed by ISO TC184/SC1/WG7

## Slide 15
Machine tool data model : Composite machine tool

## Slide 16
Machine tool data model : Spindle

## Slide 17
Machine tool data model : Axis

## Slide 18
Machine tool data model : Turret

## Slide 19: Execution plan
Resolution
Call for participation !!!
(joint working group/authorship, etc)