## Slide 1: Developing process of STEP Manufacturing
Len Slovensky
Information System Technologist
Northrop Grumman Corp. IT
Charleston Operations
+1 513-383-8311
slovensky@scra.org

## Slide 2: Status of STEP standards since last Sapporo meeting in 2005

## Slide 3: Development since 2005 Sapporo meeting
AIC 522 - Application interpreted construct: Machining features
  2ND edition published 2006
AP219 - Dimensional inspection information exchange
  Passed DIS ballot 2006, IS to be published early 2007.
AP224 - Mechanical product definition for process planning using machining features
  3rd edition published 2006
  SCRA has discovered errors and has submitted SEDS against part.

## Slide 4: Development since 2005 Sapporo meeting
AP238 - Application interpreted model for computerized numerical controllers
  1st edition in publication process - 2006
AP240 - Process plans for machined products
  SCRA has discovered errors and has submitted SEDS against part.
AP223 - Exchange of design and manufacturing product information for cast parts
  CD ballot passed 2006
  DIS to be ready by the end of 2006
AP229 - Exchange of design and manufacturing product information for forged parts
  NWI approved 2006

## Slide 5: Review of STEP suite of APs architecture

## Slide 6: Conceptual Basis -- SMS
Function
Defense
C4 Data
Standards
Org
Technology Pro/ENGINEER ICAD CAM System CNC Controllers
Example STEPTrans MetCAPP STEPTools, Inc Turning and/or
STEPValidator STEPPlan Technology Milling Centers
STEP
Product Data Generation
AP224
AP203
DESIGN or Legacy Data Capture
AP224
AP240
Macro Process Planning
AP240
w/ AP224
Features
AP238
AP238
FACTORY
Part
Fab
Finished Part
Micro Process Planning/NC Coding
Inspection
AP219
CMM
AP238
AP240
Classic Work Tasks | Design or Capture Part Features Dim. & Tol. Material Notes & Spec’s Translate to STEP AP224 Validate AP224 file against design | Define Route steps and Sequence Select Resource for each step Apply Operation Standard Times Material/BOM Cost Est. Input Order Tools/ Fixtures Inspection Instructions | Setup Graphics Develop Cutter paths Post Process NC Program Operator instructions Finalize Tool List | Download NC Program Load Preset Tools Set Offsets Load Part Machine Part Optimize NC Program Inspection Unload Part Move part to next Route Step
Prototype Facility
Or FACTORY
Prototype Facility
Or FACTORY

## Slide 7
Function
Defense
C4 Data
Standards
STEP
Product Data Generation
AP223
AP229
AP224
AP240
Macro Process Planning
AP240
w/ AP224
Features
AP238
AP238
Part
Fab
Finished Part
Micro Process Planning/NC Coding
Inspection
AP219
CMM
AP238
AP240
AP223
Macro Process Planning
AP223
AP229
Org
FACTORY
AP223
AP229
Micro Process Planning/NC Coding
AP238
AP223 or
AP229
w/ AP224
Features
Cast or
Forged Part
Part
Fab
AP238
Conceptual Basis – SMS (for cast or forged parts)
Molding/ Die design
AP223
AP229
ISO-13399
Cutting tools

## Slide 8
Part and Shape
Shapes of cast parts and rigging
Materials of cast parts
Tolerances and surface finish
Physical and mechanical properties
Harmonized withAP224 features, tolerances, properties
Mold Design
Shapes of sand mold, die assembly, and investment pattern assembly
Materials used in the casting processes
Building a sand mold, a die assembly, and an investment pattern assembly
Casting process simulation
Shape representation
Process design parameters
Simulation input and results
Quality Control Records
Processes of building a sand mold, of building a die assembly, and of building an investment pattern assembly.
Processes of melting, pouring, cooling, shaking out, extracting, and knocking out a casting
Melting processing and resulting metal composition
Inspection and testing results of the cast part.
Process Plan
Process_plan harmonized with AP240
Melting, pouring, cooling, shakeout, extracting, and knocking out a casting
Process used to produce a casting
Metal alloys used to product a casting.
Equipment used to produce a casting.
AP223 - Exchange of Design and Manufacturing Product Information for Cast Parts
Cast_part
Designed_part
Cast_part_with_rigging
Cast part Tooling

## Slide 9: Integrated Manufacturing Architecture using Manufacturing features
Dimensional Inspection Information Exchange
Manufacturing
Features
&
Tolerances
Exchange of Design and Manufacturing Product Information for Cast Parts
AP219
AP224
Mechanical product definition for process planning
using machining features
Process plans for
machined parts
AP240
CMM
Application interpreted model for computerized numerical controllers
CNC
AP238
AP223
CAD/CAM
Exchange of Design
and Manufacturing
Product Information
for Forged Parts
AP229
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10
Feature harmonization

## Slide 11
1993
1999
1996
2000
2002
2004
AP224 New Work item Included GD&T
AP224 & AP214 Finalized harmonization of GD&T
AP224 Published with GD&T
AP214 Published with harmonized GD&T
AP240 NWI included GD&T Harmonized With AP224
AP240 DIS with harmonized GD&T
AP219 CD Published with GD&T
Harmonization of GD&T with AP203e2
2005
AP223 and AP229 NWI included GD&T Harmonized With AP224
Today
AP203e2, AP219, AP223, AP229, AP238 & AP240 GD&T Harmonized With AP224
AP238 DIS with harmonized GD&T
AP224 team joined Part 47 team to support GD&T development
Note: All GD&T development except for AP238 was a lead by members of SCRA and PDES Inc.
Dimensional and Geometric Tolerance Time Line

## Slide 12: UoF Harmonization
Features
Administration Data
Properties
Tolerances
Shape Representation
Materials
AP224
Requisitions
Process Control
Documents
Process requirement
Documents
Part Model
Features
Part Model
Administration Data
Properties
Tolerances
Shape Representation
Materials
AP240
Machine tool
Resources
Process requirement
Documents
Process Plan &
Process Activities
Machine operations
Features
Part Model
Properties
Tolerances
Shape Representation
AP238
Machine tool
Resources
Micro
Process Activities
Workpiece Parameters
Manufacturing APs have harmonize data other than features and tolerances:
Properties
Part model
Materials
Administration data
Process Plans

## Slide 13: Traditional AP
Application Activity Model
Conformance Classes
Application Reference Model
Mapping Specification
Application Interpreted Model
Application Protocol
Application Resource
Application Interpreted Construct

## Slide 14: Modular AP
Level 1 foundation modules define EXPRESS constructs such as entities, types, and extensible selects for the ARM application objects and the corresponding MIM.
Level 2 implementation modules are a collection of modules (Level 1 or 2) that define a capability that can be implemented and against which conformance classes may be defined

## Slide 15: Manufacturing APs structure
All of the manufacturing APs are traditional AP and not modular APs.
  Development of modular APs took more manpower resources than were available.
  Existing modular APs were duplicating modules because there was disagreements on requirements
    For example AP210 and AP203 have different modules for geometric and dimensional tolerances
  Created a structure to difficult to explain to the industry that was supplying requirements to the AP development team.

## Slide 16: Manufacturing APs issues
The exchange for AP223 castings have discovered a need for an interface to
  Finite Element Analysis (FEA)
  Finite Difference Analysis (FDA)
There is a need to develop a manufacturing FEA FDA interface or AP.

## Slide 17: Manufacturing APs issues
Product Life Cycle (PLM)
  PLM (Product Lifecycle Management) is the latest buzzword floating around in the manufacturing industry.
  First of all, there is no common agreement on what PLM is
  Secondly, the road map of PLM implementation is still pretty vague as the boundary of its coverage is hard to define.
  Need to research on how manufacturing APs can be used for PLM.

## Slide 18: Status of manufacturing APs
Backup slide
(info but not a part of presentation)

## Slide 19
Part and Shape
Shapes of cast parts and rigging
Materials of cast parts
Tolerances and surface finish
Physical and mechanical properties
Harmonized withAP224 features, tolerances, properties
Mold Design
Shapes of sand mold, die assembly, and investment pattern assembly
Materials used in the casting processes
Building a sand mold, a die assembly, and an investment pattern assembly
Casting process simulation
Shape representation
Process design parameters
Simulation input and results
Quality Control Records
Processes of building a sand mold, of building a die assembly, and of building an investment pattern assembly.
Processes of melting, pouring, cooling, shaking out, extracting, and knocking out a casting
Melting processing and resulting metal composition
Inspection and testing results of the cast part.
Process Plan
Process_plan harmonized with AP240
Melting, pouring, cooling, shakeout, extracting, and knocking out a casting
Process used to produce a casting
Metal alloys used to product a casting.
Equipment used to produce a casting.
AP223 - Exchange of Design and Manufacturing Product Information for Cast Parts
Cast_part
Designed_part
Cast_part_with_rigging
Cast part Tooling

## Slide 20
Defense
C4 Data
STEP
Product Data Generation
AP223 for
Red line markup
Macro Process Planning
Foundry
AP223 for
Cast part or
Cast part with rigging
Tooling/
Pattern shop
AP223 for
Cast part
Mold
Flow
Simulation
Inspection
Machine
shop
AP223 for
Cast part with rigging
AP219
AP223 for
Design part and
Cast part
Quality Control
AP223 with
AP224 features
Customer
AP223 for
Design part and
Cast part with rigging
AP240
AP223 for
Cast part and
Tooling
AP233 reports
Foundry
AP223 for
Design part
Conceptual Basis – SMS (for cast parts)
Process Planning/NC Coding
Factory
AP238
AP233
All types of part data
AP233 reports
CC1
CC2
CC3
CC4
CC5
CC7
CC4
CC5
CC6

## Slide 21: AP224 3rd edition
AIC522 support
Removed features from AP224s
  Short listing (clause 5.2)
  Changed mapping tables to reference AIC522 instead of clause 5.2
  Recreated EXPRESS short form
    Compiled successfully on multiple compilers
    Successfully tested new schema with test parts

## Slide 22: AP224 3rd edition
Standard part fasteners
Assembly of parts for manufacturing process
  Add standard part fasteners to the mating definition
  AP224 will reference a parts library (PLIB) that contains fasteners definitions

## Slide 23: AP224 3rd edition
Explicit base shape representation
Add information to indicate type of explicit shape, for example:
  Machined from Forgings and Castings
  Machined from Aluminum Plate or Block (Hog Out)
  Machined from Aluminum Extrusions

## Slide 24: AP224 3rd edition
Pocket feature
To harmonize with AP238:
  Added attribute to Pocket feature to have relationship with Boss feature

## Slide 25: AP224 3rd edition
Gear feature
Bevel gear
Spur gear
Helical gear

## Slide 26: AP224 3rd edition
GD&T Harmonization
Response to TC213 Concerns
Value Qualifications
  Value Limit / Value Range / Plus/Minus / Limits and Fits
Size Dimensions
  Common Set of Size Dimensions
  Envelope Principle
  Angular Size Full/Half
Angular Location Dimension
AP-214 SEDS
  Qualifying notes
  Dimension standard

## Slide 27: AP224 3rd edition
Other small editorial changes
  Several found by AP238 development

## Slide 28: AIC 522 2nd edition
Gear feature
Bevel gear
Spur gear
Helical gear

## Slide 29: AIC 2nd edition
Pocket feature
To harmonize with AP238:
  Added attribute to Pocket feature to have relationship with Boss feature

## Slide 30: AIC 522 3rd edition
Other small editorial changes
  Several found by AP238 development
    Flat_face add new attribute removal depth
    Rounded_U_profile ans Square_U_profile add new attribute for depth.
    Vee_profile add new attribute first_side_length and second_side_length
    Move constaint rules for chamfer and edge_round to AP global rules, AP238 does not use these constraints
    Miscellaneous editorial fixes
  These changes also were made to the AP224 3rd edition document.

## Slide 31: AP219 - Dimensional Inspection Information Exchange
Analysis
Feature analysis mode
Feature tolerance mode
Parameter analysis mode
Dimensional Measurement features
Circle, arc, sphere
Geometric surface
Lines, planes
Pattern
Measurement execution
Execution result
Execution result measurement
Data acquisition software
Result parameter
Program run
Program identification
Run administrator
Measurement location
Program Run
Tolerances
Geometric tolerances
Dimension tolerances
Material condition modifier
Tolerance range
Part Properties
Calculated value
Parametric calculated value
Parameters
  Property
  Numeric
  Descriptive
Part
Part
Manufacturing features
Shape representation
  Brep model
  Explicit base shape
  Implicit base shape
Measurement parameters
Dimensional parameter
Point parameter
Vector parameter
Parameter value limits
Administration data
Person and Organization
Date and time
Time offset
Notes: <number>
<footer>
<header>
<date/time>
This Application Protocol will specifies the information requirements to manage dimensional inspection of solid parts or assemblies, which includes administering, planning, and executing dimensional inspection as well as analyzing and archiving the results. Dimensional inspection can occur at any stage of the life cycle of a product where checking for conformance with a design specification is required. AP219 uses AP224 features to define the “as designed” machining feature, and uses this information to create an inspection feature to define data “as inspected” AP219 then defines the calculated values from the inspection and links this data to the “as designed feature” and the “as inspected feature” for analysis.

## Slide 32: Harmonization: Mapping and integration
Harmonization through mapping between requirements specifications
Harmonization through integration of requirements specifications
AP219
View
AP224
View
integration
mapping
AP219
View
DMIS
View

## Slide 33: AP219 Harmonization activities
Dimensional inspection
  DMIS (Dimensional Measuring Inspection Standard)
  ISO 22093 (DMIS equivalent)
  Metrology Interoperability Project
  (Reporting Work Group of the Automobile Industry Action Group)
mapping
integration
STEP
  AP224 (Process Planning using Machining Features)
  AIC 522 (Machining Features)
  AIC 519 (Geometric Tolerances)

## Slide 34: AP219 feature sets
Dimensional_inspection_features
  Dmf_arc
  Dmf_circle
  Dmf_cone
  Dmf_cylinder
  Dmf_edge_point
  Dmf_ellipse
  Dmf_generic_feature
  Dmf_geometric_curve
  Dmf_geometric_surface
  Dmf_line_bounded
  Dmf_line_closed_parallel
  Dmf_line_unbounded
  Dmf_pattern
  Dmf_plane
  Dmf_plane_closed_parallel
  Dmf_plane_symmetric
  Dmf_point
  Dmf_sphere
  Dmf_surface_of_revolution_dml
  Dmf_torus
Machining_features
  different categories of features
  Many features have sub-categories
    Boss
    Pocket
    Hole
    Slot
    Protrusion
    Rounded_end
    Outer_round
    Step
    Planar_face
    Revolved_feature
    Spherical_cap
    General_outside_profile
    Thread
    Marking
    Knurl
    General_volume_removal
Transition_features
  different types of transitions
    Chamfer
    Fillet
    Edge_round
Replicate_feature
  3 different ways to replicate features
    Circular_pattern
    Rectangular_pattern
    General_pattern
Compound_feature
  Union of one of more features to create a more complex feature definition.
DMIS Feature nominal
DMIS Feature actual

## Slide 35: AP219 tolerances
Dimensional tolerances
  Size tolerance
    radial
    diameter
    curve dimension
    angular size
  Location tolerance
    distance along curve
    angular
    Location
Tolerance value
  Plus minus value
  tolerance limit
  tolerance range
  limits and fits
Geometric tolerances
  Angularity
  Circularity
  Circular runout
  Concentricity
  Cylindricity
  Flatness
  Linear profile
  Parallelism
  Perpendicularity
  Position
  Straightness
  Surface profile
  Symmetry
  Total runout
Geometric tolerance precedence
Datum
Compound datum
Material condition modifier
Tolerance zone
Datum target

## Slide 36: AP219 - Dimensional Inspection
Manufacturing
view
Dimensional
measurement
view
15mm + .25
25mm + .5
Hole 2
Hole 1
-
-
Circle 2
Circle 1
Circle 4
Circle 3
AP219 defines two different feature views:
Manufactured feature
Inspection feature
Instances: Counterbore_hole measurement
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: AP219 - Dimensional Inspection with tolerances
Manufacturing view
Dimensional
measurement
view
15mm + .25
25mm + .5
Hole 2
Hole 1
-
-
Circle 2
Circle 1
Circle 4
Circle 3
AP219 defines
  Dimensional Tolerances
  Geometric Tolerances
Instances: Counterbore_hole measurement
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: Manufacturing and dimensional measurement views
Dimensional
Measurement view
Manufacturing view
Manufacturing
feature
Parameter
nominal
Parameter
tolerance
Manufacturing info
Part
Dimensional
measurement
feature
Dimensional
Measurements
Points
Measurement data
Dimensional
measurement
parameter
Calculated
value
Measurement results
DMIS Feature actual
DMIS Feature nominal
specification

## Slide 39: Example part: Nominals, tolerances, and calc values
Counterbore_hole
Hole 1
Hole 2
Nominal
Tolerance
Calc value
15mm
25mm
.25mm
.5mm
15.12mm
24.8mm
+
-

## Slide 40: AP238 Application interpreted model for computerized numerical controllers
Manufacturing Features
Slot
Hole
Planar face
Thread
Outer Round
Chamfer
Workpiece
Workpiece
Material
Parameters
  Property
  Numeric
  Descriptive
Project
Project
Person and address
Tool path
Tool path
Feed stop
Parameterized path
Cutter contact and location trajectory
Measure
Limits and fits
Plus minus value
Tolerance length measure
Operation
Machine functions
Machining operation
Tool direction
Tool path list
Executable
Working step
Working plan
Setup
Cutting tool
If and While statement
Program structure
Process data for milling
Boring
Drilling
Reaming
Tapping
Cutting tools
Drill
Tap
Reamer
Boring tool
Notes: <number>
<footer>
<header>
<date/time>
AP238 is the next step in manufacturing after AP240; this AP defines the micro process planning. Where AP240 defined the high level details for manufacturing a part, this AP defines the specific information for a specific machine. This AP defines specific process information like boring, drilling, reaming or tapping. AP238 defines the setup, sequential working steps, cutting tool specifications for tools like drills, taps, boring tools, and reamers. AP238 describes how to make geometry from a piece of stock by removing AP224 machining features in a sequential order with specific tolerances with tools that meet all of these requirements.

## Slide 41: AP238 – Machining operation
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
L[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Machining features
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: AP240
Several SEDS issues have been submitted by SCRA

## Slide 43: AP240 SEDS #1
5.1.7.5 Dimensional_tolerance
5.1.7.5.1 dimension_description
Other Parts Affected by the Issue: AP203e2, AP224, AP238, AP223, AP229, AP219, AP214
Related Issues:
Summary/Abstract/Keywords: dimensional tolerance, dimensional size
Problem Description:
5.1.7.5 Dimensional_tolerance has two subtypes: size_tolerance and
location_tolerance. size_tolerance mapps to the part 47 entity dimensional_size, and location_tolerance
maps tgo the part 47 entity dimensional_location. However the mapping for Dimensaion_tolerance maps
to part 47 shape_dimension_representation. The mapping to the subtypes is incomplete.
5.1.7.5.1 dimension_description - the mapping is incorrect size_tolerance and all of the size_tolerance
subtypes. The size tolerance subtimes use dimensional_size.name as a part of the entity mapping.

## Slide 44: AP240 SEDS #1
5.1.7.5 Dimensional_tolerance
#1: Dimensional_tolerance as Dimensional_size
AIM element: shape_dimension_representation
Source: ISO 10303-47
Reference Path: shape_dimension_representation <-
dimensional_characteristic_representation.representation
dimensional_characteristic_representation
dimensional_characteristic_representation.dimension ->
dimensional_characteristic
dimensional_characteristic = dimensional_size
dimensional_size
#2: Dimensional_tolerance as Dimensional_location
AIM element: shape_dimension_representation
Source: ISO 10303-47
Reference Path: shape_dimension_representation <-
dimensional_characteristic_representation.representation
dimensional_characteristic_representation
dimensional_characteristic_representation.dimension ->
dimensional_characteristic
dimensional_characteristic = dimensional_location
dimensional_location

## Slide 45: AP240 SEDS #1
5.1.7.5.1 dimension_description
#1: Dimensional_tolerance as Dimensional_size
AIM element: (dimensional_size.name)
Source: ISO 10303-47
ISO 10303-41
Reference Path: shape_dimension_representation <=
shape_representation<=
representation<-
description_attribute_select=representation
description_attribute_select<-
description_attribute.described_item
description_attribute
description_attribute.attribute_value
#2: Dimensional_tolerance as Dimensional_location
AIM element: (shape_aspect_relationship.description)
Source: ISO 10303-47
ISO 10303-41
Reference Path: shape_dimension_representation <-
dimensional_characteristic_representation.representation
dimensional_characteristic_representation
dimensional_characteristic_representation.dimension ->
dimensional_characteristic
dimensional_characteristic = dimensional_location
dimensional_location <=
shape_aspect_relationship
shape_aspect_relationship.description

## Slide 46: AP240 SEDS #2
Part and Clause where Issue Originates: 4.2.55 Geometric_tolerance, 4.3.65 Geometric_tolerance to Shape_aspect,
5.1.7.8 Geometric_tolerance, 5.1.7.8.1 geometric_tolerance to shape_aspect (as applied_shape),
Annex G diagram G14
Other Parts Affected by the Issue:
Related Issues:
Summary/Abstract/Keywords: geometric tolerances GD&T
Problem Description: The intent of the Geometric_tolerance entity was to create one entity that would define the
need for geometric tolerances, and to use AP224 as a reference, saying that the Geometric _tolerance
entity represents all of the entities defined in AP224 for geometric tolerances, and mapped to AIC 519.
The problem is this does not bring into AP240 all of the datum requirements or tolerance zone requirements.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 47: AP240 SEDS #2

## Slide 48: AP240 SEDS #2

## Slide 49: AP240 SEDS #3
Part and Clause where Issue Originates: 5.2.3.2.20 document_file
Other Parts Affected by the Issue: none
Related Issues: none
Summary/Abstract/Keywords: document
Problem Description: The definition of the entity documen_file defines it as a subtype of
characterized_object and document. This is backwords from AP224 which defines a document_file
as a document and characterized_object, this effects inheritance.
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240
Proposed Solution (Optional):
ENTITY document_file
SUBTYPE OF (characterized_object, document);

## Slide 50: AP240 SEDS #4
Part and Clause where Issue Originates: AP240
Clause 5.1.7.2.1 full_or_half
Other Parts Affected by the Issue: none
Related Issues: none
Summary/Abstract/Keywords: angular size dimension, dimensinal tolerances
Problem Description:
Ap224v3 changed the mapping (5.1.9.2.1) for the full-or-half attribute to a descriptive-rep-item.description.
AP240 has it like AP224v2, mapped to a representation-item.name.
Is Ap240 going to be made consistant with ap224v3?
Conditions Under Which the Issue Was Discovered: SCRA implementation of AP224e3 and AP240

## Slide 51: AP240 SEDS #4
Proposed Solution (Optional): Make the same as AP224e3
5.1.9.2.1 full_or_half
AIM element: descriptive_representation_item.description
Source: ISO 10303-43
Reference Path: angular_¬size <=
dimensional_size
dimensional_characteristic = dimensional_size
dimensional_characteristic <-
dimensional_characteristic_representation.dimension
dimensional_characteristic_representation
dimensional_characteristic_representation.representation ->
shape_dimension_representation <=
shape_representation <=
representation
representation.items[i] ->
representation_item
descriptive_representation_item
descriptive_representation_item.description
{(descriptive_representation_item.description= 'full angle')
(descriptive_representation_item.description= 'half angle')}

## Slide 52
AP229 - Exchange of Design and Manufacturing Product Information for Forged Parts
Parts and process plans for parts that are made by forging processes;
Design data for forged parts, including geometry, materials, tolerances, required physical and mechanical properties, required tests;
Characterization of products used to make forged parts, including molds, dies, equipment, materials, and consumable items;
Specifications for patterns and die assemblies;
Input to and output from forging process simulation software;
Data exchange between customer and forger, within the forging shop, and between forger and supplier;
Use of data for forging automation and shop floor control;
Use of data for archiving of design and manufacturing data for forged parts.