## Slide 1: Common Requirements for the Representation & Exchange of Piece Part Functional Geometrical & Dimensional Tolerance Definitions
Curtis W. Brown
Honeywell Federal Manufacturing & Technology
Principle Engineer
Kansas City, MO
cbrown@kcp.com
Kim Summerhays
MetroSage
Technical Director
Volcano, CA
kdsummerhays@metrosage.com

## Slide 2: Requirements Summary
Minimum Requirements
  Tolerance Features
  Datum Features & Datum Reference Frames
  Tolerances
    Dimensional
    Geometrical
  Associations
Representation then Presentation
Other Considerations

## Slide 3: Tolerance Features
Planar Face
Cylindrical
Radial Segments (non-size feature, less than 180° of arc length)
  Cylindrical Radial Segment
  Toroidial Radial Segment
  Spherical Radial Segment
Opposite Parallel Planes (e.g., Slots, Tabs)
Profile Groups (faces and/or other tolerance features grouped to accommodate a single profile tolerance)
Runout Groups (faces and/or other tolerance features grouped to accommodate a single runout tolerance)
Compound (to support compound datums)
  Planar Compound (two or more co-planar tolerance features)
  Axial Compound (two or more co-axial tolerance features)
“Tolerance features" may include one or many faces or other tolerance features; Tolerance features are not, in general, the same thing as design or manufacturing features, though there are significant overlaps.

## Slide 4: Datum Reference Frame
Datum Features
  Ability to designate a tolerance feature (single or compound) as a datum feature.
  Label as a functional datum.
Datum Reference Frames
  A precedence ordered set of datum features that define a datum reference frame.
  Material Condition Modifiers are appropriately applied to datum features within the datum reference frame.
  Rules determines a part coordinate system.

## Slide 5: Tolerances
Dimensional
  Adjoining Radial (arc is tangent with adjacent faces, resulting in a crescent moon tolerance zone shape)
  Directed Linear (linear referenced from an origin)
  Non-directed Linear
  Size (e.g., diameter, width)

## Slide 6: Tolerances
Geometrical
  Flatness
  Perpendicular
  Position
  Total Runout
  Surface Profile
Surface Finish
Thread Specification

## Slide 7: Tolerance Associations
Where appropriate, associate Tolerance with their relevant reference tolerance features or datum reference frames.
Assign Tolerances to one or many Tolerance Features

## Slide 8: Representation then Presentation
The appropriate GD&T annotation should be derived from the tolerance representation, verified, and then correctly presented to the user.
One should perform product data exchange from the representation (meaning), not the presentation.
FBTol (Feature-Based Tolerancing) is an example of a technology that augments a solid modeler with complete and unambiguous representation of a product’s tolerance definition.

## Slide 9: Other Considerations
Tolerance Features
  Complex Surface (e.g., bsplines)
  Conical
  Conical Radial Segment
  Revolute Surface
  Spherical
  Threaded

## Slide 10: Other Considerations
Tolerance
  Circularity
  Conical Size
  Coordinate Tolerancing (linear tolerance w.r.t. datum reference frame)
  Cylindtricity
  Non-Directed Angle
  Parallelism