## Slide 1: Status of ISO 14649 Part 110 : Machine tools for STEP-NC
2006. 10.
Suk-Hwan Suh
Center for Ubiquitous Manufacturing
POSTECH, Korea
shs@postech.ac.kr

## Slide 2: Specification of Part 110
ARM: Requirement or Functional Model like Part 111 & 121 compared with catalogue model ISO 13399
  ASME B5.59-2 is a kind of the catalogue model for machine tools
  ISO 14649 Part 110 is a kind of the requirement model for machine tools
Necessities addressed and unanimously agreed in ISO TC184/SC1 Beijing Meeting, October 2005
Related with Machine Tool (catalogue) data model under development by ISO TC39
Need to be harmonized with ISO TC39
Joint Meeting between ISO TC184/SC1/WG7 and ISO TC39/SC2 held in Busan Korea, May 11, 2006

## Slide 3: Scope of ISO 14649 Part 110 : Machine tools for general process
Compared with product lifecycle data model for machine tools
  Part 110 as “Small” data model compared with “Large” data model (product lifecycle data model for machine tools)
Scope & main usage
  General and functional requirement data model for machine tools to execute a STEP-NC part program
  To Specify machine tool type and specification to execute STEP-NC part program, which can be used as a means for selecting actual machine tools to be used for executing the STEP-NC part program in the shop floor
Others usages
  Digital manufacturing (STEP-Manufacturing)
    Process planning / Machine programming
    Virtual machining
    Virtual NC
    Factory flow simulation
    Workspace design
  Performance verification and tracking/process variability/quality control
  Plug-and-play machine installation, self-identification
  Machine intelligence (self-knowledge)
  Interference between components of machine tool
    Interference between chuck and tool holder in milling machining.
    Interference between spindle and turret in turning machining.

## Slide 4: Relationship with product lifecycle data model for machine tools
Covered by ISO 14649 Part 110

## Slide 5: Digital Manufacturing solution (e.g., Delmia)
Product design
Process Planning
Layout Planning
Ergonomics
Time Measurement
Production
Factory Flow Simulation
NC Simulation
Quality Assurance
Robotics & PLC verification
Machine Tools Data Model
Post processing
Virtual CAM
Virtual Inspection
Maintenance (MTTF, Utilization)
Geometry
Kinematics
Performance & Accuracy
Controller

## Slide 6: Virtual Machining
Virtual Machining
  predicts an output of the machining process by simulating the actions of the machine tool in response to the part program and the environment.
Based on data model, new systems such as virtual machining and virtual inspection can be developed.
Virtual Machining
(POSTECH)
Virtual Inspection
(NIST)
Machine Tools Data Model

## Slide 7: Considerations for data model
Functionality
  Data model can represent the functional characteristics of the machine tools
Comprehensiveness
  Data model can represent the general properties of machine tools with regardless of the machine tool type.
Extensibility
  Data model can represent a new type of machine tools without adding or modifying existing data model.
Interoperability
  Data model can be interoperable with existing standards such as STEP, STEP-NC and so on.

## Slide 8: Related International Standards to be referenced for the Machine tools data model
ISO TC39
  The standards for interchangeability between components
    Headstock, spindle, column, base, table, rotary table, etc.
  The standards for testing machine tools
    Test method, Test code, Test condition, etc.
ASME B5 : Catalogue model
  Draft B5.59-1: “Data Specification for Machine Tool Performance Tests”
  Draft B5.59-2: “Data Specification for Properties of Machine Tools for Milling and Turning”
POSTECH model: Functional model for complex machine
  Developed for TurnSTEP, Type 3 STEP-NC system for turning developed by POSTECH
  Mainly for configuration (structure, kinematics) of machine tools

## Slide 9: Overall data model for machine tools
Under development
From
PLCS
To be
developed

## Slide 10
Machine tool data model : Composite Machine Tool

## Slide 11
Machine tool data model : Spindle

## Slide 12
Machine tool data model : Axis

## Slide 13
Machine tool data model : Turret

## Slide 14: Execution plan
Resolution
Call for participation !!!
(joint working group/authorship, etc)