## Slide 1: Forging Product Lifecycle Management
AP229 - Exchange of design and manufacturing product information for forged parts
Dr. Bill Freeman
(843) 760-3791
freeman@scra.org
Mr. Len Slovensky
(513) 383-8311
slovensky@scra.org

## Slide 2: Forging workflow
Design
Analysis
3D Drafting
Manufacturing
AP229 Forging PLM data
Customer
Forging
Requirements
Simulation
Forging &
Tooling
Geometry
Forging
Process
plan
Part Geometry
Part Geometry
Part Geometry
Part Geometry

## Slide 3: Master Model
3D geometry is the Master Model used by forging product data
  To perform a structural Finite Element Analysis for simulation
  To perform a macro process plan for machining
  To create CNC tool paths for part manufacturing
  To perform dimensional inspection
  To create a macro process plan for forging operations
  To create Request for Quote from customer to forging shop
Structuring geometry data as the core keeps all other data in synch.
Allows the part geometry to be the container for adding additional product data requirements

## Slide 4: Forging PLM
Forging
Process
plan
Customer
Forging
Requirement
2D drawings
Simulation
(FEA)
Inspection
(AP219)
Part Geometry
Machining
(AP238)
Macro planning
For machining
(AP240)
3D Part Geometry core to all forging workflow data
Machining
(AP238)

## Slide 5: Part Geometry structure
AP229 contains geometry for
Multiple product data
Required to forge a part
Part Geometry
Design
part
Tooling
Forged
part
Red line

## Slide 6: Part Geometry structure
Designed
part
Forged
part
Tooling
Red line
part
Product data
For finished forged
Part:
Geometry & Topology
GD&T
Machining features
Materials
Properties
Product data
For forging the
Part:
Parting line
Draft
Machine allowance
Flash
Product data
For tooling to
Forge the part:
Impression die
Die material
Die characteristics
Die blocks
Part ejectors
Parting surface
Die draft
Product data
For part proposed
changes. Markup
For change to:
Shape
Properties
Materials
Features

## Slide 7: Part Geometry structure
Designed part
Forged part
Forged part with flash
Red line part
Tooling
Contained in one file

## Slide 8: Part Geometry structure
Designed part
Forged part
Red line part
Forged part
with flash
Tooling
References to files containing
Other Forging data

## Slide 9: Design part structure
Designed part
Geometry
Topology
Features
Dimensional tolerances
Geometric Tolerances
Materials
Properties
Part information
Revision
Security
Approval

## Slide 10: Part Geometry structure
AP229
AP238
AP224
AP240
AP219
Design part data harmonized across
STEP application protocols
Design part data consistent with
Other STEP application protocols
Designed part

## Slide 11: Forged part structure
Intermediate shapes
Draft
Parting surface
Forging plane
Machining allowance
Material elements
Material structure
Forged part
Die tooling required for each forging
operation. Intermediate shapes
Required for each die tool.

## Slide 12: Forged part structure
Intermediate shapes
Draft
Parting surface
Forging plane
Machining allowance
Material elements
Material structure
Forged part features include:
Parting line, flash, draft angles
Forged part

## Slide 13: Forged part structure
Intermediate shapes
Draft
Parting surface
Forging plane
Machining allowance
Material elements
Material structure
When hot impression dies are selected,
Four options are available
(a)
Forged part

## Slide 14: Tooling structure
Intermediate shapes
Draft
Parting surface
Forging plane
Materials
Properties
Standard terminology for various features
of a typical impression-forging die.
Tooling

## Slide 15: Tooling structure
Tooling definitions for different
Forging processes
Tooling
Impression dies
Dies for Cogging
Roll dies
Extrusion dies

## Slide 16: Red line part structure
Recommendations to
Change design of part
For forgability:
Modify shape
Modify tolerance
Recommend a feature be
machined rather than
forged
Red line part

## Slide 17: Customer Forging Requirements
Designed part
Forged part
Forged part with flash
Red line part
Tooling
Customer
Forging
Requirement
Customer Forging Requirements
are defined as properties of
a part. These requirements
are directly attached to the
product data of a part,
regardless of the type:
design, forging, red line, or
tooling.
Customer
Forging
Requirement

## Slide 18: Customer Forging Requirements
Customer
Forging
Requirement
Mechanical stress requirements
chemical analysis certification
  indicates if the chemical composition for the forging is met and certified.
material hardness
  maximum hardness value of the material the customer will accept for the forged part.
mechanical properties certification
  indicates if the mechanical properties for the forging are met and certified.
requirement specification
  document or standard where the specification requirements for the Mechanical property requirements are defined.
tensile strength
  maximum stress in uniaxial tension testing that a material will withstand prior to fracture.
yield strength
  stress at which a material exhibits a specified limiting permanent strain or deformation.

## Slide 19: Customer Forging Requirements
Customer
Forging
Requirement
Mechanical stress
maximum psi design stress
  maximum design loads for mechanical properties for which the forged part is designed.
percent safety factor required
  factor of safety for the application loads for which the forged part is designed.
type of stress
  design mechanical properties with numerical data for which the forged part is designed.

## Slide 20: Customer Forging Requirements
Customer
Forging
Requirement
Corrosion Service
corrosive environment
  atmospheric or ambient condition that has a erosive or acidic reaction to the forged part as designed.
corrosive material
  substance that has a erosive or acidic reaction to the forged part as designed.
ph value
  measure of its acidity or alkalinity with units for which the forged part has been designed.
temperature
  operating temperature with units that causes a corrosive reaction to the forged part as designed.

## Slide 21: Customer Forging Requirements
Customer
Forging
Requirement
Elevated temperature service
maximum cyclic temperature
  highest designed operating temperature with units for periodic application for which the forging part is designed.
maximum temperature
  highest designed operating temperature with units for the in-service application for the forging part.
minimum cyclic temperature
  lowest designed operating temperature with units for periodic application for which the forging part is designed.
service descriptions
  conditions where elevated temperatures problematic to the forging part as designed.

## Slide 22: Customer Forging Requirements
Customer
Forging
Requirement
Machining operations
None
Conventional machining
Nominal Automatic machine tools
Extensive
High energy grinding
Locating points are shown on drawing
Tool path
(AP238)
Machining
(AP240)

## Slide 23: Customer Forging Requirements
Customer
Forging
Requirement
Finishing operations
None
Painting
Filling, rubbing, painting
Plating
Comments

## Slide 24: Forging Process Plan
Forging
Process
plan
Process plan
  Multiple revisions
  Alternate process plan
  Security
    Security code: confidential, secret, unclassified, etc.
  Sequential list of manufacturing processes to be performed
  Process plan special instructions

## Slide 25: Forging Activities
Forging
Process
plan
  Forging operations
  Tooling activity
  Inspection activity
  Simulation activity
  Secondary operations

## Slide 26: Secondary operations
Forging
Process
plan
  Heat treat
  Finishing operation
  Surface finish
  Machining operation

## Slide 27: Forging operations
Forging
Process
plan
  Open die
  Impression die
  Hot upsetting
  Roll forging
  Ring rolling
  Rotary swaging
  Radial forging
  Rotary forging
  Coining
  Powder forging

## Slide 28: Open die Forging
Forging
Process
plan
Cogging

## Slide 29: Impression die Forging
Forging
Process
plan
One impression die may have
multiple impressions to create
several intermediate shapes
Allowable flash amount
Die temperature range (amount
Of pre-heat temperature for the die

## Slide 30: Heading/Upset Forging
Forging
Process
plan
Ideal deformation of a solid cylindrical specimen compressed between flat frictionless dies.

## Slide 31: Roll Forging
Forging
Process
plan
Multiple Roll forging dies are needed to create multiple impressions of several intermediate shapes.
Allowable flash amount
Die temperature range (amount
Of pre-heat temperature for the die

## Slide 32: Ring Roll Forging
Forging
Process
plan
Multiple Roll forging dies are needed to create multiple impressions of several intermediate shapes.
Allowable flash amount
Die temperature range (amount
Of pre-heat temperature for the die

## Slide 33: Rotary Forging
Forging
Process
plan
The die is in contact with only a portion of the workpiece surface.
Used for forming bevel gears, wheels, and bearing rings.

## Slide 34: Rotary swag Forging
Forging
Process
plan

## Slide 35: Extrusion
Forging
Process
plan

## Slide 36: Coining
Forging
Process
plan

## Slide 37: Powder forging
Forging
Process
plan