## Slide 1: Scope
Capture and store common PDM information for STEP Manufacturing AP’s.
Common entities
Common attributes
Rules for usage across the life cycle
Publish as EXPRESS model and XML Schema

## Slide 2: Common Backbone Entities
Product
Product revision/version
Product definition
Owner – contact data
Approval – date and time
Application Protocol
Security status
Data source
Data destination

## Slide 3: Rule of usage #1
Thou shall not trash the previous AP’s data.
  203 geometry shall not be changed by downstream applications
  224 features & GD&T shall not be changed by downstream applications
  Upstream PDM data shall not be changed
AP-203
AP-224
AP-240
AP-238
AP-219

## Slide 4: Rule of Usage #2
An upstream application that changes data shall alert the downstream applications
  Geometry changes
  Feature changes
  PDM changes
An upstream application shall create the new data as a new version

## Slide 5: Rule of Usage #3
A downstream application may request changes to the upstream data by redlining/markup of the upstream data
See rule #1

## Slide 6: Rule of Usage #4
The data path shall be documented

## Slide 7
Product
Pdf 1
Pdf 2
203 PD
224 PD
240 PD
238 PD
219 PD
How to document a red-line version?
How to document path?

## Slide 8
Product
Pdf 1
Pdf 2
203 -> 224
Out PD
203 -> 224
In PD
224 -> 238
Out PD
224 -> 238
In PD
Start PD
Export PD
Import PD
Redline/markup PD
Process Flow PD
End PD
For each PD:
Application context
Owner (required)
Approval (optional)
Date/time (required)
Security (optional)
Software system (required)
Red line (action)
Red line (consequence)
PDR