## Slide 1: Dimensional Tolerances
SEDS issue against AP224 & AP240
Dr. Bill Freeman
(843) 760-3791
freeman@scra.org
Mr. Len Slovensky
(513) 383-8311
slovensky@scra.org

## Slide 2: Tolerances
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
STEP tolerances are based
Off of a 2D application.

## Slide 3: 2D Tolerances
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
This is equivalent to establishing the Origin and
Termination shapes as points
In a 2D environment shapes
Are viewed in flat planar views

## Slide 4: 3D Tolerances
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
If the origin and termination shapes
Are planar and parallel, there is no
Problem.
In a 3D environment shapes
Are viewed in 3D views

## Slide 5: 3D Tolerances problem
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
If the origin shape and termination
shape are not parallel planes
where is the Location tolerance
applied?
Origin shape
Termination shape

## Slide 6: 3D Tolerances solution
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
Add two new attributes
Origin point
And
Termination point
Origin shape
Termination shape
Origin point
Termination
point

## Slide 7: 3D Tolerances problem
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
The origin shape is a plane
The termination shape is
A cylindrical surface that
defines a hole.
Origin shape
Termination
shape

## Slide 8: 3D Tolerances problem
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
if a dimension between a tangent
on the hole and an edge, the
translated shape aspects wouldn't
indicate what is being dimensioned.
Nothing in the output entities indicates
it’s the tangent being looked for.
Which one?

## Slide 9: 3D Tolerances problem
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
By adding the new attributes
Of origin point and termination
point a problem still exist.
Which one to use?
Origin shape
Termination
shape
Origin point
Termination
point

## Slide 10: 3D Tolerances problem
AP224 defines a
Location tolerance
As having a
Origin shape
and a
Termination shape.
To get the correct tolerance
An applied direction would
need to be used.
Origin point
Termination
point
Applied direction

## Slide 11: 3D Tolerances problem
Proposed new
Upward compatible
change

## Slide 12: Funchal solutions
Write informal proposition, that the origin and termination shapes are unambiguous measurable shapes.
Use datums in dimensional tolerancing