## Slide 1: HIgh-level Measurement Process Planning (HIPP): Proposal for Integration into AP238 ed. 2
John Horst
Metrology Interoperability Project Leader,
The National Institute of Standards and Technology (NIST) Gaithersburg, MD
ISO TC184/SC4 meeting
July 2 - 5, 2007 ◊ Ibusuki, Japan

## Slide 2: Summary
History
Options
Measurement Requirements
  IDEF0
Proposal
  AP238 HIPP ARM

## Slide 3: History
Who are we?
  Organizations: DMSC, AIAG MEPT, I++, IA.CMM, STEP (AP219), CMSC

## Slide 4: History
Why am I here?
  NIST 2001: quick specs

## Slide 5
Effective standards

## Slide 6: History
Why am I here?
  NIST 2001: quick specs
  IMIS 2006: Process planning a hot topic

## Slide 7: History
Inspection execution
High-level inspection
process planning
Reporting
& analysis
CMM control commands
and responses
I++ DME
Coordinate measuring machines (CMMs)
Part
design
Measurement
results
DML, I++ DMS,
STEP AP219
Part geometry, manuf info, features,
and
tolerances
AP203e2, AP219, DML, I++DMS
Quality device integration
Quality measurement data
QMD
Planning
Design
Execution
Analysis
High-level inspection
process planning
Low-level inspection
process planning
Meas.process
plans
AP238,
AP219, I++DMS
Meas
process
plans
DMIS

## Slide 8: History
Why am I here?
  NIST 2001: quick specs
  IMIS 2006: Process planning a hot topic
  HIPP 2007:
    Next generation DMIS
    Upstream
    Downstream

## Slide 9: History
Inspection execution
High-level inspection
process planning
Reporting
& analysis
CMM control commands
and responses
I++ DME
Coordinate measuring machines (CMMs)
Part
design
Measurement
results
DML, I++ DMS,
STEP AP219
Part geometry, manuf info, features,
and
tolerances
AP203e2, AP219, DML, I++DMS
Quality device integration
Quality measurement data
QMD
Planning
Design
Execution
Analysis
High-level inspection
process planning
Low-level inspection
process planning
Meas.process
plans
AP238,
AP219, I++DMS
Meas
process
plans
DMIS

## Slide 10: History
What came out of HIPP 2007?
  Several additional meetings
    Discussion of PP boundaries
    Discussion on way forward
    Definition of metrology requirements
      Measurement features
      Other
  Initial AP238 ed. 2 integration

## Slide 11: History
HIPP will be progressed within the DMSC (Dimensional Metrology Standards Consortium) http://www.dmisstandards.org/

## Slide 12: Summary
History
Options
Measurement Requirements
  IDEF0
Proposal
  AP238 HIPP ARM

## Slide 13: Options
Define HIPP requirements for output of HIPP:
  Develop a “local spec” like DMIS; bring as-is to ISO
  Seek integration into ISO14649
  Seek integration into AP219
  Seek integration into STEPNC
  Define AIC for use in multiple STEP APs

## Slide 14: Options
Define HIPP requirements for input to HIPP:
  Develop a “local spec” using DML or I++DMS; bring as-is to ISO
  Create AP219 ed. 2
  Seek integration into AP203 ed. 2

## Slide 15: Summary
History
Options
Measurement Requirements
  IDEF0
Proposal
  AP238 HIPP ARM

## Slide 16: Measurement Requirements
High-level Measurement Process Planning activity model

## Slide 17: Measurement Requirements
Inspection execution
High-level inspection
process planning
Reporting
& analysis
CMM control commands
and responses
I++ DME
Coordinate measuring machines (CMMs)
Part
design
Measurement
results
DML, I++ DMS,
STEP AP219
Part geometry, manuf info, features,
and
tolerances
AP203e2, AP219, DML, I++DMS
Quality device integration
Quality measurement data
QMD
Planning
Design
Execution
Analysis
High-level inspection
process planning
Low-level inspection
process planning
Meas.process
plans
AP238,
AP219, I++DMS
Meas
process
plans
DMIS

## Slide 18: Measurement Requirements
High-level Measurement Process Planning activity model
  Activities with in/out data in IDEF0
  Data and activities defined in separate vocabulary document

## Slide 19: Measurement Requirements
Approach
  Objective HIPP
    Scoped set of measurement features and tolerances
  Executable HIPP
    Scoped list of measurement features and tolerances with other details

## Slide 20
Perform High-level
Measurement Process
Planning (HIPP)
A0
Product Definition
Production Schedule
Batch size
Dimensional Measurement
Resource Database
Measurement Knowledge Base
Fixture Knowledge Base
Standards for Quality
Measurement Criteria
Sampling Statement
Manufacturing Process Plan
GD&T Standards
High-level Measurement Process Plan
Criticality weighting
Quality Plan
Part Characteristics
Measurement Requirements

## Slide 21
Determine Measurement
Scope
A1
Product
Definition
Production
Schedule
Batch size
Dimensional Measurement
Resource Database
Measurement Knowledge
Base
Standard for Quality
Measurement Criteria
Sampling Statement
Manufacturing Process Plan
GD&T Standards
Sup-
port
Data
Determine Dimensional
Measurement Method
(optional)
A2
Develop
High-level Measurement
Operation Plan (optional)
A3
Develop Reaction Plan (optional)
A4
Generate Support Data (optional)
A5
Measurement Scope
Criticality weighting
Reaction Plan
High-Level Measurement
Operation Plan
Quality Plan
Part Characteristics
High-level Process Planning
Measurement Scope
High-level
Measure-ment
Process Plan
Measurement Method Specification

## Slide 22
Identify Measurement
Requirement
A11
Product
Definition
Measurement Knowledge
Base
Measurement
Criteria
Define Accuracy Requirements
A12
Measurement
Requirement
Criticality
Weighting
Accuracy
Requirements
Production
Schedule
Batch size
Determine
Measurement
Tasks
A13
Measurement
Tasks
Determining Measurement Scope
Measurement
Scope
Standard for
Quality
Quality
Plan

## Slide 23
Select Coordinate
Metrology
Method
A21
Product
Definition
Measurement Knowledge Base
Measurement Method Specification
Select
Sensors
A22
Measurement
Scope
Coordinate Metrology
Specification
Sensor Specification
DME Database
+
Select Gage
Method
A23
Gage Specification
Production
Schedule
Batch
size
Part Characteristics
Determining Measurement Method

## Slide 24
Determine
Setup and
Fixturing
A31
Measurement Knowledge Base
Determine High-level Measurement Operations
A34
Fixture Synthesis System
Setups
and
Fixturing
Develop Sampling Plan and Select Evaluation Functions
A33
Measurement
Scope
Measurement Resource Specification
Sampling Plan
High-level Operation
List
Batch Size/
Production
Schedule
High-Level Measurement
Operation Plan
Determine Features to be Measured
A32
Measurement Features
Determining High-Level Measurement Operation Plan

## Slide 25: Summary
History
Options
Measurement Requirements
  IDEF0
Proposal
  AP238 HIPP ARM

## Slide 26: AP238 HIPP ARM
Approach
  Objective HIPP
    Dimensional metrology workingsteps with less detail
  Executable HIPP
    Dimensional metrology workplan with details

## Slide 27: AP238 HIPP ARM
Approach
  On-machine or off-machine measurement uses the same data representation
  Measurement and machining use the same structure and format, allowing easy integration

## Slide 28: Measure Features in AP238 HIPP ARM
Harmonized between DMIS 5.1, AP219, and FBMeas
Model measure features
Insert attributes from AP219 Express or DMIS 5.1
Tolerances are separate entities -> toleranced_length_measure had to go
Some 3D features are unbounded; need means to specify total boundedness
Features only ½ associative with geometry; need to add machining feature geometry associativity
All feature placement is in nominal part coord sys
Nominal versus measured not in model; should it be?
Some feature constraints in text, but should be put into Express ARM as WHERE rules
  Curtis W. Brown
  Principle Engineer
  NNSA’s Kansas City Plant
  Operated by Honeywell FM&T
  P.O. Box 419159
  Kansas City, MO 64141
  816-997-3548
  cbrown@kcp.com

## Slide 29: Measure Feature Taxonomy Harmonized with DMIS 5.1, DML, AP219, FBMeas By Curtis W. Brown . June 15, 2007
DM Measure Feature
  Simple DM Feature
    Point DM Feature
      EdgePt DM Feature
    2D Simple DM Feature
      Bi 2D Simple DM Feature
        Circle Bi 2D Simple DM Feature
        Arc Bi 2D Simple DM Feature
        CParLn Bi 2D Simple DM Feature
        Flat CParLn Bi 2D Simple DM Feature
        Round CParLn Bi 2D Simple DM Feature
        Ellipse Bi 2D Simple DM Feature
      GCurve 2D Simple DM Feature
      Line 2D Simple DM Feature
        Bnd Line 2D Simple DM Feature
        UnBnd Line 2D Simple DM Feature

## Slide 30
  3D Simple DM Feature
    Bi 3D Simple DM Feature
      Cuboid Bi 3D Simple DM Feature
    FOS Bi 3D Simple DM Feature
      Conical FOS Bi 3D Simple DM Feature
      Cylindrical FOS Bi 3D Simple DM Feature
      Spherical FOS Bi 3D Simple DM Feature
      SymSurf FOS Bi 3D Simple DM Feature
        ElongCyl FOS Bi 3D Simple DM Feature
        SymPln FOS Bi 3D Simple DM Feature
        ParPln FOS Bi 3D Simple DM Feature
      Toroidal FOS Bi 3D Simple DM Feature
    RadSegmnt Bi 3D Simple DM Feature
      Conical RadSegmnt Bi 3D Simple DM Feature
      Cylindrical RadSegmnt Bi 3D Simple DM Feature
      Spherical RadSegmnt Bi 3D Simple DM Feature
      Toroidal RadSegmnt Bi 3D Simple DM Feature
    RevSurf Bi 3D Simple DM Feature
    Planar 3D Simple DM Feature
  GSurf 3D Simple DM Feature

## Slide 31
  Composite DM Feature
    Compound Composite DM Feature
      Axial Compound Composite DM Feature
      Planar Compound Composite DM Feature
      Spherical Compound Composite DM Feature
    Simple Pattern Composite DM Feature
      Axial Pattern Composite DM Feature
        Parallel Axial Pattern Composite DM Feature
        Radial Axial Pattern Composite DM Feature
      Spherical Pattern Composite DM Feature
      SymSurf Pattern Composite DM Feature

## Slide 32: FBMeas Measure Feature Taxonomy
DME
Measure
Feature
Simple
FOS
Composite
2D
GSurf
Point
Cuboid
Spherical
Cylindrical
Conical
RevSurf
Line
Toroidal
RadSegmnt
Spherical
Cylindrical
Conical
Toroidal
Compound
Planar
Axial
SymSurf
SymPln
ElongCyl
ParPln
Pattern
ParPln
Spherical
3D
Spherical
Circle
GCurve
Arc
Flat
CParLn
Round
Ellipse
EdgePt
UnBnd
Bnd
Bi
Bi
Planar
Parallel
Axial
Radial

## Slide 33: Measure Definition Model Object Design
Part
Coordinate
Systems
Machine
Resources
Measure
Feature
Measure
Definition
1
Measure
Definition
0..n
PCSs
Measure
Definition
1
0..n
Measure
Features
Sensor
Resources
0..n
Measure
Definition
1
Sensors
0..n
Measure
Definition
1
Machines
Datum
Reference
Frame
Tolerance
Feature
Tolerance
Definition
1
Tolerance
Definition
0..n
DRF
Tolerance
Definition
1
0..n
Tolerance
Features
Tolerance
0..n
Tolerance
Definition
1
Tolerances
Tolerance
Feature
0..1
Tolerance
Definition
1
DRF
0..1

## Slide 34: Measure Definition Model Object Design
Toleranceable
Aspects
Tolerance
Datum
Reference
Frame
Datum
Measure
Feature
may reference
is referenced by
1..n
0..1
may have a secondary
may have a tertiary
has a primary
0..1
1
0..1
is used has datum feature
1..n
is implemented by
satisfies a feature’s
1..n
1
is constrained by
constrains
n
2..5
1..n
1..n
may be designated as
is a
1
Shape
Aspect
Topological
Entity (e.g., face)

## Slide 35: AP238 HIPP ARM
Pre-existing probing entities
  Those with defects were removed
  workpiece_complete_probing entity seemingly not usable; due to
      weaknesses and incompleteness on operation description
      incompleteness of alignment options
      measured_offset value meaningless
      cannot assign surfaces for datum definition
      Attributes such as search and retract distances not provided
  workpiece_complete_probing entity could be replaced by variant of DMIS DATSET
  touch_probing entity seemingly unusable, since it is a subtype of both workingstep and operation; not consistent with machining equivalent

## Slide 36: AP238 HIPP ARM
Physical resources
  Needs more complete and precise (useful) definition of classes of resource…classes of measurement devices and classes of sensors
Not in ARM, but specified in IDEF0
  Criticality weighting of features
  Reaction plan

## Slide 37
John Horst, NIST
john.horst@nist.gov * 301.975.3430
Gaithersburg, MD