## Slide 1: Open seminar “Planning, Machining and Measurement using STEP and STEP-NC” 52nd ISO TC184/SC4 Meeting July 1 – 6, 2007 Ibusuki, Japan Towards the Realization of Conformance Class 4 on STEP-NC
Takeshi KISHINAMI
President
Kushiro National College of Technology
Kushiro city, Hokkaido, Japan
kisinami@office.kushiro-ct.ac.jp

## Slide 2: Partners of Japanese STEP-NC Project
Takeshi KISHINAMI(Kushiro Techinical College,Japan)
Fumiki TANAKA(Hokkaidio University)
Chiaki SAKAMOTO(MER,Japan)
Takashi INOUYE(Fujitsu, Japan)
Tohru MIZUNO(FANUC,Japan)
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 3: Contents
Current Situation of STEP-NC
Hurdle of STEP-NC Deployment
Advantages of STEP-NC
Requirements of STEP-NC realization
  Feature Dependency
  Capturing Technical Information from Legacy data(ISO 6983)
Prototype
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 4: Related standards
STEP-NC standard
  ISO 14649
  STEP AP238
ISO 6983
  A list of M and G code to control the machine motion and various function
STEP AP224
  Machining Features
STEP AP219
  Measuring
STEP AP240
  Process Planning
STEP-NC is able to replace the ISO 6983 as primary interface between CAM and CNC
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 5
AIM
ARM
Since inplementation of the CNC model based on ISO14649 is easy, we indicate the practicality to 5-axis machining of machining feature using its CNC model.
We will use STEP AP238, if practicality is checked in future work.
STEP AP238 (ISO 14649) is a new standard for transferring data between CAD/CAM systems and CNC machines.
ISO 14649 is ARM version on STEP and STEP AP238 is AIM version of ISO14649. Therefore, STEP AP238 and ISO14649 is equivalent semantically.
STEP AP238 and ISO14649
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 6: STEP-NC standard is
STEP-NC is an extension of STEP that enhances the design information with manufacturing information, including information about the workpiece material, its manufacturing features, tolerances, tool requirements, process sequence, speeds, feeds and other process parameters.
STEP-NC defines data in workingstep – a group of specific operations to be performed on a CNC machine tool. It breaks down every machining operation into the steps required to perform the operation.
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 7
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterized_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen
STEP-NC data model(ISO14649)

## Slide 8: Original Concept of STEP-NC standard
The original concept of STEP-NC envisioned capturing all the data and process information required to create a part, and the STEP-NC-enabled CNC was expected to generate the toolpath.
STEP-NC file was transferable between various machine tools because each machine tool was responsible for generating it own toolpath, given the information contained in the STEP-NC file.
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 9: Conformance classes of STEP-NC standard
The conformance classes :
  CC1 : explicit toolpath geometry,
  CC2 : part geometry,
  CC3 : feature and operation data,
  CC4 : design specification data(dimension and tolerances)
  are introduced for step by step development.
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 10: Current Situation of STEP-NC standard
The lowest-level conformance class, CC1, literally is an ISO standard representation of explicit toolpath with some structure that directly replaces standard M and G code.
CC2 file provides a more complete representation of the machining process. It is also easy to take advantage of the second conformance class, CC2, because all the end-user needs to do is merge the CAD models of the part and the workpiece and the fixtures with the toolpaths to create a more complete description of manufacturing process.
The function of generative toolpath is relegated to the highest conformance class, CC4.
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 11: Industries situation
STEP-NC’s adoption by the industry really depends on how the end users, CNC machine tool vendors, and CAD and CAM vendors respond to it.
Most of customers are still in the process of adopting other STEP application protocols, such as AP203 and AP214. For them, AP238 is not even on their radar. End users already have systems in place that work well enough for them. They are not willing to put their conventional production at risk.
From Cutting Tool Engineering Magazine/April 2006/Vol58/No.4
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 12: CNC Vendors & CAM Vendors
The CNC vendors are saying, ‘We can not get any STEP-NC data, so why should we implement it?’ and
The CAM vendors are saying, ‘Well even if we implement it, who is going to use it?’
From Cutting Tool Engineering Magazine/April 2006/Vol58/No.4
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 13: Hurdle of STEP-NC Adoption(1)
Part of the problem with getting CNC venders on board is that they rely on being able to differentiate their products from other vendor’s products.
There is specialization that each control vendor introduces into M and G code to allow them to differentiate themselves from other vendors.
These vendors see STEP-NC as something that homogenizes the marketplace, which means that anything they might use to differentiate their products essentially gets boiled away.
From Cutting Tool Engineering Magazine/April 2006/Vol58/No.4
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 14: Hurdle of STEP-NC Adoption(2)
They have to buy one of every CAD/CAM system in order to service all of their customers. It is expensive for them. While they might not realize it, STEP-NC can be in the CNC vendors’ best interest.
If they have a unique feature in their CNC, the only way their customers are going to be able to use it is if they invest the time and effort.
If a vendor introduces a new feature for their controller, it is going to have some new G code for it. So in order for customers to use this new feature, they have to buy a new postprocessor.
Since that is an expensive proposition, they probably are not going to use that feature.
There is a balance between tying customers to a CNC vendor’s proprietary language and making it riskier for them to use new features.
From Cutting Tool Engineering Magazine/April 2006/Vol58/No.4
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 15: Hurdle of STEP-NC Adoption(3)
CAM systems also need to be re-engineered to support STEP-NC. Part of this depends on the quality of information provided to CAM systems from CAD systems.
This is another hurdle that needs to be overcome. CAD systems need to provide a product data model with geometry, surface-finish and tolerance specifications.
CAD vendors are beginning to evolve their geometric modeling systems, but the evolution is not complete.
From Cutting Tool Engineering Magazine/April 2006/Vol58/No.4
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 16: Advantages of STEP-NC
Easy to maintain the traceability
Easy to modify.
Easy to reuse.
Decrease the human error.
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 17
Advantages of STEP-NC/CC4
ISO6983
NCdata
Drawing
Technical Information is scattered
ISO6983 NC machine tool
Technical Information has recorded isolately each other.
・ Difficult to traceability.
・ Difficult to modify.
・ Difficult to reuse.
・ Cause of the human error.
Tool Info.
Material Info.
Process
Chart
Machine
ISO14649
NCdata
Technical Information is
Integrated into one data.
ISO14649 NC machine tool
Advantages:
・ Easy to traceability
・ Easy to modify.
・ Easy to reuse.
・ Decrease the human error.
・Machining Feature
・Machining strategy
・Approach and retract motion
・Tool information
・Material Information
・Machine Information
Integration of
Technical
Information
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 18
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterized_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen
Requirements for STEP-NC data model
Feature Dependecy and Unified shape
More Complicated Operational Model
Capture Technical Information from Legacy Data
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 19
Feature Dependency
for Process Planning
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 20
What is the Manufacturing Feature ?
AP224 Manufacturing Feature is
still in the world of Geometry
Unification of Manufacturing Feature is
needed from the view point of machining
Feature Dependency among explicit and/or
implicit feature should be introduced
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 21
Unification and Dependency between Features
Create Feature dependency and Unification
Manufacturing Context
Features
Unification and
Feature Dependency
Manufacturing
Geometry
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 22
“Explicit Feature” and its dependency
Feature-6
Feature-5
Feature-4
Feature-3
Feature-2
Feature-1
Compound_feature-2
Compound_feature-1
Base Plane-1
Feature-1
Compound_feature-1
Feature-6
Base Plane-2
Feature Pool
Feature Dependency
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 23
Slot  Pocket 1,2
Pocket 1,2  Slot
“Dynamic Feature”
Unification of Features and
Division of Features
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 24
Base Plane-1
Pocket-1+2
Pocket-1
Base Plane-2
Base Plane-1
Pocket-1
Pocket-2
Base Plane-2
Pocket-2
“Dynamic Feature” and its dependency
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 25
“Implicit Feature”
Thread
Surface finish
Removal thickness
Finishing allowance
Hole top/end finishing
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 26
Thread
Surface finish
Removal thickness
Finishing allowance
Hole top/end finish
AP203/214 AP224
Non-support
Explicit Rep.
Explicit Rep.
“Implicit Feature”
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars
Non-support
Non-support
Non-support
Non-support
Semi-support
support
support

## Slide 27
“Implicit Feature” and “Explicit Feature”
(AE)
Explicit_ feature
(AE)
Implicit_ feature
explicit_feature S[0:?]
(INV) dependency
Thread
Finishing
Removal_ from_raw_stock
1
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 28
Implicit Feature and its dependency
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 29
“Implicit Feature” and its dependency
Base Plane-1
Pocket-1
Hole-1
Base Plane-2
thread-1
thread-2
finishing-1
Removal_thickness-1
Hole-2
finishing-2
dependency
Feature Dependency Tree
Implicit Feature
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 30
More Complicated operational
Model for Process Planning
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 31
course_of_travel
swept_shape
More Complicated Operational Model
Next-generation CNC language
Contains rich information enabling feature-based. programming
■ Data Model Structure of ISO 14649 ■
Entity A
Supertype Entity
Subtype Entity
Entity B
Attribute
■ Diagram Notation ■
Machining_workingstep
(ABS)
Machining_operation
its_operation
(ABS)
Milling_machining_operation
(ABS)
Approach_retract_strategy
retract
(ABS)
Milling_type_operation
approach
1
Approach-Retract strategy
(ABS)
Machining_tool
(ABS)
Two5D_milling_strategy
(ABS)
Two5D_milling_operation
Machining strategy
Tool Information
Endmill
its_tool
1
1
(ABS)
Machining_feature
(ABS)
Manufacturing_feature
(ABS)
Two5D_manufacturing_feature
1
Machining feature
Slot
its_machining_strategy
its_feature
its_operations S[0:?]
(ABS)
Workingstep
Example of
Slot Machining
Center_milling
AP_retract_angle
Plunge_toolaxis
Slot
(ABS)
Open_profile
(ABS)
Travel_path
Linear_path
Square_U
_profile
1
1
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 32
5-axis machining CNC data can be described by adding the orientation data of a tool to 2.5D machining data .
But, there is only limited research and development about 5-axis machining.
Enhanced Machining Operation
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 33
Generate Technical Information
from Legacy Data
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 34
Analyze based on ISO 14649
(STEP-NC)
Technical
Information
DATA
Generation of Technical Information for STEP-NC
ISO 6983
NC data
DATA
ISO 6983
Machine Tool
Current Process
ISO6983 CAM
Machining Feature
Machining Strategy
Workpiece
Machining Tool
Relationship between Workingsteps
…
ISO14649 CAM
ISO 14649
NC data
DATA
ISO 14649
Machine Tool
Future Process
CAD
Skilled Worker’s Knowledge
Database
Retain to
Database
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 35
Generation of Technical Information
Input data
Workpiece
blank model
ISO6983
NC data
1.Cutter motion
2.Cutting condition (coolant etc.)
ISO6983
NC data
N11 G1 Z20. F7.
N12 X35. F800.
N13 Z30. F7.
N14 G0 Z50.
N15 M5
N16 T5 M6
information
Tool
Technical Information
Analyze
ISO14649
CNC Data Model
Technical Information
ISO 14649 contains …
Machining feature
Machining strategy
Approach-Retaract strategy
Tool information
ISO 14649 does not contain …
Relationship between workingsteps
Output data
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 36
…
T01
M06
G91G28Z0
…
Generation of Workingstep including Technical Information
Split NC data into tool path elements for a cutting tool
A1
Generate Machining strategy and Approach-Retract strategy A3
Generate Machining feature
A2
ISO6983
NC data
Workpiece blank model
Generate
Workingstep
A4
ISO14649
Workingstep
Machining strategy &
Approach-Retract strategy
Tool information
ISO14649
Machining
feature
Slot
Bounded
tool path
Approach path
&
Retract path
ISO14649 schema
XY_planar_ curve_path
Center_milling
Plunge_toolaxis
AP_retract_angle
Slot machining
Generation rule for Bounded tool path
Generation rule of Machining feature
Generation rule of Machining strategy and Approach-Retract
strategy
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 37
Generation of Machining feature from ISO6983
Generation rule of MF
Tool information
Generation rule of
Working tool(Path-Profile)
Generation rule of
Removal volume(Path-Profile)
Generation rule of Machining feature
Workpiece
blank model
Bounded tool path
Generate
Working tool
A21
Bounded
tool path
ISO14649
Machining feature
Path
Profile
Machining_
feature
path
profile
Bounded_
tool_path
Tool
information
Endmill
Profile
path
Slot
Generate
Removal volume
A22
Generate
Machining feature
A23
Removal_volume_
boundary_element
Removal_volume
boundary_element
Bounded_
tool_path
Bounded_
sweep_profile
Removal
_volume
profile
sweep
_path
boundaries
L[0:?]
Removal volume
（Path-Profile）
Removal volume（Path-Profile）
Removal volume
XY_planar_
curve_path
ZERO_parameter_
sweep _path
Working tool
（Path-Profile）
Bounded_
tool_path
Bounded_
sweep_profile
Working
_tool
profile
sweep
_path
Working tool
Working tool（Path-Profile）
Z_straight_line_profile
Circular_disk_profile
Surface_of_Rev._profile
Mapping
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 38
Generate
Workingstep
A4
Needs for definition of relationships between Workingsteps
ISO14649
Workingstep
ISO14649 schema
Associate with
Workingsteps
A5
Machining information
Machiningfeature
Machining strategy &
Approach-Retract strategy
Tool information
Bounded tool path
Machining_workingstep
(ABS)
Machining_operation
its_operation
1
(ABS)
Two5D_milling_operation
(ABS)
Workingstep
Bottom_and_side_
rough_milling
Bottom_and_side_
finish_milling
1
(ABS)
Plane_millimg
(ABS)
Side_millimg
(ABS)
Bottom_and_side_millimg
1
1
Roughing operation
Finishing operation
Not for describing relationship between workingsteps
More information is required to use as the database.
■ Data structure of Workingstep ■
Generation rule for relationship between Workingsteps
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 39
Results
ISO6983-NC data
N100 G21
N102 G0 G17 G90
N104 T1 M6
N106 G0 G90 X-20.
Y50. S5000 M3
N108 Z50.
N110 Z45.
N112 G1 Z20. F7.
…
ISO6983 NC data for Slot, Round hole, Closed pocket generated by MasterCAM
ISO14649 Workingstep
<?xml version="1.0" encoding="utf-8"?>
<iso_10303_28 version="2.0">
:
<ms:Machining_workingstep id="id462"> …
</ms:Machining_workingstep>
<ms:Slot id="id302">..</ms:Slot>
:
<ms:Milling_cutting_tool id="id443">
<ms:Its_id>Flat Endmill D:20</ms:Its_id>
</ms:Milling_cutting_tool>
<ms:Center_milling id="id438">
</ms:Center_milling>
<ms:Ap_retract_angle id="id448"/>
<ms:Plunge_toolaxis id="id449"/>
:
:
<ms:Machining_workingstep id="id463"> …
<ms:Closed_pocket id="id303">..</ms:Closed_pocket>
:
<ms:Machining_workingstep id="id464"> …
<ms:Round_hole id="id304">..</ms: Round_hole>
:
</iso_10303_28>
Slot
Closed pocket
Round hole
Slot
Closed pocket
Round hole
Machining strategy
Tool information
Machining feature
Approach-Retract strategy
Analysis program written in EXPRESS-X is executed on Express Data Manager
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 40
Summary
Technical information is able to be extracted from the ISO6483/NC program, and transformed into workingstep of STEP-NC/CC4 (ISO 14649).
The method of extracting the machining feature and the process information from an NC program is proposed.
An analysis system for ISO 6983 NC data based on ISO 14649 is implemented using EXPRESS-X.
ISO 6983 NC data generated by CAM software are applied to the implemented test system, and valid ISO 14649 NC data are obtained.
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 41
Prototype of STEP-NC 5-Axis
Machine Tool
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 42
The structure of this machine tool combines a tool and table tilt to 3-axis.
X
Y
Z
C(Table Tilt )
A(Tool Tilt )
Axis
motion range
maximum speed
X
1000 mm
1000 mm/sec
Y
1000 mm
1000 mm/sec
Z
250 mm
1000 mm/sec
A
±90 degree
150 rpm
B
360 degree
50 rpm
Specification
Configuration of 5-axis machine tool
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 43
Machine tool Kinematics model
base_to_tool_mechanism
mechanism
kinematic_structure
kinematic_joint
kinematic_pair
end_link
prismatic_pair
revolute_pair
su_parameters
kinematic_link
base_to_workpiece_mechanism
su_parameters
A loop structure
Kinematic structure from base to tool
Placement between pairs
Placement of end-effector
・・・
・・・
base
SU
parameter
Kinematic Model structure
kinematic_link_ representation_relation
kinematic_link_ representation
Connect to shape_rep
ISO10303-105
Kinematic structure from base to work
Proposed
shape_represntation
kinematic_link_representation_association
Proposed
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 44
To verify the CNC data model, the machining data of a hemisphere was created by Express Data Manager, and the hemisphere was machined with this 5-axis machine tool.
5-axis machine tool
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 45
#1= PROJECT('Hello world!',#2,$,$,$,$);
#2= WORKPLAN($,(#3),$,$,$);
#3= MACHINING_WORKINGSTEP($,$,$,#5,$);
#5= FREEFORM_OPERATION(#6,$,$,$,$,$,$,$,$,$,$,$);
#6= TOOLPATH_LIST((#7));
#7= CUTTER_LOCATION_TRAJECTORY($,$,$,$,$,$,#11,#3770,$);
#11= POLYLINE($,(#13,#15,#17,#19,#21,#23,#25,#27,………………
#13= CARTESIAN_POINT($,(0.,0.,5.));
#15= CARTESIAN_POINT($,(0.,45.,5.));
………
#39= CARTESIAN_POINT($,(0.,44.8903823312964,-41.8609596769032));
#41= CARTESIAN_POINT($,(0.,44.5620632257812,-38.7372113989472));
………
#3770= POLYLINE($,(#3772,#3774,#3776,#3778,…………
#3772= CARTESIAN_POINT($,(0.,0.,1.));
#3774= CARTESIAN_POINT($,(0.,0.,1.));
#3776= CARTESIAN_POINT($,(0.,-0.156434467332172,0.98768834023213));
This shows the processing of the CNC-model data of a hemisphere that has a diameter of 80 mm.
A hemisphere was created by machining a free-form surface, and Cutter_Location_trajectory described the instance of a tool path.
The center position and ordinate of the tool were specified by Polyline, and Cartesian_point described each point.
Description of CNC model data using STEP part 21
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 46
The 5-axis CNC machine tool input previous data and machined urethane foam using a ball end mill with radius of 3 mm.The cutting conditions were a feed rate of 500 mm/min and a spindle speed of 25,000 rpm.The practicality of the CNC data model was thus able to be shown.
Machining using CNC model data
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 47: Benefits of STEP-NC Adoption
STEP-NC essentially eliminates the need to have a unique postprocessor for each machine tool configuration.
STEP-NC make it possible to be the portability
STEP-NC make it possible to be a traceable machining system.
STEP-NC will have micro process plan information (Feature Dependency) in conjunction with workingstep.
The purpose of STEP-NC is to displace all of these various postprocessors with one format, the STEP-NC format.
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars

## Slide 48: Thank you for your attention
We continue to develop a High level STEP-NC/CNC Machining System.
Every year, Sapporo Workshop of manufacturing group was held for discussing some New Manufacturing Data Model and Related Standards.

## Slide 49
A machining feature-driven 5-axis CNC machine tool that is based on ISO 14649, verified the usefulness of the CNC data model for 5-axis processing and can be summarized as follows:
(1) A 5-axis CNC machine tool that directly inputs 5-axis machining data based on ISO 14649 and that can machine parts was manufactured. Then, it was verified that the CNC data model could fully equal that of existing 5-axis machining.
(2) Since the CNC-model data was information about a tool tip course, it could be used regardless of the structure of a machine. The advantage of the CNC data model in providing compatibility of data has thus been verified.
(3) By describing the CNC-model data using XML, data exchange was possible and Web representation was made easier.
(4) The 5-axis CNC machine tool constructed the functions of the tool-path generation and interpolation, so that the 5-axis machining could be independent of CAM system.
Summary
ISO/TC184/SC4/Ibusuki Meeting July/1-6/2007 Open Seminars