## Slide 1: AP-238 Plate Cutting and Marking
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
NSRP Panel Project

## Slide 2: STEP-NC Panel Project
Demonstrate STEP-NC for cutting and marking from actual shipbuilding data sources
  AP203 geometry for plate shape
  CATIA APT to describe the marking and cutting process
  Include straight and bevel cuts, line and text marking
Prototype tools to drive ESAB plasma cutter and laser marking machines from AP238 data
Cut actual plate at EB Quonset Point facility

## Slide 3: Original CATIA Data
T999-0001S1 3D MODEL with footprints on
T9990002-STEP2
T9990002-STEP1

## Slide 4: Cutting and Marking APT
T9990002-STEP2 with far side footprints visible

## Slide 5: Construct AP238 Data
Process APT data to produce AP238 process
  Used tools already developed for milling and turning information
  Created AP238 “extended nc function” instances for extra plate cutting APT data like head on/off, bevel angle, marking line width
  Eventually extend AP238 to hold these in the operation technology descriptions
  Use results of NGIT project
Add STEP geometry to the process to see in context of workpiece
  Matching location required moving geometry 100 yards!

## Slide 6: AP238 Data for Plate Cutting and Beveling

## Slide 7: Add Manufacturing Preparation Data
As designed, cuts start right on edges
  For plasma cutting, lead ins and lead outs are required to avoid gouging the part
  Also important for bevels to give cutting head time to traverse into position after piercing
Created utilities to add lead ins and lead outs to the STEP-NC data
  Today, these are added by nesting systems like Optimation, Majestic, Sigmanest, etc.
  These systems can read and write STEP-NC in the future.

## Slide 8: STEP-NC Manufacturing Prep.
Tangential Entry/Exit

## Slide 9: STEP-NC Manufacturing Prep.
Bevel Entry

## Slide 10: Drive Plasma Cutter / Laser Marker
Extend existing AP238 CNC interface to export codes for ESAB controls
  Many unique codes, machine peculiarities, close contact with EB personnel required to understand them
  Local conventions for setup and registration of the plate, coordinate system transformations for near/far, etc.
Single STEP-NC program for entire plate
  Need to split into separate programs to cover near-side marking, far-side marking and cutting
STEP-NC Plate
Program
ESAB Near Mark
ESAB Far Mark
ESAB Plasma Cut

## Slide 11: Unique Codes and Peculiarities
Some APT and ESAB codes are rather obscure
Example, marking the text “-STEP11”
  In APT: MARK/ 45, 83, 84, 69, 80, 49, 49, 0, 0
    Represented as numbers corresponding to ASCII
  In ESAB Codes:
    F100.0
    G89D003
    G81D0.375
    G82D271.1
    G80
    (-STEP11)
    D004
    M75
In addition, there are machine peculiarities like ordering of codes, decimal points, etc.

## Slide 12: Quonset Demonstration
May 9, 2007, Marked and cut the test part at EB Quonset Point facility
  Marking and cutting successful. Minor issue discovered with ordering of an ESAB marking code, corrected on site.
  Simulator no substitute for the real thing!

## Slide 13: Current vs STEP-NC Process
APT
Drawings
Nesting
G-Code Near,
Far Marking,
Cutting
Catia
STEP-NC
Nesting
STEP-NC
CNC
Potential for other value adds
Catia
Current Process:
STEP-NC Process:

## Slide 14: Future Work
Integrate Cutting and Marking Parameters into STEP-NC ARM
  Extend technology descriptions for cutting and marking parameters
  Use results of Northrop Grumman study
Test process improvement opportunities
  Beveling for small and/or detailed edges
  Edge quality control (e.g bounce prevention)
  Combine cutting and milling for bevels
Demonstrate at second site
  Validate ARM
  Ensure portability