## Slide 1: First Conference Call Wednesday November 7th 10:30AM Eastern, 4:30PM France
Report on results of the Dallas meeting
Discuss goals for next meeting
Interface with HiPP team
Distribution policy for the STEP-NC Explorer and DLL
Location for next meeting
Potential Participants

## Slide 2: Goals for next meeting
Feed and Speed optimization
  Show the procedure
  Compute feeds and speeds for maximum throughput
Traceability demonstration
  Operation time
  Maximum path deviation
Determine how to inspect the fish head to improve the machining accuracy for the subsequent meeting/demonstration

## Slide 3: Feed Speed Optimization
Vericut
Boeing
code
CVS
File
STEP
Merge
process
Fishead
AP-238
Enhanced
Fishead
AP-238
STEP CNC
Converter
Boeing
Optimization
Algorithms
Optimized
Machine
Program
G-code
& STL/STEP models
STEP CNC
Converter
Today’s machining conditions
Interface
1
2
3
4

## Slide 4: Tool path attributes for Speed and feed optimization
Average Depth (d)
Average Width (w)
Cross sectional area (sometimes = d * w)
Center of the area (Y, Z) (standard must describe origin – tip of tool)
Maximum depth
Maximum width
Toleranced spindle power profile
Key
In standard
Speed/Feed extension
Adaptive control extension
See Cross-Sections.ppt

## Slide 5: Tool path attributes for Sensor adaptive control
Tolerance force vector as bounded curve
Tolerance power scalar as bounded curve
Temperature scalar as bound curve – standard must define measurement point
Acoustic emission???
Vibration???

## Slide 6: Traceability and Measurement
Test the Traceability model for AP-238 e2
  Get time function for workingstep execution time
  Maximum path deviation function for machining lag/error
Analyze results to determine correlations between deviation error and machining error
  Correspondence indicates tool bending and feed/speed/power error?
  No correspondence indicates tool path error?
Determine how to correct error in next round using five axis cutter compensation

## Slide 7: Traceability
get_time
get_time
Path max deviation on
Path max deviation off
STEP Tools to make the data and convert to Siemens 840D codes
NIST to machine the part
University of Vigo in Spain to analyze the log file

## Slide 8: Interface with HiPP team
Try to obtain “real” AP-203 e2 file to define the tolerances
Determine measurement goals for next round (March)
Plan for closed loop machining in subsequent round (June)

## Slide 9: STEP-NC Explorer and DLL New Distribution Policy
Available on request to anyone that wants to test STEP-NC AP-238.
For evaluation and research use only
  No production usage
  No work-for-hire usage
Download from ftp site
  Must contact us to get a key

## Slide 10: Location for next meeting
Meeting should be in March about the time of the next SC4 meeting
Suggested locations
  NIST
  Sandvik
  OMAC meeting in Orlando?
  SC4 meeting in Louisville
  Other?

## Slide 11: Participants in Next Round
Continuing participants
  Sandvik
  NIST
  Boeing
  University of Auckland, New Zealand
New participants
  KTH, Sweden
  CCAT, Connecticut
  University of Harbin, China
  Others?