## Slide 1: Current Status of Dallas Demonstration Preparation
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
October 17, 2007

## Slide 2: Status
Sandvik data has been roughed
  The roughing takes 12 minutes
The following changes were made to the data
  APT parser was changed so that each tool change makes a new workingstep even if the tool change is redundant
  APT parser was changed to add approach and retract operations for UGS UDE operation
    “$$UDE: <> MOVE BACK <>/TYPE=MAX”
The following changes have been made to the converter
  Manual DMIS mode has been updated to include the measurement operations shown in FishheadToleranceSuggestionsIssueC.ppt

## Slide 3: Data
Dallas_sandvik2.238
  Is the latest AP-238 data (compressed XML)
Dallas_sandvik2_roughing.fanuc
  Is the Fanuc file used for the 3-axis roughing.
Dallas_sandvik2_finishing.i
  Is the Heidenhain AC file used for the 5-axis finishing
Dallas_sandvik2_inspection.dmi
  Is the Manual Mode DMIS data the inspection

## Slide 4: Open issues
Inspection issues
  Are we required to probe exactly the points given in FishheadToleranceSuggestionsIssueC.ppt
    Points used in current inspection plan were generated by software
    Only number of points was checked
  The inspection operations are normal to the faces to eliminate cosine errors but we do not have a code generator.
    Need to develop a new code generator that rotates the part in raw mode so that inspection movements use only one axis.
    Testing?
  What is the meaning of Manual Mode?
    What are the key differences from CNC mode
    How do we control the free space movements to avoid collissions?

## Slide 5: Building data

## Slide 6: Building data - Boeing