## Slide 1: AP-238 Walkthrough
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: AP-238 Units of Functionality
General Process Description
  Project
  Executable
  Operation
  Toolpath
Product Description
  Workpiece, PDM and Product Geometry
  Manufacturing Features
  Dimensions and Tolerances
  Measures and Part Properties
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 3: Workpiece, Shape, and PDM
Workpiece is a STEP product description with owner, approvals, dates, material.
Stock, fixtures also have full product description.
Workpiece uses same shape representations as AP203, AP214, AP224, and other APs.
Make with any CAD system that supports STEP.

## Slide 4: Machining Features
round hole
counterbore hole
compound feature
pocket with
through bottom
condition
pocket with
flat bottom
condition
slot with
radius
ends
2.5D milling features
  Hole, pocket, slot, step, etc
Transition features
  Edge round and chamfer
Replicate feature
  Patterns of repeated features
Region features
  Surfaces for freeform milling
Turning features
  Outer round, knurl, groove
Notes: This slide represents the highlights of AP224.
The list of items in each box represents a sample of what AP224 contains.
To summarize - AP224 contains everything found on a drawing of a part

## Slide 5: Machining Features
Features can have implicit and explicit shape
  Implicit feature shape is a parametric description using profiles and paths
    The parameters may have plus/minus, limits and fits, max/min limitations.
  Explicit feature shape links geometry faces to features for visualization, machining, simulation etc.
Implicit description
A round_hole is defined by a complete circular profile and a linear path
Explicit description
Refers to the B-REP faces on the geometry that describe the hole

## Slide 6: Process and Final Features
An AP-238 model can document both final feature and process feature
  Final feature is on final part, from upstream, possibly from an AP-224 or AP-240 application. As such, some features might only define a volume when combined with the stock.
  Process features are the features pointed to by workingstep. Specific to a workplan, need full volume limits.
  Workingstep can also point to one or more final features that it contributes to. Many workingsteps and process features may contribute to one final feature.
Final feature in red (POCKET)
Process features describe:
- Drill the corners (HOLE)
- Mill out center with large tool (POCKET)
- Mill remaining material
with smaller tool (FINAL POCKET)

## Slide 7: Dimensions and Geometric Tolerances
Dimensions defining location
  Location defined by a linear distance
  Location defined by a distance along a curve
  Location defined by an angle
Dimensions defining size
  Curves, angle, diameter, radius, thickness, length, width, height
Geometric characteristics with datums as needed.
  angularity, circular runout, coaxiality, concentricity, cylindricity, flatness, line profile, parallelism, perpendicularity, position, roundness, straightness, surface profile, symmetry, total runout
0.01
0.01
A
0.01
A

## Slide 8: GD&T and Measures
The GD&T definitions are harmonized across all design and manufacturing APs.
  Harmonized across AP-214, AP-224, AP-240, and AP-203e2, which uses Modules 1050 and 1051. Will also be going into AP-219 and other APs.
AP238 measure values and units
  Geometric shape and measure parameters can specify their units, as in all other APs.
  Parameter tolerances can be used for any quantity, not just lengths. Now available for angles, speeds, etc.

## Slide 9: Linkage: Features and GD&T
STEP geometric tolerances link to the workpiece through “shape aspects”
Features are special types of shape aspects
  Can refer to explicit geometry (faces, etc) on workpiece
  Can describe key parameters with +/- tolerances
  Machining or probing operations refer to features.
  Geometric tolerances and datums can refer to features.
Round Hole
Feature
Position
Geometric
Tolerance
Roundness
Geometric
Tolerance
Planar Face
Feature
Datum

## Slide 10: Features and Measurement
Inspection features have been defined by AP-219 but have not yet been added to AP-238
  Current features describe nominal form, with tolerances.
  Probing operations describe measurement points with link to measured value.
  No technical barrier to adding AP-219 features, would further characterize the measurement points.
Round Hole
Feature
Workpiece Probing
Operations
Workpiece Probing
Operations
Workpiece Probing
Operations
Workpiece Probing
Operations
Workpiece Probing
Operations
Circle
Inspection
Feature
(future)

## Slide 11: AP-238 Units of Functionality
General Process Description
  Project
  Executable
  Operation
  Toolpath
Product Description
  Workpiece, PDM and Product Geometry
  Manufacturing Features
  Dimensions and Tolerances
  Measures and Part Properties
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 12: Machining Programs
The heart of the STEP-NC model
  Workplans containing a sequence of workingsteps.
  Each workingstep associates an operation with a feature somewhere on the workpiece.
  Each operation describes what to do (mill/drill/turn, toolpaths), tool requirements, strategies and parameter settings to use.
More information than M and G codes. Linked with geometric and technological information.
  Parameters can be grouped and shared, e. g. tools, feeds, etc.
  Toolpaths specified in STEP geometry in part space.
  Part shape and feature descriptions could be used by intelligent NC controllers for collision detection or even to calculate some tool movements.

## Slide 13: Machining Programs
Project
  Starting place, defines setup and main workplan
Executables
  Describes control flow and sequencing.
  Workingstep associates an operation and a feature.
  Technology independent
Operations
  Describes what a workingstep does — plane mill, center drill, contour turning, etc.
  The basis for all technology-specific extensions.
  Specifies details like
    spindle, feedrate and other technology parameters
    coolant & other machine functions
    tool paths, plunge strategies, etc.

## Slide 14: Control Flow and Sequencing
executable
nc function
program
structure
workingstep
machining workingstep
rapid movement
touch probing
STEP-NC Executables
Program steps that do not move any machine axes
(display message, etc.)
Control flow for the machining program
workplan
parallel
if_statement
while_statement
Program steps that move
the machine axes

## Slide 15: Toolpaths
Used for explicit control of the tool motion for an operation.
  Can use splines or other curves to describe motion and feedrates.
  Can describe path as machine independent motion of tool center point or tool contact point.
  Can also describe path using old-style machine dependent motion of individual axis.

## Slide 16: AP-238 Units of Functionality
General Process Description
  Project
  Executable
  Operation
  Toolpath
Product Description
  Workpiece, PDM and Product Geometry
  Manufacturing Features
  Dimensions and Tolerances
  Measures and Part Properties
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 17: Technology Description
Drilling
  Drilling, boring, back boring, tapping/threading
  Many strategy parameters
2.5D Machining
  Plane and side milling, roughing and finishing
  Set of strategies
Freeform Machining
  3, 4, and 5axis motion
  Set of strategies
Turning
  Contouring, facing, grooving, threading and knurling.
  Set of strategies

## Slide 18: Milling and Turning Cutting Tools
Every operation has an associated tool.
  Description calls out required characteristic tool parameters
  Can link to product model for tool, including geometry.
  Potential for some optimization by the controller.
G&M codes just referenced tool #1, #2, etc.
  Human must make sure that #1 corresponds to the right thing.
  Controller can not add any value to the process.

## Slide 19: Touch Probing Operations
AP-238 has four probing operations
  Workpiece Probing  probe a single point
  Complete Workpiece Probing  probe for part orientation
  Tool Length Probing
  Tool Radius Probing
Can stand alone, but workpiece probing most useful with associated feature and tolerances.
Round Hole
Feature
Workpiece Probing
Operations
Workpiece Probing
Operations
Workpiece Probing
Operations
Workpiece Probing
Operations
Workpiece Probing
Operations
Position
Tolerance
Roundness
Tolerance

## Slide 20: Measurement Example
Probe to determine whether a face meets a flatness tolerance
Workpiece
Probing
Operations
Workpiece Face
Feature
Probing Tool
and Toolpath

## Slide 21: Example
Compute the status using the measured values and tolerances associated with feature.

## Slide 22: AP-238 Summary
From ISO 14649-10
Measures
Project
Workpiece
Features
Milling Process Operations From ISO 14649-11
Milling Cutting Tools From ISO 14649-111
Turning Process Operations From ISO 14649-12
Turning Cutting Tools From ISO 14649-121
Executable
Operation
Toolpath
AP-238 pulls together machining process, tool requirement, geometry, tolerances, and PDM.
  Start with process and tools described by ISO 14649 parts
  Add STEP PDM, Geometry, and Tolerances, and integrate so that features and all other data can be shared across APs
Dimensions and Tolerances STEP GD&T
PDM and Product Geometry Common to all APs

## Slide 23: Summary
AP-238 a published standard and available on ISO website.
Testing and Demonstrations
  Made using CATIA, Pro/E and UGS
  Milled and Turned parts
  Production parts and test parts
STEP-NC is easy to implement
  Basic prototype in 4 weeks
  Level 2 by adding CAD geometry
Machining benefits
  CNC independent tool paths
  Collision detection on the control
  Feature based programming
  Visual closed loop programming
Enterprise benefits
  Long term data retention
  Interchange with suppliers