## Slide 1: DRAFT HiPP MODEL HiPP = High-Level Dimensional Measurement Process Plan
Thomas R. Kramer
Guest Researcher, Knowledge Systems Group
National Institute of Standards and Technology
October 31, 2007

## Slide 2: Outline
Preliminaries
HiPP Functionality
EXPRESS-G diagram review
Big Ideas

## Slide 3: Preliminaries (1)
Addressing two audiences: DMSC and STEP-NC
  DMSC folk know dimensional measurement but need STEP information
  STEP-NC folk know machining and STEP but need information about dimensional measurement
Draft HiPP model
  Started with AP238 model (ARM) which already stubbed out data used from other STEP models (e.g. geometry)
  Stubbed out machining features and machining operations
  Modified existing model of probes and probing operations
  Added material for HiPP
  Have both EXPRESS (text) and EXPRESS-G (graphical) versions of HiPP model

## Slide 4: Preliminaries (2)
Input to draft HiPP model came from:
  AP238 EXPRESS ARM (Dave Loffredo)
  IDEF0 activity model (Shaw Feng)
  Dimensional Measurement Feature Taxonomy (Curtis Brown)
  AP238 EXPRESS-G markup for HiPP (Curtis Brown)
  Report of HiPP meeting at NIST in April 2007
  DMIS standard
  AP238 (IS review version)
  ISO 14649 (2004 IS version, Parts 10, 11) semantics for AP238

## Slide 5: Preliminaries (3)
Materials for this presentation include:
  Desirable functionality table (1 page, pdf)
  Possible functionality table (1 page, pdf)
  EXPRESS-G notation cheat sheet (1 page, pdf)
  HiPP on color-coded EXPRESS-G diagrams (23 pages, pdf)
  this Powerpoint document (66 slides)
Also available:
  HiPP in EXPRESS text (includes some documentation of meaning), file “hippOnly.exp”
Aiming at two hours to present materials, plus time for questions
Please ask questions whenever you wish

## Slide 6: Preliminaries (4) - STEP
EXPRESS is a high-level information modeling language
  EXPRESS is object-oriented (similar to C++ header files defining classes, types, enumerations -- but with no methods)
  A complete EXPRESS document is called a schema
EXPRESS works with a file format called Part 21
  If you have a schema, you have a file format
EXPRESS can work with other file formats (e.g. XML)
EXPRESS-G is a graphical version of EXPRESS
STEP uses two types of model (ARM and AIM)
  ARM is in terms of the domain being modeled and is readable
  AIM is same meaning encoded using STEP integrated basic resources and is unintelligible
  Using only ARM in this presentation

## Slide 7: Big Ideas (1)
Define HiPP language for writing high-level dimensional measurement process plans
Have two kinds of HiPP:
  Objective Plan: say only what the objectives are (what should be measured) not how to do it
  Executable Plan: say what the objectives are and how to do it (provide a computer-interpretable plan that can be executed)
Be able smoothly to develop an Executable Plan from an Objective Plan
  Both in the same model

## Slide 8: Big Ideas (2)
Use a high-level information modeling language to define HiPP
  For example: EXPRESS, UML, XML Schema (maybe)
  Lets you work with concepts, not notation
  Gives a file format automatically
  Enables using tools that automatically: write software (e.g. C++ classes and class access functions), read file, write files
Have HiPP plans be interoperable
  Be able to read and understand plans on the basis of the standard alone, with no communication between sender and receiver other than a HiPP file transfer
  No user-defined semantics

## Slide 9: Big Ideas (3)
Take advantage of existing AP238 model
  Already contains a large chunk of functionality needed in HiPP
  Is at the same level of abstraction as a HiPP executable plan
Have HiPP be integrated with metal-cutting (milling and turning) so that dimensional measurement can be done concurrently with cutting
  An important capability for the near future (already done in some applications)

## Slide 10: Desirable HiPP Functionality (1)
Dimensions and tolerances
  essential
  already in AP238
  said to be harmonized with other parts of STEP, including AP214 (automotive) and AP224 (machining features)
  very similar to DMIS
  harmonized with AP219 (?)
  based on ANSI Y14.5 (?)

## Slide 11: Desirable HiPP Functionality (2)
Dimensional measurement features
  essential
  added to AP238 for HiPP
  exists in DMIS (28 kinds of FEAT)
  taxonomy provided by Curtis Brown
  draft HiPP model includes all DMIS features

## Slide 12: Desirable HiPP Functionality (3)
Actual vs. nominal for features
  essential
    best way to model is not obvious
    flags may suffice in the HiPP model to indicate whether nominal or actual is to be used (for output, constructions, etc.)
    execution systems need to record both actual and nominal parameter values, but it may or may not be desirable to include both in the HiPP model
  exists in DMIS (F vs. FA)
  not yet added to AP238 for HiPP

## Slide 13: Desirable HiPP Functionality (4)
executable dimensional measurement process plan
  essential
  execution either generates a lower-level plan (e.g. a DMIS program) or controls machine to perform dimensional measurement
  added to AP238 for HiPP
    similar to executable machining process plan model already in AP238
  is represented by a tree of entities with its root at a project (not by a single entity)
  functionality is roughly equivalent to a DMIS input file

## Slide 14: Desirable HiPP Functionality (5)
objective dimensional measurement plan
  essential
  states what the objectives are (what features and tolerances to measure) and what to report
  does not specify how to measure
  not in DMIS
  added to AP238 for HiPP

## Slide 15: Desirable HiPP Functionality (6)
method to make executable plan from objective plan
  extremely desirable
  add parameter values to dm_workingsteps or other dm_executables
  change (unordered) sets to (ordered) lists
  not in DMIS
  added to AP238 for HiPP

## Slide 16: Desirable HiPP Functionality (7)
dimensional measurement operation
  essential
  operations are things like touch probing, scanning, setting datums
  exists in DMIS
  five stubs have been added to AP238 for HiPP (dm_operation, coordinate_system_operation, datum_operation, point_measurement_operation, and algorithm_operation)
  HiPP model needs additional dm_operations that are subtypes of the five listed above

## Slide 17: Desirable HiPP Functionality (8)
dimensional measurement workingstep
  links an operation with a feature
  essential
  functionality exists in DMIS under other names
  added to AP238 for HiPP
    similar to machining workingstep already in AP238

## Slide 18: Desirable HiPP Functionality (9)
output of measurement results
  essential
  exists in DMIS
  a small amount existed in AP238
    set a variable by performing a measurement
  AP238 modified slightly for HiPP
  more needs to be done in the HiPP model

## Slide 19: Desirable HiPP Functionality (10)
datums
  essential
  already in AP238 (full set)
  exists in DMIS
  should be adequate as is

## Slide 20: Desirable HiPP Functionality (11)
setups
  desirable
  already in AP238
  specifies where the workpiece is in machine coordinates
  also has operator instructions and restricted area
  not in DMIS

## Slide 21: Desirable HiPP Functionality (12)
coordinate systems
  essential
  need to be able to create, locate, and transform coordinate systems
  exists in DMIS
  tiny amount added to AP238 for HiPP
  more needs to be done in the HiPP model

## Slide 22: Desirable HiPP Functionality (13)
workpiece
  essential
  already in AP238
    includes full nominal BREP description using STEP geometry and topology
  a little exists in DMIS

## Slide 23: Desirable HiPP Functionality (14)
machines for dimensional measurement
  desirable
  not in DMIS
  a little added to AP238 for HiPP (gage and CMM)

## Slide 24: Desirable HiPP Functionality (15)
tools for dimensional measurement
  desirable
  includes probes, probe assemblies, extensions, holders, etc.
  AP238 had a small amount, which has been modified for HiPP
  DMIS has a great deal
  more needs to be done in the HiPP model

## Slide 25: Desirable HiPP Functionality (16)
strategies for dimensional measurement operations
  desirable
  stub added to AP238 for HiPP
    AP238 has strategies for machining
  DMIS has an equivalent in the RMEAS command (others?)

## Slide 26: Desirable HiPP Functionality (17)
accuracy requirements
  desirable
  says how accurate the measurements are required to be
  added to AP238 for HiPP

## Slide 27: Desirable HiPP Functionality (18)
uncertainty
  desirable
  includes uncertainty data and rules for using uncertainty in making in-tolerance/out-of-tolerance decisions
  exists in DMIS
  not yet added to AP238 for HiPP

## Slide 28: Desirable HiPP Functionality (19)
geometry and topology
  desirable
  used to specify shape in designs and workpiece descriptions, possibly also for tool assembly descriptions, tool paths, forbidden zones, etc.
  in DMIS as text only
  already in AP238 (full brep)
  should be adequate as is

## Slide 29: Desirable HiPP Functionality (20)
machining features
  desirable
  needed in HiPP so dimensional measurement can feed back to machining
  already in AP238
  needs improvement by ISO14649 developers

## Slide 30: Desirable HiPP Functionality (21)
association between geometry and dimensional measurement features
  desirable
  says what elements of geometry and topology correspond to a dimensional measurement feature
  a little exists in DMIS, but DMIS has no geometry model
  added to AP238 for HiPP

## Slide 31: Desirable HiPP Functionality (22)
association between machining features and dimensional measurement features
  desirable so that dimensional measurement can feed back directly to machining (when dimensional measurement is done during the machining process) or feed back to process planning for machining
  not in DMIS
  not in AP238
  needs to be added to HiPP model

## Slide 32: Desirable HiPP Functionality (23)
flow of control operations
  essential
  already exists in AP238 (but weakly)
    only “if” for branching and “while” for looping (also has parallel, selective, and non-sequential)
    example of weakness: does not seem to be possible to increment a counter while looping
  exists richly in DMIS
    DO, IF (with ELSE), SELECT (with CASE)
  needs to be improved in HiPP model

## Slide 33: Desirable HiPP Functionality (24)
variables (of various data types)
  essential
  exists weakly in AP238
    variables may be only numeric (integer or real)
  exists in DMIS
    variables may be: char (i.e. string), integer, long, real, double, boolean, or vector

## Slide 34: Desirable HiPP Functionality (25)
expressions and operators
  essential
  AP238 has only boolean expressions and operators
    cannot add, subtract, multiply, or divide
  exists richly in DMIS
  need to add more to HiPP model

## Slide 35: Desirable HiPP Functionality (26)
functions
  desirable
  AP238 has no functions
  exists in DMIS, examples are:
    sine (numeric argument, double return value) -- SIN
    substring (character and integer arguments, character return value) -- SUBSTR
    cross product (vector arguments and return value) -- VCROSS
  need to add to HiPP model

## Slide 36: Desirable HiPP Functionality (27)
choice of units (for length, time, speed, etc.)
  desirable
  already in AP238 (profusely)
  exists in DMIS
  should be adequate as is

## Slide 37: Desirable HiPP Functionality (28)
administrative data (dates, approvals, security, etc.)
  already in AP238
  exists a little in DMIS
  may be adequate as is

## Slide 38: Desirable HiPP Functionality (29)
messages to operator (on operator’s console)
  desirable
  already in AP238
  exists in DMIS (TEXT)
  may be adequate as is

## Slide 39: Desirable HiPP Functionality (30)
input from operator
  desirable
  not in AP238
  exists in DMIS (PROMPT)
  should be added to HiPP model

## Slide 40: Desirable HiPP Functionality (31)
command for rotary table motion
  desirable
  not in AP238
    There may be a rotary axis implemented by a rotary table, but AP238 has no commands to set a specific axis. The rotary table moves only as necessary to achieve a tool position and orientation.
  exists in DMIS
  should be added to HiPP model

## Slide 41: Desirable HiPP Functionality (32)
integration of dimensional measurement and machining
  desirable
  included in draft HiPP model primarily by virtue of being able to produce a process plan with both types of operation in it
  a little was already in AP238
    probe a point
    fit a coordinate system to a workpiece

## Slide 42: Desirable HiPP Functionality (33)
command for return to home position
  desirable
  already in AP238
  exists in DMIS (GOHOME)

## Slide 43: Desirable HiPP Functionality (34)
high-level language used to build HiPP information model
  desirable (meta-functionality)
    high-level information modeling languages include EXPRESS, UML, and (maybe) XML schema
    high-level language enables automatic file format definition, automatic readers and writers, automatic generation of computer code for structures and access functions
  already in AP238 (written in EXPRESS)

## Slide 44: Possible HiPP Functionality (1)
use cylindrical or cartesian coordinates
  not in AP238
  exists in DMIS (CART vs POL)

## Slide 45: Possible HiPP Functionality (2)
set variable by reference to parameters of features (or other data)
  not in AP238
  exists in DMIS (OBTAIN)

## Slide 46: Possible HiPP Functionality (3)
select various output devices
  not in AP238
  exists in DMIS (OPEN, WRITE, CLOSE)

## Slide 47: Possible HiPP Functionality (4)
set the home position
  home position is where the controlled point goes when a home command is given
  not in AP238
  exists in DMIS (FROM)

## Slide 48: Possible HiPP Functionality (5)
command a sensor change
  not in AP238
    tool change happens automatically when a tool not in the spindle (or ram) is required to be used
  exists in DMIS (SNSLCT)

## Slide 49: Possible HiPP Functionality (6)
calibrate a sensor
  not in AP238
  exists in DMIS (CALIB)

## Slide 50: Possible HiPP Functionality (7)
set probing motion parameters
  parameters include:
    approach distance (SNSET)
    search distance (SNSET)
    retract distance (SNSET)
    speed while measuring (FEDRAT)
    acceleration while measuring (ACLRAT)
  not in AP238

## Slide 51: Possible HiPP Functionality (8)
construct features by referencing other features
  not in AP238
  exists in DMIS
    supported by point-reducible and plane-reducible features (Table 8)
    15 types of construction (CONST)

## Slide 52: Possible HiPP Functionality (9)
handle multi-carriage machines
  not in AP238
  exists in DMIS (CRSLCT)

## Slide 53: Possible HiPP Functionality (10)
set program execution mode (e.g. manual, prog, auto)
  not in AP238
  exists in DMIS (MODE)

## Slide 54: Possible HiPP Functionality (11)
define and use macros
  not in AP238
  exists in DMIS (MACRO, CALL)

## Slide 55: Possible HiPP Functionality (12)
have an “include” directive
  not the sort of thing that would be dealt with in an AP, so not in AP238
  the equivalent may be possible with STEP Part 21 files using FOR_EXPORT and EXTERNAL_REFERENCE_FOR_COMPUTER
    awkward at best
  exists in DMIS (INCLUD)
    straightforward text insertion (like C or C++)

## Slide 56: Possible HiPP Functionality (13)
allow sections of alien code in programs
  not in AP238
  exists in DMIS (DMIS/ON, DMIS/OFF)

## Slide 57: Possible HiPP Functionality (14)
allow selection of algorithms
  not in AP238
  exists in DMIS
    ALGDEF and SNSET for vision algorithms
    GEOALG for fitting algorithms
    UNCERTALG and UNCERTSET for uncertainty decision rules
    CALIB for calibration algorithms
    PATH for scanning

## Slide 58: Possible HiPP Functionality (15)
have predefined QIS (quality information system) variables
  not in AP238
  exists in DMIS (Table 5)

## Slide 59: Possible HiPP Functionality (16)
define and use boundaries for features
  not in AP238
  exists in DMIS
    BOUND command applies to features and tolerances
    some features may optionally include a bound (e.g. cylinder)
    some features have required bounds (e.g. spherical segments)
  this is probably essential

## Slide 60: Possible HiPP Functionality (17)
define and use mating features
  not in AP238
  exists in DMIS (MATDEF, LOCATE)

## Slide 61: Possible HiPP Functionality (18)
specify conditions in which an error should be signalled
  not in AP238
  DMIS has a few statements regarding this

## Slide 62: Possible HiPP Functionality (19)
have predefined error conditions and error handling
  not in AP238
  exists in DMIS (ERROR, SILTCH function, SENSNOTOUCH function)

## Slide 63: Possible HiPP Functionality (20)
have a single command to measure and define a coordinate system
  was in AP238 (workpiece_complete_probing)
    did not seem well-defined
    was removed from HiPP model
  not in DMIS

## Slide 64: Possible HiPP Functionality (21)
have a “reaction plan” for handling error conditions
  not in AP238
  not in DMIS
  was suggested at NIST HiPP meeting as possible functionality

## Slide 65: Possible HiPP Functionality (22)
define acceptable pass/fail errors
  not in AP238
  not in DMIS (different from INTOL/OUTOL)

## Slide 66: Questions and Discussion