## Slide 1: STEP-NC Plate Cutting and Marking Extension for AP238 E2
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: STEP-NC Plate ARM Extension
STEP-NC for cutting and marking from actual shipbuilding data sources
  AP203 geometry for plate shape
  CATIA APT to describe the marking and cutting process
  Include straight and bevel cuts, line and text marking
Constructed AP238 CC2 data to describe plate and process
Prototyped tools to drive ESAB plasma cutter and laser marking machines from AP238 data
Cut actual plate at EB Quonset Point facility

## Slide 3: Original CATIA Data
T999-0001S1 3D MODEL with footprints on
T9990002-STEP2
T9990002-STEP1

## Slide 4: Cutting and Marking APT
T9990002-STEP2 with far side footprints visible

## Slide 5: Construct AP238 Data
Process APT data to produce AP238 process
  Used tools already developed for milling and turning information
  Created AP238 “extended nc function” instances for extra plate cutting APT data like head on/off, bevel angle, marking line width
  Eventually extend AP238 to hold these in the operation technology descriptions
Add STEP geometry to the process to see in context of workpiece
  Matching location required moving geometry 100 yards!

## Slide 6: AP238 Data for Plate Cutting and Beveling

## Slide 7: Add Manufacturing Preparation Data
As designed, cuts start right on edges
  For plasma cutting, lead ins and lead outs are required to avoid gouging the part
  Also important for bevels to give cutting head time to traverse into position after piercing
Created utilities to add lead ins and lead outs to the STEP-NC data
  Today, these are added by nesting systems like Optimation, Majestic, Sigmanest, etc.
  These systems could read and write STEP-NC in the future.

## Slide 8: STEP-NC Manufacturing Prep.
Tangential Entry/Exit

## Slide 9: STEP-NC Manufacturing Prep.
Bevel Entry

## Slide 10: Drive Plasma Cutter / Laser Marker
Extend existing AP238 CNC interface to export codes for ESAB controls
  Many unique codes, machine peculiarities, close contact with EB personel required to understand them
  Local conventions for setup and registration of the plate, coordinate system transformations for near/far, etc.
Single STEP-NC program for entire plate
  Need to split into separate programs to cover near-side marking, far-side marking and cutting
STEP-NC Plate
Program
ESAB Near Mark
ESAB Far Mark
ESAB Plasma Cut

## Slide 11: Unique Codes and Peculiarities
Some APT and ESAB codes are rather obscure
Example, marking the text “-STEP11”
  In APT: MARK/ 45, 83, 84, 69, 80, 49, 49, 0, 0
    Represented as numbers corresponding to ASCII
  In ESAB Codes:
    F100.0
    G89D003
    G81D0.375
    G82D271.1
    G80
    (-STEP11)
    D004
    M75
In addition, there are machine peculiarities like ordering of codes, decimal points, etc.

## Slide 12: Quonset Demonstration
May 9, 2007, Marked and cut the test part at EB Quonset Point facility
  Marking and cutting successful. Minor issue discovered with ordering of an ESAB marking code, corrected on site.
  Simulator no substitute for the real thing!

## Slide 13: Current vs STEP-NC Process
APT
Drawings
Nesting
G-Code Near,
Far Marking,
Cutting
Catia
STEP-NC
Nesting
STEP-NC
CNC
Potential for other value adds
Catia
Current Process:
STEP-NC Process:

## Slide 14: Extensions to the STEP-NC Model
probe point, tool, …
plane milling, side milling, drilling, plate cutting, plate marking
workplan, if/then, parallel, …
cutter location trajectory, cutter contact trajectory, …
pocket, plane, hole, region, possible future extensions
workpiece
S[0:?]
S[0:?]
executable
machining_workingstep
tool
machine functions
strategy
L[0:?]
toolpath
geometry
geometry
geometry
as workpiece,
stock, fixture,
or tool use
possible extension
technology
machining_operation
machining_feature

## Slide 15: New ARM Entities
Operation
  plate_cutting_operation
  plate_marking_operation
    plate_explicit_text_-marking_operation
    plate_workpiece_id_-marking_operation
    plate_line_marking_-operation
Approach_retract_strategy
  plate_lead_strategy
    plate_lead_linear
    plate_lead_tangential
Feature
  ap224 marking subtypes
Technology
  plate_cutting_technology
  plate_marking_technology
Machine Functions
  plate_machine_function
Machining_tool
  plate_tool (placeholder)

## Slide 16: Explicit Toolpaths
An operation can specify explicit toolpaths
  Each toolpath specifies a curve, technology parameters and machine state information can vary between them.
Cutting Operation
Technology
bevel = 45deg
Technology
bevel = 0deg
Machine Functions
kerf = left
height sensor = on
Toolpath
Toolpath

## Slide 17: Feature-Based
An operation can be associated with a feature
  Strategies for lead in/out
  Bevel for entire profile? Taper on feature?
Cutting Operation
linear lead strategy
length = 2 inch
linear lead strategy
length = 1 inch
lead-in
lead-out
start point
Technology
bevel = 45deg
Machine Functions
kerf = left
height sensor = on
feature profile (from workingstep)

## Slide 18: ARM Issues for Discussion
Coverage of current APT capabilities
Completeness of Parameters
Explicit Toolpaths vs. Features and Strategies

## Slide 19: Discussion - APT
APT capabilities we have seen
  CYCLE/BOTTOM Bottom bevel pass on multi-pass edge
  CYCLE/DUMMY Dummy cycle to define part perimeter
  CYCLE/FAR Far side single-pass bevel
  CYCLE/LAND Land pass on multi-pass edge
  CYCLE/NEAR Near side single-pass bevel
  CYCLE/PLABEL Near side laser marked part label
  CYCLE/PLABELF Far side laser marked part label
  CYCLE/PLASMA Straight cut pass. No bevels on the part
  CYCLE/PMARK Near side punchmarked/laser marked geometry
  CYCLE/PMARKF Far side laser marked geometry
  CYCLE/STRGHT Straight cut single pass entity on bevel part
  CYCLE/TEXT Near side laser marked text
  CYCLE/TEXTF Far side laser marked text
  CYCLE/TOP Top bevel pass on multi-pass edge

## Slide 20: Discussion - APT
APT capabilities we have not seen or tested
  CYCLE/BEVEL GX3 style bevel pass
  CYCLE/LABEL Old style part label (GX4 marker support)
  CYCLE/OXFUEL Oxyfuel - GX3 only
  CYCLE/TAB Straight cut pass to cut tabs
  Others?

## Slide 21: Discussion - Parameters
Completeness of Parameters
  Tested for laser marking and plasma cutting
  What other parameters needed for laser cutting, oxyfuel cutting, water cutting, punch marking? others?
  Line styles for marking, depth of marking?
  Bar code marking of plates?
  Parameters to simplify nesting?
    Minimum distance?
  Data example to verify that plate material and thickness can be modeled

## Slide 22: Discussion – Toolpath vs Feature
Explicit Toolpaths vs. Features and Strategies
  Use of existing general profile and pocket features, text marking features (in aim, but not arm).
  Handling bevels and tabs at the feature level
  Explicit leads vs. lead strategies only

## Slide 23: Future Work
Answer ARM questions
Test process improvement opportunities
  Beveling for small and/or detailed edges
  Edge quality control (e.g bounce prevention)
  Nesting
  Supply chain interoperability
Demonstrate at second site
  Validate ARM
  Validate increase in data quality
    Elimination of extended NC functions
    Consolidation into cohesive operations