## Slide 1: STEP-NC Traceability Pilot Project
Fred Proctor, Mike McGlauflin and John Michaloski
NIST Manufacturing Engineering Laboratory

## Slide 2
Today, OLE for Process Control (OPC) has emerged as a leading worldwide specification in enabling connectivity and interoperability of factory floor equipment.

## Slide 3: CNC OPC Tag Naming & Mapping
OPC does not define any application item tag names
OMAC HMI Working Group has defined a list of CNC-related OPC tags
  Object orientation is attained by a tag naming strategy – using slash or period – Axis.Label, Axis.Position
Comparison of Commercial CNC OPC tag collections has been done at NIST against OMAC tags
  There are some gaps which we hope to identify
Notes: OPC does not define any application item tag names , e . g . AxisLocation
Object oriented or hierarchical naming using slash or period Axis.Label, etc.

## Slide 4: Data Logging Virtual Machine
The predominant CNC machine tool programming language is RS274
Most CNCs have their own programming language extension to RS274, known as User Macros or Subprograms
Subprograms and Macros provide a layer of programming abstraction on top of the CNC, acting as a Virtual Machine
A Data Logging virtual machine will be specified as a set of subprogram calls that are implemented in the native CNC RS274 dialect

## Slide 5: Data Logging Process
CNC with an OPC server provides OPC tagged data
Data Logging OPC client is a separate application running in the background of the CNC computer or a remote computer
  You specify a Data list that you wish to collect from the CNC
  When one or more values change in the data list, the CNC OPC server will notify the OPC Client of the changes and the OPC Client can read these values.
Notes:   Supporting a limited number of import/export file formats with broad industry support has been deemed preferable to having a separate language to describe formatting and analysis of the data. The None format allows data logging without physical file saving to allow monitoring for potential machine faults.

## Slide 6: Data Logging Process
A Data Handler component manipulates the data according to a given configuration
  For a more concise data, configure the options of the data collection by defining a Filter. The default filter is to log all the data items whenever one changes.
  The Formatter provides support for saving the log to a Destination, such as Persistent Data Store, in some common data collection and analysis format. Typical formats include None, Text, Comma Separated Values (CSV), XML, or database.
A Data Analysis can generate reports, fine tune or troubleshoot machining performance, analyze trends, or tie-in directly to the CNC and provide safeguarding machining operations – such as machine halting or feed rate override.

## Slide 7: Method 1: Explicit Naming
AddDataItem(NAME , FILTERTYPE, value1 {, value2}) is implemented in the CNC Virtual Machine as a subprogram or macro
NAME is one of
  Axis
  AxisLoad, SpindlePower
  CmdFeedrate, ActualFeedrate
  CmdSpindleSpeed, ActualSpindleSpeed
  State, Mode, ProgramName, Block, LineNumber
FILTERTYPE is one of
  Deadband: logs only if changes between values is greater than value1
  Threshold: logs only if abs(value) > value1
  Range: logs if value is in [value1 , value2] range
  Dependent: unmonitored, logs only if other values change
  Equality: supervisory, logs only if value equals value1
  Inequality: supervisory, logs only if value not equal to value1

## Slide 8: Method 1: Explicit Naming
StartLogging(TYPE, FILENAME)
  TYPE defines the type of archival destination for the captured data, either NONE, TXT or CSV (text files), or DB (data base)
  FILENAME defines the archival destination file name or other appropriate identifier
Problem here is enumerating list of all potential data items. Possible solutions: use categories of data logging, such as axis position, axis dynamics, axis servo, program

## Slide 9: Method 2: Delegation
OpenLogging(TYPE, FILE, DATA, FILTER) references files that contain the explicit data
  TYPE is one of NONE, TXT, CSV or DB
  FILE is the destination file or identifier name
  DATA is the file specifying the data to be captured
  FILTER is the file specifying the filter to be applied
Example:
  OpenLogging(“CSV”, “PartA”, “DataItems”, “”)
Associated Start,Stop,CloseLogging() macros

## Slide 10: OPC-CNC Synchronization
Method 2 used for this pilot:
  We built an OPC client in C++ that listens to CNC and reads out tagged data
  Siemens 840D NC code calls
    MSG(OpenLogging(…)) to set up the OPC client
    MSG(StartLogging) tells OPC client to begin
  NC code continues with machining, while OPC client logs the data according the configuration files

## Slide 11
Spindle power log plot, showing spikes in some corners

## Slide 12
Spindle power log plot, subset with clean data

## Slide 13
Axis path deviation and spindle load