## Slide 1: ISO TC184 / SC4 WG3/T24
HSM machining in Bordeaux
STEP AP238 demonstration
10-12 March 2008 SWEDEN

## Slide 2
STEP AP238 demonstration in SWEDEN
BORDEAUX
HSM 600U
iTNC530
BC
36000
D=16
C40
iTNC530
AC
18000
D=16
RENISHAW
SCANIA - KTH
FEED & SPEED
OPTIMISATION
CLOSED LOOP
HSM
Data compression
TRACEABILITY
NIST - VIGO

## Slide 3: Resources
BORDEAUX
MIKRON
HSM 600U
HEIDENHAIN
iTNC530
BC
29000 – 36000 rpm
D=16 R4 finishing
D=12 R1.5 roughing
EROWA
320x320 pallet
MASTERCAM
VERICUT

## Slide 5
BORDEAUX
MIKRON
HSM 600U
iTNC530
BC
36000
D=16 R4 finishing
D=12 R1.5 roughing
VALIDATION
VERICUT
AP238 
G code
TCP
CL
STEP AP238
3D data
STEP
AP203
OK
ST explorer
TOOLPATH GENERATION
MASTERCAM
Cutter locater
File
roughing
CLFile
finishing
This chart tracks the conversion of a MASTERCAM CL File
which in turn is converted into a tool centre processing file
that was checked and used to machine the fishead
in the MIKRON HSM600U with HEIDENHAIN iTNC530
.i
.238
.i
.CLfile

## Slide 6: Setup
On pallet EROWA 320x320
Bolts on bottom side

## Slide 7: Cutting parameters
Roughing 2 ½ axis up to 0.5 mm
  Tool D=12 R=1.5
  36 000 rpm
  From outside to inside
  Plunge strategy for pockets
  Ap = 2.5 mm
Finishing 5 axis 1 run
  Tool D=16 R=4
  29 000 rpm
  Ae(minimum) =0.5 mm
  Issues:
      Steps
      Vertical to 15 ° correction
      Milling

## Slide 9: Metrics
Roughing
  1 hour
Finishing
  30 mn

## Slide 10: Comments
Toolpath generation
  plunging in pockets
  left side corner
  extensive use of VERICUT
Cooling issues
  moisture and coolant
Surface quality
  End of travel