## Slide 1: Speed/Feed Optimization Demonstration
3-axis roughing of ”fishhead” component
Bengt Olsson
Sandvik Tooling
Leon Xu
Boeing
Fred Proctor
NIST
Sten-Åke Ekström
Sandvik Coromant
Alain Brail
Airbus
Martin Hardwick
STEP Tools

## Slide 2: Step 1 Preparation of tool paths
Design
  Design by Airbus (CATIA)
Tool paths
  Tool selection and tool paths by Sandvik Coromant (NX5)
Cross section calculations
  Simulation by Sandvik Coromant (VERICUT)
  Cross section calculations by Boeing
All combined into one STEP-NC file
  by STEP Tools (STEP NC Explorer )

## Slide 3: Step 2 Optimization for specific machine and cutting tools
Combine tool paths with optimized speed&feed values
  Cutting tools defined by Sandvik Coromant
  Machine tool defined by Mori Seiki
  Algorithms by Boeing
machine limitations: -power/torque curve
tool usage recommendations: -chip thickness -engagement -cutting speed
All combined into one STEP-NC file
  by STEP Tools (STEP NC Explorer )
Benefits with optimized paths
  Smooth performance =no over rides by operator
  Consistant tool life
  Part quality

## Slide 4: Step 3 Preparation of the actual cutting tools
Assembly of the physical cutting tool
  ”Current data” of actual tool (ISO13399)
Ready for STEP-NC machining!
  STEP NC Explorer by STEP Tools

## Slide 5: Step 4 Manufacturing
CNC Machining at Sandvik Coromant (Mori Seiki NH8000)
  Spindle specification: -Coromant Capto C8 tool interface -25kW at 8,000rpm
  Comparison between optimized vs. non-optimized
  Optimized program saves 6% cycle time (9 min 53 sec instead of 10 min 28 sec )
CNC Machining moved to Boeing (Okuma MC-V4020)
  Spindle specification: -HSK40 tool interface -11kW
  Optimized program takes 19 min 53 sec
  Part is manufactured without any problems from 1st piece

## Slide 6: Step 5 Inspection
CNC probing
CMM probing
How should we integrate the results?

## Slide 7: Step 5 Inspection
How should we integrate the results?
Flatness tol__84712(PLANE_TOLERANCE_FEATURE_83180)
-----------------------------------------------------------------------------------------
Name Desc Nominal Actual Deviation Graphic
-----------------------------------------------------------------------------------------
tol__84712 FLAT 0.050 0.020 |---+*--|
-----------------------------------------------------------------------------------------
Perpendicularity tol__86123(CYLINDRICAL_TOLERANCE_FEATURE_84714)
-----------------------------------------------------------------------------------------
Name Desc Nominal Actual Deviation Graphic
-----------------------------------------------------------------------------------------
tol__86123 PERP 0.250 0.002 |---*---|
-----------------------------------------------------------------------------------------
Diameter tol_DIAMETER_86125(CYLINDRICAL_TOLERANCE_FEATURE_84714)
-----------------------------------------------------------------------------------------
Name Desc Nominal Actual Deviation Graphic
-----------------------------------------------------------------------------------------
...METER_86125 DIAM -0.050 -0.085 *|---+---|
...METER_86125 DIAM 0.050 -0.085 *|---+---|
-----------------------------------------------------------------------------------------

## Slide 8: Multi Task Machining Demonstration One tool spindle, one lower turret and two workpiece spindles
Lower turret
Sp 1 Main spindle
Sp 2 Sub spindle
Op 2
Op 1
Capto C4
Auto transfer
Alt. 4
Two spindles
V/H
V/H 45º
V/H 45º Yoffset
Alt. 1
Alt. 2
Alt. 3

## Slide 9: Multi Task Machining Demonstration Including CNC probing
1. Measure cut
2. Probing and correction of tool length (x-value)
3. Finishing cut
a
a
Finishing cut
Close tolerances
Ø 40 h7 0/ -0,025
0,0125
Roughing
a
re