## Slide 1: STEP-NC Technical Issue
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
File size reduction for High Speed Machining

## Slide 2: Description
HSM files contain many arc’s.
The STEP-NC representation for arc’s is verbose
  An additional line segment requires one additional Cartesian point entity in a polyline.
  An additional arc requires:
    A composite curve entity
    A circle entity
    An axis2_placement entity
    2 direction entities
    2 Cartesian point entities
  And it has to be repeated for every curve because of the parameterization rules
    Tool axis curve
    Cross section parameter curve
    Feed override curve

## Slide 3: Analysis
STEP representation for bounded curve is very powerful
  Allows many types of entities to be included in the curve
  Line, arc, b-spline, curve-on-surface, others
But legacy machining data today is either
  Millions of line segments – traditional data
  Millions of line and arc segments – HSM data
We need a more compressed method for representing legacy data
  Full semantics are not helpful for this data
STEP Kinematics schema shows how
  Three points define an arc
  Four points (with two coincident) define a complete circle

## Slide 4: Proposed Solution
The STEP schema for kinematics has via-entities.
  The path goes via the given point
We propose enhancing the representation of tool path polylines to allow for two types of via-points
  “via_arc”
  The curve to and from the via is an arc
  “via_helix”
  The curve to and from the via is a helix arc

## Slide 5: via_arc
ENTITY via_arc SUBTYPE_OF (cartesian_point);
start
end
ccw arc
start
end
via arc
Bounded Curve Encoding
Start = composite_curve,trim._1
End = composite_curve.trim_2
Radius = composite_curve.circle.radius
Center = composite_curve.circle.placement.location
Sense = composite_curve.sense_agreement
Axis = composite_curve.circle.placement
Via Encoding
Start = polyline[0]
Via = polyline[1]
End = polyline[2]
Radius = radius (start, via, end)
Center = center (start, via, end)
Sense = pdistance (sense, start, via) <
pdistance (sense, via, end)
Axis = toolpath_axis
Center (a, b, c) computes a circle center from three distinct points
Radius (a, b, c) compute a circle radius from three distinct point
Pdistance (sense, a, b) is the distance along the perimeter in the sense direction

## Slide 6: Special case 1 – complete circle
start and end
via arc 2
Via Encoding
Start = polyline[0]
Via 1 = polyline[1]
Via 2 = polyline[2]
End = polyline[3]
Radius = distance (center (start, via 1, via 2)
Center = center (start, via 1, via 2)
Sense = pdistance (sense, start, via 1) <
pdistance (sense, via 2, end)
via arc 1
start and end
ccw circle
via arc 1
via arc 2
cw circle

## Slide 7: Special case 2 - Helix
A via helix is an arc or complete circle where the z coordinate increases or decreases.
The increasing or decreasing z coordinate is in the coordinate system defined by the axis of the arc/circle.
If there is more than one via_helix point then the z coordinate of each must be on the helix
ENTITY via_helix SUBTYPE_OF (cartesian_point);

## Slide 8: Rules
The first and last points of a polyline cannot be via’s.
If two consecutive points are via’s then they must be of the same type (arc or helix) and be on the same arc
A via cannot have the same coordinates as the preceding or following point.
It is illegal for a single via to separate two regular points that are coincident.

## Slide 9: Measurements
Measurements made for: Bordeaux_20080116.238
  A high speed machining file for the fish head
  Contains part geometry, tolerances and tool paths
Using Bounded Curve encoding
  1,938 K bytes
If arc’s are converted to lines (semantic loss)
  647 K bytes
If arc’s are converted to via’s to preserve semantics
  1,019 K bytes
For reference for same file
  3,514 K bytes Mastercam 9 (MC9)
  574 K bytes ISO 6983 (Heidenhain)