## Slide 1: STEP-NC Explorer
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Making and Viewing Tolerances

## Slide 2: View All Part Tolerances
Part Property Tab Shows All Tolerance and Surface Finishes
Click each one to blink tolerance faces
Highlight datum surfaces

## Slide 3: Defining a Datum on the Part
Select the Probing | Define Datums menu entry to bring up the datum dialog box.

## Slide 4: Pick The Datum Face
Pick the face in the geometry window
Select appropriate datum options
Switch between rotate, pan, and pick modes as needed

## Slide 5: Defining a Tolerance on the Part
Select the Probing | Define Tolerance menu entry to bring up the tolerance dialog.
Pick tolerance or dimension type from the list

## Slide 6: Pick The Tolerance Face
Pick the face in the geometry window
Set value and any options
Switch between rotate, pan, and pick modes as needed

## Slide 7: Create Linear Dimension
When creating a linear dimension, you must pick two faces from the model.
Icon shows which face is being selected.
Click on other “Use” button to switch

## Slide 8: Save as STEP-NC or AP203e2
Save as STEP-NC AP238 using File | Save
Save as AP203e2 using File | Export | Workpiece

## Slide 9: Read STEP-NC or AP203e2
Read a STEP-NC AP238 file using File | Open
To read AP203e2, create a project (File | New)
Then import the AP203e2 (File | Import | Workpiece)