## Slide 1: STEP-NC a new language for the CNC
Martin Hardwick
STEP Tools, Inc.
hardwick@steptools.com
518 687-2848 x 306

## Slide 2: The STEP-NC Concept
New programming paradigm for the CNC
  Workingsteps apply operations to features
  Tool paths are machine independent
  Tolerances enable measurement and automated correction on the CNC
STEP-NC XML
AB Tool Tilt
BC Table Tilt

## Slide 3: STEP-NC Model
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 4: Business Benefits
Supply chain interoperability
Real time simulation and verification
Integrated CMM and CNC
Automated cutter compensation

## Slide 5: New features since Dallas
Import and export of AP-203 e2 files containing tolerance data
Automated assembly and disassembly of data for integrated data management
Integration with ISO 13399 for physical tool parameters
Automated computation of tool compensation offsets using tolerance measurements
Data compression using via points
Material removal simulation
Feed/Speed optimization

## Slide 6: International Testing
AP-203
File
AP-238
File
Geometry
Toolpaths, Feeds and Speeds
Machine and
Measure
Path 2 Direct Translation
For Videos see
http://www.steptools.com/library/
stepnc

## Slide 7: Five Axis machining

## Slide 8: 3 Axis Machining

## Slide 9: Turning

## Slide 10: Measurement
Rib Profile
Dull corner
Hole size

## Slide 11: Data Sources
APT
  CATIA
  UGS
  Pro/E
Mastercam 9 & X2
SCRA (AP-224)
RS274D
  Haas
  Fanuc
  Siemens
  MDSI
  Okuma
  Heidenhain
CAD
CAM
CNC
STEP-NC
AP-238
XML File
PDM

## Slide 12: Implementation
CAD
CAM
CNC
STEP-NC dll
APT
Query
Process
Finder
Design
Plan
Machine
AP-203 e2
AP-238
Information flow
Function call to an interface in the dll
AP-203
File
AP-224
File
AP-238
File
ST-Machine®
CAD
Planning
Machining