## Slide 1: CNC VIRTUAL MACHINE – LOGGING ABSTRACTION LAYER
February 26, 2008

## Slide 2: OPC Integrated with CNC Machining
Today, Ole for Process Control (OPC) has emerged as a leading worldwide specification in enabling connectivity and interoperability of factory floor equipment.
Notes: Legacy OPC leverages the Microsoft Component Object Model (COM) to specify OPC COM objects and their interfaces. OPC Unified Architecture is Web-friendly, vendor-neutral.
Quickly DRILL DOWN on OPC.
OPC is a series of integration standards defined as interface specifications to support connectivity in industrial automation and the enterprise systems. OPC handles integration by creating a “software bus” so that applications need only know the data required from OPC data sources, not how to get it. This has benefits for both the application developers and the control vendors. On the application side, control device are easier to use since they provide a consistent interface so that applications are smaller and simpler to develop and maintain. On the control vendor side, device drivers are only required to provide data in a single format, according to the OPC specifications.
The OPC interfaces always return the process data in a VARIANT. It is assumed that the server has a ‘native’ or ‘prefered’ datatype which is also known as the canonical datatype (e.g. real or string).
XML

## Slide 3: CNC OPC Tag Naming & Mapping
OPC does not define any application item tag names , e.g., Axis.Velocity
OMAC HMI Working Group has defined a list of CNC-related OPC tags.
  Object oriented attained by tag naming strategy – using slash or period – Axis.Label, Axis.Position
Comparison of Commercial CNC OPC tag collections has been done at NIST against OMAC tags
  There are some gaps which we hope to identify
Source: www.isd.mel.nist.gov/projects/omachmi/OMAC2OPCVariableMapping.doc
Notes: OPC does not define any application item tag names , e . g . AxisLocation
Object oriented or hierarchical naming using slash or period Axis.Label, etc.

## Slide 4: “Data Logging” CNC VM
The predominant Computer Numeric Control (CNC) machine tool programming language is RS274.
Most CNCs have their own programming language extension to RS274 known as User Macros or Subprograms
Subprograms and Macros provide a layer of programming abstraction on top of the CNC or Virtual Machine.
Data Logging virtual machine will be specified as a set of Subprogram calls that are implemented in the Native CNC RS274 dialect.

## Slide 5: “Data Logging” CNC VM Process
CNC with an OPC server will be required to provide OPC tagged data. MT-Connect might work.
Data Logging OPC client is a separate application running in the background of the CNC computer or a remote computer. You specify a Data list that you wish to collect from the CNC. When one or more values change in the data list, the CNC OPC server will notify the OPC Client of the changes and the OPC Client can reads these values.
Data Handler component is required to manipulate the data according to a given configuration.
  For a more concise data logging scenario, you need to configure the options of the data collection by defining a Filter. The default filter is to log all the data items whenever one or more of the data item change.
  The Formatter provides support for saving the log to a Destination, such as Persistent Data Store, in some common data collection and analysis format. Typical formats include None, Text, Comma Separated values (CSV), XML, or data base.
Data Analysis can generate reports, fine tune or trouble shoot machining performance, or tie-in directly to the CNC and provide safeguarding machining operations – such as machine halting or feed rate override reduction should analysis reveal a problem.
Notes:   Supporting a limited number of import/export file formats with broad industry support has been deemed preferable to having a separate language to describe formatting and analysis of the data. The None format allows data logging without physical file saving to allow monitoring for potential machine faults.

## Slide 6: Data Logging Mantra
machining data collection for early detection and prevention of defects or quality loss.
  Part quality is paramount to machining. Defective parts translate to lost revenue or lost customers. To maintain part quality, the inspection process measures parts against specified tolerances for quality assurance. Even if the inspection process finds an out-of-tolerance defect in a part, remedial action can be difficult, and is akin to finding a needle in a haystack as to cause of the toleration deviation. Instead, a more proactive approach with continuous on-line data monitoring of the part machining is desirable.

## Slide 7: Data Logging Mantra
Data Analysis can generate reports, fine tune or trouble shoot machining performance, or tie-in directly to the CNC and provide safeguarding machining operations – such as machine halting or feed rate override reduction should analysis reveal a problem.
Logging done over time and stored in an archival Data Base can provide historical perspective for trending or regression analysis.

## Slide 8: Method 1- WS enumeration with filtering
AddDataItem(NAME , FILTERTYPE, value1, value2)
where the arguments include:
NAME could be one of the following:
Axis[1..n]
AxisLoad[1..n]
ActualFeedrate
ActualSpindleSpeed
CmdFeedrate
CmdSpindleSpeed
SpindlePower
State
Mode
ProgramName
Block
LineNumber
FollowingError[1..n]
FILTERTYPE could be one of the following:
DEADBAND logs only if changes between values is greater than value1
THRESHOLDlogs only if abs(value) > value1RANGElogs if value in [value1 , value2] range
DEPENDENT unmonitored, logs only if other values change
EQUALITY supervisory, logs only if value equals value1
INEQUALITY supervisory, logs only if value not equal to value1
StartLogging(INT type, STRING filename)
where the arguments include:
type – defines the type of archival destination for the captured data, either NONE, TXT(text file), CSV (csv file), or (DB) data base.
filename – defines the archival destination file name
Problem here is enumerating list of all potential data items. Possible solutions, use categories of data logging: axis position, axis dynamics, axis servo, program.

## Slide 9: Method2 - WS delegates to ini & scripting files
StartLogging(INT type,
STRING filename,
STRING datalist,
STRING filter)
where the arguments include:
  type – defines the type of archival destination for the captured data, either NONE, TXT(text file), CSV (csv file), or (DB) data base.
  filename – defines the archival destination file name
  datalist – filename specifying data to be captured
  filter – filename of filter to apply to data
Example:
StartLogging(“CVS”, “PartA”, “DataItems”, “”)

## Slide 10: Method2 - WS delegates to ini
Ini File
  PARTPROGRAM=/Channel/ProgramInfo/progName
  LINENUMBER=/Channel/ProgramInfo/actLineNumber
  FEEDRATE=/Channel/State/cmdFeedRateIpo
  RPM= /Channel/Spindle/cmdSpeed[1]
  X=/Channel/MachineAxis/actToolBasePos[1]
  Y=/Channel/MachineAxis/actToolBasePos[2]
  Z=/Channel/MachineAxis/actToolBasePos[3]
  SPINDLELOAD=/Channel/Spindle/driveLoad[1]

## Slide 11: Method2 - WS delegates to script
#Deadbanding Script Example
Var X, Y, Z;
Var Xlast, Ylast, Zlast;
X= GetOPCVariable("X");
Y= GetOPCVariable("Y");
Z= GetOPCVariable("Z");
if(fabs(X-Xlast) > 0.01)
{
Xlast=X;
Save();
}
if(fabs(Y-Ylast) > 0.01)
{
Ylast=Y;
Save();
}
if(fabs(Z-Zlast) > 0.01)
{
Zlast=Z;
Save();
}
problem here is defining a scripting language. Hides listing all potential data problem

## Slide 12: OPC-840 Synchronization – HOW?
Issues: synchronization of CNC and other applications
Solution:
  Write Msg(“StartLogging”)
  Run StartLogging Subprogram that DWELLS for 1 seconds.
  Write to OPC user area – none found for 840D. Lack of OPC scratchpad or personal area for external communication

## Slide 13: Questions?