## Slide 1: STEP-NC
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
A new language for the CNC

## Slide 2: The STEP-NC Concept
  Workingsteps apply operations to features
  Tool paths are machine independent
  Measurement and correction on the CNC
STEP-NC XML
AB Tool Tilt
BC Table Tilt

## Slide 3: STEP-NC Model
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 4: Business Benefits
Supply chain interoperability
Real time simulation and verification
Integrated CMM and CNC
Automated cutter compensation

## Slide 5: New features since Dallas
Import and export of AP-203 e2 files containing tolerance data
Automated assembly and disassembly of data for integrated data management
Integration with ISO 13399 for physical tool parameters
Automated computation of tool compensation offsets using tolerance measurements
Data compression using via points
Material removal simulation
Feed/Speed optimization

## Slide 6: View All Part Tolerances
Part Property Tab Shows All Tolerance and Surface Finishes
Click each one to blink tolerance faces
Highlight datum surfaces

## Slide 7: Defining a Datum on the Part
Select the Probing | Define Datums menu entry to bring up the datum dialog box.

## Slide 8: Pick The Datum Face
Pick the face in the geometry window
Select appropriate datum options
Switch between rotate, pan, and pick modes as needed

## Slide 9: Defining a Tolerance on the Part
Select the Probing | Define Tolerance menu entry to bring up the tolerance dialog.
Pick tolerance or dimension type from the list

## Slide 10: Pick The Tolerance Face
Pick the face in the geometry window
Set value and any options
Switch between rotate, pan, and pick modes as needed

## Slide 11: Create Linear Dimension
When creating a linear dimension, you must pick two faces from the model.
Icon shows which face is being selected.
Click on other “Use” button to switch

## Slide 12: Save as STEP-NC or AP203e2
Save as STEP-NC AP238 using File | Save
Save as AP203e2 using File | Export | Workpiece

## Slide 13: Automated Assembly
Fixture.stp
Blank.stp
Workpiece.stp
Tool.stp
CAD
Systems
Import
Export
CAM
Systems
STEP-NC
DLL
AP-238 cc1
File
Assembly
Script
Export
AP-238 cc4
File
Read
Write
Read
Write
Directory

## Slide 14: Integration with ISO 13399

## Slide 15: ISO 13399 attributes for tool

## Slide 16: Tool compensation corrections
Correction of 2mm fixes the 18 (20mm) error
Correction of 3mm fixes the 18 (20) mm error and the 5 (4) mm errror

## Slide 17: Tool offsets
Tool T2 affects one linear tolerance
Tool T1 affects two linear tolerances
The Tool property pane shows the tool wear compensation values programmed for each tool

## Slide 18: Correcting the tolerances
Distance tolerance measures can be stacked
  We can correct the depths of face 1 and face 2
  We need to make both faces in tolerance
  We need to correct face 1 then face 2
18 +0.1 -0.2
5 +0.05 -0.01
Top
hole
counter
bore
machined face 1
machined face 2

## Slide 19: Using tool compensation
Define the tolerances on the part
Define which workingsteps are machining each face
The STEP-NC DLL then
  Determines the tools responsible for each tolerance
  Determines an order for computing the compensations
  Recommends a best value for each correction
  Lets the user accept or modify each value

## Slide 20: Picking faces to features
Algorithm finds closest faces using path geometry
CAM system writes face data to STEP-NC file
Or user picks

## Slide 21: Measurements
Measurements made for: Bordeaux_20080116.238
  A high speed machining file for the fish head
  Contains part geometry, tolerances and tool paths
Using Bounded Curve encoding
  1,938 K bytes
If arc’s are converted to lines (semantic loss)
  647 K bytes
If arc’s are converted to via’s to preserve semantics
  1,019 K bytes
For reference for same file
  3,514 K bytes Mastercam 9 (MC9)
  574 K bytes ISO 6983 (Heidenhain)

## Slide 22: Simulator

## Slide 23: Feed Speed Optimization
Vericut
Boeing
code
CVS
File
STEP
Merge
process
Fishead
AP-238
Enhanced
Fishead
AP-238
STEP CNC
Converter
Boeing
Optimization
Algorithms
Optimized
Machine
Program
G-code
& STL/STEP models
STEP CNC
Converter
Today’s machining conditions
Interface
1
2
3
4

## Slide 24: New Feed Speed Optimization
Ordinary
Fishead
AP-238
STEP CNC
Converter
Customer
Optimization
Algorithms
Optimized
Machine
Program
Today’s machining requirements (schedule)
Interface
New simulator converts cross section area
Cutting parameters taken from tool database
ISO 13399
Tool Database

## Slide 25: Conclusion
Benefits of STEP-NC are becoming clear
Feed/Speed Optimization
  Time saved * cost of machining per hour
  Tool life increase * cost of cutting tools
Closed loop programming
  Time to program part * cost of programming
Real time verification
  Number of crashed detected * (cost of repairs + cost of scrap)
Supply chain interoperability
  Time to create new CAM program * number of programs that can be reused