## Slide 1: Parameters Used in Machining Optimization (Draft 1)
Leon Xu
The Boeing Company
December 20, 2007

## Slide 2: Unit
Unit (a flag, indicating metric or empirical)
  If in metric, all dimensions will be in mm, feed rate will be in mm/min, bending moment will be in Nm, and power will be in kW.
  If in empirical, all dimensions will be in inch, feed rate will be in inch/min, bending moment will be in lbf-inch, and power will be in hp.

## Slide 3: Milling Cutter Parameters (1)
Tool number (an integer number, called by the program at tool change)
Tool name (a text string)

## Slide 4: Milling Cutter Parameters (2)
Diameter at flutes
Set length (or gage length, cutter tip to gage line)
Number of flutes
Flute length
Helix angle
Corner radius

## Slide 5: Milling Cutter Parameters (3)
Shank diameter
Shank length
Holder diameter (average)
Holder length
Use set-screw(s) (a flag)
Set-screw distance (from the center of the first set-screw to the tip of the holder)

## Slide 6: Milling Cutter Parameters (4)
Insert-type cutter (a flag to differentiate from solid cutters)
Insert edge length
Insert edge helix angle
Insert overlap (in axial direction)

## Slide 7: Milling Cutter Parameters (5)
Cutting edge material (an integer variable (or a formatted text string) to represent High Speed Steel, Carbide, etc.)
Body material (an integer variable (or a formatted text string) to represent High Speed Steel, Carbide, etc.)

## Slide 8: Milling Cutter Parameters (6)
Maximum allowed rotational speed
Maximum allowed surface speed (also depending on the workpiece material and cutting fluid)
Maximum allowed chip load (feed per tooth, also depending on the workpiece material)
Maximum allowed deflection (also depending on the dimensional requirement of the part and the process)

## Slide 9: Example of a Milling Cutter

## Slide 10: Example of an Insert Type Cutter

## Slide 11: Machine Constraint Parameters (1)
Spindle maximum rotational speed
Spindle power (a power vs. speed curve, or a single value from the curve if the spindle rotational speed is determined)
Maximum bending moment allowed at the gage line
Maximum feed rate

## Slide 12: Machine Constraint Parameters (2)
Maximum allowed radial force to the spindle front bearing(s)
Maximum allowed axial force to the spindle front bearing(s)
Distance from the spindle front bearing(s) to the spindle gage line
Distance between the front bearing(s) and the rear bearing(s)

## Slide 13: Example of Power vs. Speed Curve

## Slide 14: Process Parameters (1)
Optimization mode (an integer for selecting a optimization formula, such as cutting force, tool life or other user defined formulas)
An integer identification number for each cutting path or segment

## Slide 15: Process Parameters (2)
Spindle speed selection (a flag, using the originally programmed speed or assigning a new speed)
Assigned spindle speed
Maximum allowed feed rate for the process
Lowest feed rate to be optimized (feed rate below this value will not be optimized)
Highest feed rate to be optimized (feed rate above this value will not be optimized)

## Slide 16: Process Parameters (3)
“Air cutting” feed rate selection (a flag for selecting the programmed or the maximum allowed feed rate)
Ramping option (a flag, whether to optimize a path (segment) if the ramping angle reaches a predefined limit)
Ramping angle limit

## Slide 17: Workpiece Material
A formatted text string
(It refers to the workpiece material cutting property. See note below)

## Slide 18: Note: Material Cutting Property
Generally related, but different than the material physical properties (yield strength, etc)
Influenced by the cutting edge geometry and material
Often obtained from laboratory tests for a given cutting edge/workpiece combination
No industry standard for definitions, formulas and formats of cutting property