## Slide 1
TRACEABILITY INTRODUCTION
Julio Garrido Campos & the ISO SC4/WG3/T24 group
jgarri@uvigo.es
University of Vigo (Spain)
Monday, 10 – Tuesday, 11, March at Sandviken, Sweden
ISO TC184/SC4 WG3/T24 STEP-Manufacturing, Spring 2008 Meeting

## Slide 2
Traceability.
  What is Traceability?
  For what is it implemented?
  How is it performed (activities)?
  How must be implemented (some implementation issues)?
  Why Traceability in AP238?
Traceability requirements for AP-238 (some ones).
Current status of the Traceability proposal for AP-238.
  Traceability nc_Functions as SC4 Dallas meeting.
    The AP-238 executable Unit of Functionality and nc-functions.
    Proposal: Traceability nc-functions.
    How the Traceability nc-functions work: an example.
  Some discussions & progress since SC4 Dallas meeting.
    New data types for recorded data.
    Redefinition of Block I functions.
    Other comments.

## Slide 3
What is Traceability?
  The objective of Manufacturing Traceability is to provide all the relevant information about a manufacturing process.
  Which Data?
    With what and where has been manufactured a piece? raw material, coolant, tools, machine, software.
    How/how well? Tool paths, toll paths deviations, actual velocities, control events.
    Who? Operator
    When? manufacturing timings.
AP-238
File
CNC
System
with
Traceability
Traced
Data
Traced
Data
Traced
Data
parts
1. Traceability.

## Slide 4
For What?
  For Quality analysis (and long term data analysis)
    To be able to investigate the origin of a manufacturing default (TRACE). To answer questions like: Why this feature is not ok?
    To be able to identify other pieces with the same fault (TRACK). To answer questions like: Which other pieces may have also the same default and should be review?
X
Tracing
X
X
Tracking
1. Traceability.

## Slide 5
For What?
  For knowledge capture and optimization (for re-design and re-planning)
      To answer questions like: How log does it take to machine this feature?
Trace
Data
finished part
AP-203
AP-224
AP-238
CAD/CADD
CAM
CNC
CAPP
AP-240
Re-design
Re-planning
For What?
  To provide data for advanced “manufacturing” services.
    Programmed Monitoring.
    Intelligent manufacturing.
1. Traceability.

## Slide 6
How is it performed (activities)?
  Before manufacturing (Design phase).
    Definition/Configuration of what to trace, where, how.
  During Manufacturing (Shop floor phase).
    Data recording process (shop floor).
    establishment of the link between the traced data and the piece.
  After Manufacturing (Quality and re-design phase)
    Data communication.
    Data storage
    Data analysis, etc.
1. Traceability.

## Slide 7
Activity Model, 3 main activities:
Traceability
Configuration
Activity A01
Data acquisition
A02
Analyze
Data
A03
Traceability
Specifications
Traceability
Set-Up
Traceability Data
Traceability Audit
Traceability
Collected
Data
Before Manufacturing
(design phase)
While Manufacturing
(shop floor phase)
After Manufacturing
(inspection, re-design, re-planning)
1. Traceability.

## Slide 8
Why Traceability in AP-238?
  A- Many relevant data is just know by the process controller, so it has to provide this data.
  The CNC controller knows much of this data. The HMI+CNC controller knows all the data.
  B- In Client-supplier relationships, traceability data has to be understandable, trustable…
    Understandable. In terms of format and meaning.
      The contractor has to understand the requirements with out doubts.
      The client has to understand the data by its own.
    Trustable.
      There shouldn’t be doubts about the recording process.
      Traceability activities must be performed as much automatically as possible (to guarantee there is no errors)
  Traceability DATA (requirements & results) should be standard & automatically understood:
    Automatically understood by controller.
    Understood by the analysis system (linked to an understandable specification of the machining process).
1. Traceability.

## Slide 9
“Some” Traceability requirements for AP-238.
INPUTS
  Based on STEP AP238
  Machine independent
  Based on customer requirements
  Enable last minute adaptation
  Done once
OUTPUT is an extract from internally collected data according to requirements
  As required by customer.
    Probing
    Quality insurance
  As required for shop floor management: for scheduling, MES, maintenance, …
    Scheduling, durations
    Warnings and alarms,
    Corrective actions,
  Enables traceability, archiving and SPC.
    Administrative data
    On machine measurement data
    Quality stamp
  Enable knowledge capture and optimisation.
  Format “standard”.
1. Traceability.
CNC
Traceability

## Slide 10
“Some” Traceability requirements for AP-238: DATA.
1. Traceability.
Data internally required (to be used on real-time):
  For drive control
    Data used to compute and monitor the tool path
  For HMI
    Data to be displayed on controller screen
    According to mode: automatic, manual, maintenance,
    Safety and environment security
    Knowledge capture
  For shop floor, workcell management and maintenance
    Links with inventory, tools, pallets, calibration,
    Tools wear
    Resources and energy consumption
Data to Trace (data commonly saved in log blocks)
  Data for traceability is an extract of data collected during machining. Export is done after machining; this is to speed up the execution.
  Trace of the program is saved for further execution including manual override and/or on line computations (for instance: F & S instead of input data AD, RD,….)
  Specific data to be collected and conditions for capture are a global and/or default commands. This will decrease the size and improve readability.
    data from the log books, workingstep data
  Data locally collected during execution
    Measures, Test condition true or false

## Slide 11
Current status of the Traceability proposal for AP-238.
  2. Traceability NC-Functions as SC4 Dallas meeting (October 2007).
    The AP-238 executable Unit of Functionality and nc-functions.
    Proposal: Traceability nc-functions.
    How the Traceability nc-functions work: an example.
  3. Progress since SC4 Dallas meeting.
    New data types for recorded data.
    Redefinition of Block I functions.
    NIST proposals.
    Other comments.
    Open issues.
2. Proposal: nc-functions as SC4 Dallas.

## Slide 12
Executable model (AP-238).
(ABS) Program structure: Control flow for the machining program.
(ABS) workingsteps: Program Steps that move the machine axes
(ABS) nc_functions: Program steps that do not move the machine axes.
2. Proposal: nc-functions as SC4 Dallas.

## Slide 13
Program
Steps
that do not move
the machine Axes
Program
Steps
That move
The machine Axes
Control
Flow
For the machining
Program
AP 238: Adding Traceability NC-Functions
(ABS) executable
(ABS)
PROGRAM STRUCTURE
(ABS) NC_funtions
(ABS) WorkingSteps
Machinning_workingsteps
Rapid_movement
Touch_probing
WORKPLAN
parallel
If_statement
while_statement
Display_message
Program_Stop
NEW
Traceability nc_functions
2. Proposal : nc-functions as SC4 Dallas.

## Slide 14
Three Groups of Functions for data traceability:
  Group I:
    Blocking Functions, take control of the program, collect a punctual or single value of data to be used in CNC calculations and return control to machining flow.
  Group II:
    Switching Functions, activate data collection or event information for a period of time. A switching on functions activates the data monitoring until the corresponding switching off functions id found in the program.
  Group III:
    Synchronous Functions, continuously monitor data to trigger if a condition is fulfilled a series of actions grouped as a workplan.
(ABS) nc_function
Single Value traceability
functions (BLOCK I)
switching (on/off)
functions (BLOCK II)
synchronous
switching (on/off)
functions
(With action)(BLOCK III)
2. Proposal: nc-functions as SC4 Dallas.

## Slide 15
Group I Functions.
get_time
get_operator_id
get_x_position
get_y_position
get_z_position
(ABS) nc_function
nc_variable
One Value Is Returned !
2. Proposal: nc-functions as SC4 Dallas.

## Slide 16
Program Sample with Group I Functions.
2. Proposal: nc-functions as SC4 Dallas.

## Slide 17
Group II & III Functions.
(ABS) nc_function
start_measuring_maximum_deviation_position_along_toolpath
stop_measuring_maximum_deviation_position_along_toolpath
Results_
data
maximum deviation values L[0:?]
Its_threshold_value
Its_actions
measured_for
measured_results
length_measure
workplan
Bounded_curve
toolpath
Bounded Amount of Values
Returned following the same
Toolpath Parametrization !
2. Proposal: nc-functions as SC4 Dallas.
maximum_deviation_values L[0:?] is used to store in AP-238 a bounded curve, series of collected values (per toolpath and following the same parametrization as the corresponding workingstep toolpath).
its_threshold_value is used only if nc_function acts as a group III function to specify a threshold value for the comparing/triggering condition.
its_actions is an alternative workplan (a series of actions) to be done in case the specified condition is fulfilled (just for group III).

## Slide 18
Program Sample with Group II.
2. Proposal: nc-functions as SC4 Dallas.

## Slide 19
Program Sample with Group III Functions.
2. Proposal: nc-functions as SC4 Dallas.

## Slide 20
Complete Ap-238 nc-Functions Model.
Group II & III
NC_Functions
Group I
NC_Functions
2. Proposal: nc-functions as SC4 Dallas.

## Slide 21
How nc_functions Work?
Configuration: requirements are translated into nc_functions in the AP238 executable.
nc_functions are automatically executed when they are found in the executable sequence.
  2.1 Data can support run-time.
  2.2 Data can be logged when machining finish
Logged data is used.
2. Proposal: nc-functions as SC4 Dallas.
1.
2.1
2.2
3.

## Slide 22
How the Traceability nc_functions work: An example.
  1. Traceability requirements are specified by inserting nc_functions in the executable sequence
Configure
A01
Acquisition A02
Analyze A03
2. Proposal: nc-functions as SC4 Dallas.

## Slide 23
Configure
A01
Acquisition A02
Analyze
A03
2. Proposal: nc-functions as SC4 Dallas.
How the Traceability nc_functions work: An example.
2. Accessing the Data while machining:
  2.1 With Current Technology:
    nc_functions have to be translated to G&M codes. Limitations: current CNC resources (Memory, file access mechanism, etc).
    Through the HMI interface (Accessing to the PLC internal variables with, for instance OPC communication) (Experiments at NIST)
  2.2 With a AP-238 controller (TODAY, Simulation): The controller access its internal variables, computes the values, stores in memory. When mechanization ends (or when cycles ends), its writes the values to a file.
N100 $AC_TIMER[1] = 0 …
;RESET R[] variables
;R[1] WILL Hold the threshold value
..........
;START SINCHRONYZED ACTION threshold set for each segment
ID=1 WHEN $R[1] < $AC_TIMER[1] DO (ACTION: stop, alarm .. log data)
G1….
WRITE(“ERROR”,”LOGFILE”,”SEGMENT 1 TIME: “ << $AC_TIMER[1]);
$AC_TIMER[1]= 0 ;
G1…
WRITE(“ERROR”,”LOGFILE”,”SEGMENT 1 TIME: “ << $AC_TIMER[1]);
$AC_TIMER[1]= 0 ;
G1…
………
CANCEL(1)

## Slide 24
How the Traceability nc_functions work: An example.
3. Review of Logged Data.
Configure
A01
Acquisition A02
Analyze
A03
2. Proposal: nc-functions as SC4 Dallas.

## Slide 25
  Logged Data FORMAT: a new conformance class to define the traceability data structure.
    In this conformance class there will be workplans, workingsteps and tool paths. However, the toolpaths will trace the results of running the program. For example, there might be a curve describing the measured x, y z deviations, a curve describing the spindle power consumption, etc.
3. Proposal: Progress since SC4 Dallas meeting.

## Slide 26
  Block I nc_functions:
    Block I nf_functions more like Block II: Most Block I nc_function will become as block II to store data in the same way.
      Nc_fucntion to star/stop getting execution times of toolpaths.
      Nc_fucntion to star/stop getting (along toolpath): operators involved.
      Nc_fucntion to star/stop getting (along toolpath): manual override intervention.
      Nc_fucntion to star/stop getting (along toolpath):
        Used tools Identification.
        Used machines identification?.
    Still, may be some Block I nc_functions returning single values. But nc_variables are too week. Need to define data types to hold the data values.
        Administrative data? Machine software version? Etc…
  More Block II nc_functions needed for advanced services (speed control optimization, ….)
  An open mechanism to define new coming sensor/variables values as they will come in the future?
    Start_monitoring_sensor_data_along_toolpath…..IS IT OK?
3. Proposal: Progress since SC4 Dallas meeting.

## Slide 27
Conclusions.
  NC-Functions seems to be a good mechanism.
  To log data as standard format has to be defined a new Unit of functionality.
  Implementation Issues:
    Current technology is able to perform all proposed Nc-functions? some of them?
    Are there enough data types? We need more?
Thank you for your attention
4. End.