## Slide 1: STEP-NC Explorer
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Determining a resolution order for Linear Distance Tolerances

## Slide 2: Tolerances in AP-238
The Part Properties pane shows the tolerances defined on the part in CAD.
Tolerances defined for the workpiece
Toleranced faces are highlighted
Rawpiece and fixture can be toleranced

## Slide 3: Machining in AP-238
The workplan pane shows the faces machined by each tool path
Workingstep one selected
Cutting tool for workingstep one
Face being machined

## Slide 4: Tool offsets
Tool T2 affects one linear tolerance
Tool T1 affects two linear tolerances
The Tool property pane shows the tool wear compensation values programmed for each tool

## Slide 5: Correcting the tolerances
Distance tolerance measures can be stacked
  We can correct the depths of face 1 and face 2
  We need to make both faces in tolerance
  We need to correct face 1 then face 2
18 +0.1 -0.2
5 +0.05 -0.01
Top
hole
counter
bore
machined face 1
machined face 2

## Slide 6: How – 1 Associate faces to features
Algorithm finds closest faces using path geometry
CAM system writes face data to STEP-NC file
Or user picks

## Slide 7: 2. Associate tolerances to operations
Tool 1 machines one face of this tolerance
And Tool 1 machines one face of this tolerance
And Tool 2 machines the other face of this tolerance

## Slide 8: 3. Tolerances affected by each tool
Linear distance 18 +0.1 – 0.2mm
Measured value = 20mm
Linear distance 5 +0.05 – 0.01mm
Measured value = 4mm

## Slide 9: 4. Corrections to offsets
Correction of 2mm fixes the 18 (20mm) error
Correction of 3mm fixes the 18 (20) mm error and the 5 (4) mm errror

## Slide 10: General Solution
Phase 1 determine association between machining features and design tolerances.
Phase 2 determine an ordering for tolerance correction (tolerance stack).
Phase 3 recommend a best new value for each offset.
Phase 4 allow the user to fine tune the recommended offsets.
Phase 5 use the new offsets to machine the part.