## Slide 1: Status of White Paper Comparison of ISO 10303-238 to ISO 14649
Fred Proctor
National Institute of Standards & Technology
Notes: Is there a jazzier title for the white paper?
Is the white paper necessarily a pro-AIM view? If so, should the title reflect that? (Though that seems counter to our goal of being objective.)

## Slide 2: Outline
Statement of problem
STEP architecture overview
Advantages of STEP approach
Physical file comparison
Conclusions and recommended actions
Notes: The outline of this presentation follows the outline we’re proposing for the white paper.
I have several slides that describe the STEP architecture and AP development that I can briefly cover if need be, but is a 30-minute presentation by itself.
We have done an analysis of physical file excerpts of the same data represented in ISO 14649 and ISO 10303-238 formats. I’ll explain that effort and show you the results.
I’ll also cover other differences between implementations of 14649 and 10303-238.
Then I’ll present our conclusions and recommendations for short-term actions.

## Slide 3: Statement of Problem
STEP-NC is a standard for representation of CNC data that uses some or all of the representation methods and architecture developed for ISO 10303.
  ISO 14649 uses the EXPRESS language to define a set of NC domain requirements models in terminology familiar to NC experts.
  ISO 10303-238 is a STEP AP that uses the EXPRESS models in ISO 14649 as the domain requirements model with a few modifications then maps them to the STEP integrated resources to obtain the implementation model .
  The primary difference between these two standards is their level of use of the STEP architecture.
Which is better, from an implementer’s viewpoint, to implement the ISO 14649 models directly or to implement the requirements from ISO 14649 as mapped into the STEP integrated resources?
Notes: STEP-NC is a standard for representation of computer numeric control data that uses some or all of the representation methods (EXPRESS, Part 21, etc.) and architecture (AAM, ARM, AIM, IR, etc.) developed for ISO 10303.
ISO 14649 is a family of standards that uses the EXPRESS language to define a set of NC domain requirements models in terminology familiar to NC experts.
ISO 10303-238 is a STEP AP. It uses the EXPRESS model in ISO 14649 as the domain requirements model (called an application reference model, or ARM) with a few modifications then maps it to the STEP integrated resources to obtain the implementation model (application interpreted model, or AIM).
The primary difference between these two standards is their level of use of the STEP architecture.
At issue is whether it is best, from an implementer’s viewpoint to implement the ISO 14649 models directly, or to implement the requirements from ISO 14649 as mapped into the STEP integrated resources.
The white paper will provide a practical comparison of the different approaches and make recommendations on best implementation practices.

## Slide 4: ISO 14649 ISO 10303-238
#22=MILLING_CUTTING_TOOL('DRILL-0.5-2-3‘,#23,(#25),76.2, $,$);
#23=TWIST_DRILL(#24,2,.RIGHT.,.F.,0.);
#24=TOOL_DIMENSION(12.7,31.,0.,55.88,0.,0.,0.);
#25=CUTTING_COMPONENT(0.,#50,$,1000000.,$);
#50=MATERIAL('UNKNOWN','hss',());
Yellow instances define units of measure once and may be reused by other instances that share the same system of units.
#51=PLANE_ANGLE_MEASURE_WITH_UNIT(PLANE_ANGLE_MEASURE(0.01745329252),#495);
#53=(CONVERSION_BASED_UNIT ('DEGREES',#51) NAMED_UNIT(#430) PLANE_ANGLE_UNIT());
#58=SI_UNIT(*,.MILLI.,.METRE.);
#74=MACHINING_TOOL_BODY_ REPRESENTATION('drill',(#416, #417,#418),#500);
#78=RESOURCE_PROPERTY_ REPRESENTATION('','',#82,#74);
#82=RESOURCE_PROPERTY('tool_ body','',#90);
#86=ACTION_RESOURCE_TYPE('cutting tool');
#90=MACHINING_TOOL('TL DRILL-2', '12.7 mm TWIST_DRILL',(#133), #86);
#416=(LENGTH_MEASURE_WITH_UNIT() MEASURE_REPRESENTATION_ITEM() MEASURE_WITH_UNIT(LENGTH_MEASURE(12.7),#58) REPRESENTATION_ ITEM('diameter'));
#417=(LENGTH_MEASURE_WITH_UNIT() MEASURE_REPRESENTATION_ITEM() MEASURE_WITH_UNIT(LENGTH_MEASURE(21.184535069175),#58) REPRESENTATION_ITEM('flute_ length'));
#418=(LENGTH_MEASURE_WITH_UNIT() MEASURE_REPRESENTATION_ITEM() MEASURE_WITH_UNIT(LENGTH_MEASURE(118.),#53) REPRESENTATION_ ITEM('included_angle'));
#430=DIMENSIONAL_EXPONENTS(0.,0.,0.,0.,0.,0.,0.);
#493=(LENGTH_UNIT()NAMED_UNIT(*) SI_UNIT(.MILLI.,.METRE.));
#495=(NAMED_UNIT(*)PLANE_ANGLE_ UNIT()SI_UNIT($,.RADIAN.));
#499=UNCERTAINTY_MEASURE_WITH_ UNIT(LENGTH_MEASURE(1.E-006), #493, 'DISTANCE_ACCURACY_VALUE', 'Maximum model space distance between geometric entities at asserted connectivities');
#500=(GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNCERTAINTY_ ASSIGNED_CONTEXT((#499)) GLOBAL_UNIT_ASSIGNED_CONTEXT((#498,#495,#493)) REPRESENTATION_ CONTEXT('ID1','3D'));
Notes: Here are two ‘equivalent’ sections of Part 21 files based on ISO 14649 and ISO 10303-238. Both represent physical data regarding a 12.7 mm (half-inch) drill.
Martin Hardwick has objected that the AP238 excerpt is inflated. If one set of units is used throughout the file, entities 53, 58, 430, 493, 495, 499 and 500 may be defined once per file and reused for tools, geometry and features. Removing those entities would reduce the count to 9 as compared to the 7 for 14649.
If we go with Martin’s set, we’ll be able to use a more readable font, certainly. IF not, I will split these onto two separate slides so they’ll be readable.

## Slide 5: Physical File Observations
Amount of Data
  5:37 lines (5:18 excluding units setup)
  5:16 instances (5:9 excluding units setup)
Lines of Code
  Programming against the AIM is much more complex! Programmers should rely on reusable code modules
Permissiveness of AIM
  It is possible to refer to things outside the ARM; AIM does not explicitly state that only ARM entities can be referenced
Notes: There are 5 lines of ISO14649 data and 37 lines of AP238 data. So in this example, which is typical, AP238 requires about seven times as much data as ISO14649. If AP 238 data had not been compacted, there would have been 57 lines. Much of the AP238 data is simply identifying units. A fixed set of units is used in ISO14649, so this data is not necessary when ISO14649 is used. The ISO14649 data set has more information than the AP238 data set. The ISO14649 data set gives the following data not given in the AP238 data set. i. handedness of the drill (the ".RIGHT." in #23). ii. the material from which the drill is made (#50). iii. the number_of_teeth, i.e. number of flutes (the "2" in #23). If the ISO14649 data set included this information, it would be significantly longer. This is not a criticism of AP238, which can represent all of this data. The generating system simply chose not to provide it.

## Slide 6: AIM Protects Legacy Data
Two common concerns have the least impact in the long term:
  How many individual bytes does it take up in my file?
  Starting from hello_world.c, how many lines of code do I have to write?
The often ignored, but most important question:
  How am I going to make sure that I can put my data in a safe place and still use it several years from now?
STEP architecture is designed to avoid “fragile base class” types of problems by adding some indirection to the ARM data through property relationships, standard mechanisms for describing measures, units, shapes, and other common components.

## Slide 7
Description
Methods
Part 11
EXPRESS
Language
Reference
Manual
Conformance
Testing
Part 31
General
Concepts
Parts 32-35
Reqs for Test
Labs & Clients
Test Methods
for File & Data
access method
Parts 300+
Abstract Test
Suites
Application Protocols
Parts 200+
Application Interpreted Constructs
Parts 500+
Generic Resources
Parts 41-99
Integrated Resources
Application Resources
Parts 100+
Implementation Methods
Part 21 +
Data Specifications
STEP Architecture Overview
Notes: There are two distinct types of Data specifications.
  context-independent specifications, called Integrated Resources, that are the building blocks of the standard.
  application-context-dependent exchange specifications, called Application Protocols, are developed to satisfy clearly defined industrial information requirements. THESE ARE THE PARTS OF STEP THAT ARE IMPLEMENTED
The other components of the architecture provide the infrastructure of STEP.
Description methods include the SC4-developed information modeling language EXPRESS. Allows computer-sensible standards specifications.
Implementation methods include physical file exchange format and data access language. Data definition is separated from the exchange format and the data access language.
Conformance testing methods provide a built-in basis for assessing conformance of implementations. SC4 standardizes abstract test suites as well as the testing methodology and framework. Standardized test suites promote repeatability and consistency of testing.

## Slide 8: STEP Integrated Resources (IRs): Reusable and Extensible
Conceptual data models represent consensus of data semantics commonly used in product data subject areas or application systems.
A consistent data architecture integrates the set of models into a single, large conceptual schema.
The level of semantic abstraction permits reuse of general ideas within different contexts.
Partitioned to permit extensions and exclusions.
The IRs are not only building blocks, but have a basic structure common to all product data and usable by all applications of product data.
Notes: The Integrated Resources are a consensus semantic structure that spans product data usage and application for all industries.
The Integrated Resources are a single, consistent, semantically non-redundant model.
The Integrated Resources were designed with several principles in mind, primarily reusability and extensibility.
The level of semantic abstraction is is generic enough such that the model can be reused with slightly different interpretations in different contexts. It is thus shareable.
The model is partitioned into small schemas, each with a unique functionality or purpose. This partitioning facilitates management of the model and isolates specific functionality. This enables the model to be extended when additional industrial requirements are identified.
The structure of the IRs is such that there is a “vocabulary” and a “grammar” that is shared by all APs and enables implementations of different APs to “understand” one another.

## Slide 9: STEP Application Protocols (APs): Semantically Rich and Implementable
An Application Protocol represents a measurable and shareable subset of STEP capability that is expressed in the terminology of an specific industry or discipline.
An AP specifies:
  Context: A narrow, well-defined domain and a focus on a specific interface or interfaces will enable the precise identification of information requirements.
  Information requirements: The specification of a collection of concepts and their meaning that are required to perform an activity defines the functionality of an Application Protocol.
  Exchange specification: The Application Protocol specifies the subset of the Integrated Resources, constraints and specializations needed to meet the requirements.
Notes: An AP uses application domain terminology, hence it is understandable to potential users of the AP.
The AP is a measurable subset because it specifies what data structures are allowed in an exchange file and the constraints on that data.
STEP reconciles the requirements for a generic, reusable vocabulary with the semantic richness of industrial applications by defining a particular application context and explaining the meaning and usage of standard data constructs (i.e., product data) within that domain.
An application protocol specifies:
  The context within which the AP is intended to be used.
  The set of user’s information requirements the AP intends to meet.
  The exchange specification that is the selection of building blocks from the IRs, including specialized semantics and additional constraints on the generic constructs.

## Slide 10: Application Protocol Development
Application Activity Model (AAM)
A function model that describes activities within the boundaries established by application context. This is a requirements gathering and scoping mechanism.
Application Reference Model (ARM)
A model that describes the information requirements and constraints for an application domain. The model uses application-specific terminology and rules that are familiar to domain experts.
Application Interpreted Model (AIM)
A model that specifies the STEP data structures that are semantically equivalent to the concepts documented in the ARM and AAM.
Mapping Table
A table that specifies the relationship between concepts in the ARM and constructs in the AIM.
ENTITY company;
address : STRING;
composed_of : SET[1:?] OF department;
END_ENTITY;
ENTITY department;
location : STRING;
staff : SET[1:?] OF employee;
END_ENTITY;
ENTITY employee
SUPERTYPE OF (ONEOF(salaried, hourly));
lastname : STRING;
firstname : STRING;
ssn : INTEGER;
END_ENTITY;
ENTITY hourly
SUBTYPE OF (employee);
rate : REAL;
END_ENTITY;
Notes: The 4 major components of an AP are listed here.
The AAM partially describes the context of the AP. It describes the activities that may be supported by the AP, and serves as a requirements gathering and scoping tool.
The ARM also partially describes the context. It serves as both a requirements discovery mechanism and as a requirements specification mechanism.
The AIM has several functions. It specifies the subset of the IR “vocabulary” used with the AP. It specializes the semantics of the generic data structure and adds constraints, thus providing the exchange specification for the AP.
The mapping table specifies the relationship between the ARM and the AIM. It contains rules and constraints specify the usage of the IRs for the AP. The combination of the AIM and mapping table completely specify the usage of the generic structures for the AP.

## Slide 11: AP-238 in context - STEP-Manufacturing
Equipment Models (AP-2XX)
Inspection Data and Results (AP-219)
Manufacturing Operations (AP-238)
Manufacturing features & tolerances (AP-224)
Geometric Tolerances
(AP-203 ed2)
Nominal
Geometry
(AP-203)
STEP-Manufacturing
Integrates more than
10 Object models
Applications Include:
Engineering collaboration
Supply chain management
Factory automation
Micro-Machining
There are many important relationships between the object models

## Slide 12: Post Processor Benefit
ISO 14649 is a simplified object model
  Many important associations between features, geometry and tolerances are in AP-238 but not in the 14649 model.
  AP-238 can be converted to 14649 using a two stage post
    1. Compute machine specific setup (orientation, origin etc)
    2. Summarize and delete feature and geometry relationships
  However, modifications to setup are limited after the deletion
CAM
Post 1
Post 2
CNC 1
CNC 2
X
Requires significant operator input
for 14649 controllers
AP-238
AP-238
14649
14649
Reading AP-238 directly into the controller is a better solution

## Slide 13: Post Processor Example
14649 is not connected to the solid model geometry
  Careful calculation is required to flip the part
  Software assistance is limited because there is no solid model
AP-238 is connected to the solid model geometry
  Full software assistance so “Point and Click” to flip the part
H
#20 = Pocket (H, D, B, A, C)
#20 = Pocket (H’, D’, X’, Y’, C’)
A
B
C
D
X
Y
Example ISO 14649 of “hand editing” to flip the part
Before
flip
X’
Y’
A’
B’
H’
After
Flip

## Slide 14: Drawing Benefits
ISO 14649 features are not connected to a solid model or design tolerances
  Solid models are allowed as illustrations only
  Cannot show as-is and to-be status of part for an operation
  Cannot replace shop floor drawings
Manufacturing
STEP-NC CNC
Design
STEP
CAD
35% faster
programming
(Lockheed)
50% faster using better machines
(Cincinnati Machine)
CAM
Planning
14649
75% fewer drawings
for shop floor
(Raytheon)

## Slide 15: Programming Benefits
ISO 14649 features are not connected to solid model data
  Either use traditional CAM tools to make the data (no net benefit).
  Or programming benefit is reduced because cannot employ feature recognition tools on data that has been modified by the control.
Manufacturing
STEP-NC CNC
Design
STEP
CAD
25% faster
programming
(from spreadsheet)
50% faster using better machines
(Cincinnati Machine)
CAM
Planning
14649
75% fewer drawings
for shop floor
(Raytheon)
Verbal/Annotated
Feedback

## Slide 16: Spindle Time Benefits
ISO 14649 features are not connected to a solid model
  Therefore, cannot check data on the control
  Therefore, cannot use better machines for smaller jobs
  Therefore, reduced spindle time benefit is eliminated
Manufacturing
STEP-NC CNC
Design
STEP
CAD
25% faster
programming
(from spreadsheet)
0% faster using better machines
CAM
Planning
14649
75% fewer drawings
for shop floor
(Raytheon)
Verbal/Annotated
Feedback
Better = Multi-axis machines

## Slide 17: Conclusions
AP-238 files are more complex, less human-readable, and significantly larger than ISO 14649 files
AP-238 leverages benefits of STEP architecture, it is integrated with other application models
AP-238 carries all the required information from CAD to CAM to CNC
ISO 14649 loses the 3D model information
  Less automated checking for collisions
  Less automated compilation and optimization
  Less portability between machines and systems

## Slide 18: Recommended Actions
Develop STEP-NC AIM to ARM physical file converter and make it publicly accessible.
  This will allow those who do not wish to operate on an AIM file able to do so at no extra cost.
  The process of developing this converter will most certainly flush out issues with both the ARM and AIM models, improving the quality of the standard.

## Slide 19: Back-up Slides
STEP Architecture Overview

## Slide 20
Description
Methods
Part 11
EXPRESS
Language
Reference
Manual
Conformance
Testing
Part 31
General
Concepts
Parts 32-35
Reqs for Test
Labs & Clients
Test Methods
for File & Data
access method
Parts 300+
Abstract Test
Suites
Application Protocols
Parts 200+
Application Interpreted Constructs
Parts 500+
Generic Resources
Parts 41-99
Integrated Resources
Application Resources
Parts 100+
Implementation Methods
Part 21 +
Data Specifications
STEP Architecture Overview
Notes: There are two distinct types of Data specifications.
  context-independent specifications, called Integrated Resources, that are the building blocks of the standard.
  application-context-dependent exchange specifications, called Application Protocols, are developed to satisfy clearly defined industrial information requirements. THESE ARE THE PARTS OF STEP THAT ARE IMPLEMENTED
The other components of the architecture provide the infrastructure of STEP.
Description methods include the SC4-developed information modeling language EXPRESS. Allows computer-sensible standards specifications.
Implementation methods include physical file exchange format and data access language. Data definition is separated from the exchange format and the data access language.
Conformance testing methods provide a built-in basis for assessing conformance of implementations. SC4 standardizes abstract test suites as well as the testing methodology and framework. Standardized test suites promote repeatability and consistency of testing.

## Slide 21: STEP Integrated Resources (IRs): Reusable and Extensible
Conceptual data models represent consensus of data semantics commonly used in product data subject areas or application systems.
A consistent data architecture integrates the set of models into a single, large conceptual schema.
The level of semantic abstraction permits reuse of general ideas within different contexts.
Partitioned to permit extensions and exclusions.
The IRs are not only building blocks, but have a basic structure common to all product data and usable by all applications of product data.
Notes: The Integrated Resources are a consensus semantic structure that spans product data usage and application for all industries.
The Integrated Resources are a single, consistent, semantically non-redundant model.
The Integrated Resources were designed with several principles in mind, primarily reusability and extensibility.
The level of semantic abstraction is is generic enough such that the model can be reused with slightly different interpretations in different contexts. It is thus shareable.
The model is partitioned into small schemas, each with a unique functionality or purpose. This partitioning facilitates management of the model and isolates specific functionality. This enables the model to be extended when additional industrial requirements are identified.
The structure of the IRs is such that there is a “vocabulary” and a “grammar” that is shared by all APs and enables implementations of different APs to “understand” one another.

## Slide 22: Integrated Resource EXPRESS Schema
product_
definition_shape
property_
definition
product_definition
description
id
product_definition_
formation
formation
description
*id
product
description
*id
name
product_context
frame_of_reference
discipline_type
application_
context_element
name
application_
context
application
frame_of_reference
(INV) context_elements S[1:?]
product_definition_
context
1
frame_of_reference
property_definition_
representation
shape_definition_
representation
definition
representation
used_representation
name
shape_
representation
representation_item
items S[1:?]
*of_product
Notes: This is an EXPRESS-G diagram of some of the elements of the STEP Integrated Resources. These objects are the most common concepts used in product data applications. Most of these objects and their relationships appear in all APs.

## Slide 23: STEP Application Protocols (APs): Semantically Rich and Implementable
An Application Protocol represents a measurable and shareable subset of STEP capability that is expressed in the terminology of an specific industry or discipline.
An AP specifies:
  Context: A narrow, well-defined domain and a focus on a specific interface or interfaces will enable the precise identification of information requirements.
  Information requirements: The specification of a collection of concepts and their meaning that are required to perform an activity defines the functionality of an Application Protocol.
  Exchange specification: The Application Protocol specifies the subset of the Integrated Resources, constraints and specializations needed to meet the requirements.
Notes: An AP uses application domain terminology, hence it is understandable to potential users of the AP.
The AP is a measurable subset because it specifies what data structures are allowed in an exchange file and the constraints on that data.
STEP reconciles the requirements for a generic, reusable vocabulary with the semantic richness of industrial applications by defining a particular application context and explaining the meaning and usage of standard data constructs (i.e., product data) within that domain.
An application protocol specifies:
  The context within which the AP is intended to be used.
  The set of user’s information requirements the AP intends to meet.
  The exchange specification that is the selection of building blocks from the IRs, including specialized semantics and additional constraints on the generic constructs.

## Slide 24: Application Protocol Development
Application Activity Model (AAM)
A function model that describes activities within the boundaries established by application context. This is a requirements gathering and scoping mechanism.
Application Reference Model (ARM)
A model that describes the information requirements and constraints for an application domain. The model uses application-specific terminology and rules that are familiar to domain experts.
Application Interpreted Model (AIM)
A model that specifies the STEP data structures that are semantically equivalent to the concepts documented in the ARM and AAM.
Mapping Table
A table that specifies the relationship between concepts in the ARM and constructs in the AIM.
ENTITY company;
address : STRING;
composed_of : SET[1:?] OF department;
END_ENTITY;
ENTITY department;
location : STRING;
staff : SET[1:?] OF employee;
END_ENTITY;
ENTITY employee
SUPERTYPE OF (ONEOF(salaried, hourly));
lastname : STRING;
firstname : STRING;
ssn : INTEGER;
END_ENTITY;
ENTITY hourly
SUBTYPE OF (employee);
rate : REAL;
END_ENTITY;
Notes: The 4 major components of an AP are listed here.
The AAM partially describes the context of the AP. It describes the activities that may be supported by the AP, and serves as a requirements gathering and scoping tool.
The ARM also partially describes the context. It serves as both a requirements discovery mechanism and as a requirements specification mechanism.
The AIM has several functions. It specifies the subset of the IR “vocabulary” used with the AP. It specializes the semantics of the generic data structure and adds constraints, thus providing the exchange specification for the AP.
The mapping table specifies the relationship between the ARM and the AIM. It contains rules and constraints specify the usage of the IRs for the AP. The combination of the AIM and mapping table completely specify the usage of the generic structures for the AP.

## Slide 25: Application Activity Model (AAM)
Information “flows” between activities are the basis for development of the ARM.
Notes: The Application Activity Model (AAM), developed in IDEF0, shows the processes of interest to the AP.
The information flows between activities are used as a scoping mechanism - those outside the scope of interest of the AP are marked with an asterisk. The in-scope information flows serve as the source for information requirements.
The AAM shows information flows at a level of detail that is useful for requirements gathering. The label on each flow indicates a real-world document or parcel of information; the information implied by the flow is broken down or enumerated. This breakdown then serves as a basis for developing the ARM.

## Slide 26: Application Reference Model (ARM)
The ARM specifies information requirements within context set by scope and AAM.
An ARM is documented as an information model.
An ARM is not a model in the sense of a data structure specification.
An ARM is written in the language of the application experts.
  The ARM is the part of an Application Protocol that is most meaningful to users of the standard.
Notes: The ARM captures the information that is most important within the application context.
The developers of the AP determine what the AP must be able to “say”.
ARM may be documented in EXPRESS-G or IDEF1x
The modelling language chosen to represent the ARM is less important than the semantics of the model; the definitions of the objects in the model are therefore the most important and critical aspects of the AP.

## Slide 27: Example: ARM Relationship to Information Requirements
= TRUE
= wall
Notes: This example correlates a fragment of an ARM to industrial requirements, in this case, a building section.
The illustration shows the relationship between an object in the ARM and information conveyed by the drawing. In this example, the “important” information is the fact that the wall is part of a building section (shown), that it has dimensions, and that it is, in fact, a wall.

## Slide 28: Application Interpreted Model (AIM)
ARM is specified in application terminology.
The same requirements must also be specified in standard terminology (an AIM).
AIM is developed through process called interpretation:
  Building blocks are selected from the Integrated Resources.
  Building blocks are specialized and constrained in the AIM.
An AIM is an extended subset of the Integrated Resources
The Integrated Resources constitute a common basis from which the information requirements of all APs are met.
Notes: The requirements documented in an ARM are met through a selection of generic data constructs from the Integrated Resources and the specialization and constraint of these resources to meet the information needs of the ARM.
Bringing IR entities into the AIM preserves the relationships and structure that the entities had in the IRs. Within the AIM itself, the entities may not be modified in any way that changes the data structure in comparison to the IRs. Each entity or its subtype still has the same number of attributes, and the attributes still appear in the same order. Constraints only affect the permissible values of an attribute.
The fact that all APs use the same set of integrated resources means that all APs share the same fundamental underlying structure and semantics. All APs are related through the structure of the integrated resources.

## Slide 29: Example: AIM Fragment
product
product_context
frame_of_reference S[1:?]
product_related_
product_category
product_category
name
description
*id
description
name
discipline_type
product_definition_formation
*of_product
*id
description
application_context_element
name
application_
context
application
frame_of_reference
(INV) context_elements S[1:?]
product_definition
formation
structure_enclosure_
element
product_definition_context
1
life_cycle_stage
frame_of_reference
id
description
property_definition
product_definition_shape
shape_definition_
representation
property_definition_
representation
definition
negative_
component
opening
positive_
component
shape_aspect
product_definitional
description
name
representation
used_representation
definition
products S[1:?]
of_shape
Notes: This EXPRESS-G diagram is a fragment of an AIM. It looks very similar to the IR example schema presented earlier. The only differences are subtypes.
There is a subtype of product_definition called structure_enclosure_element - this subtype would be instantiated in a physical file to represent a wall (which is, after all, a structure/enclosure building element.)
There are two subtypes of shape_aspect -- positive_component and negative_component; negative_component also has a subtype called opening. An instance corresponding to opening would be created for the window in the wall; a window is an opening, which is a negative_component kind of shape_aspect of the shape property of a product_definition, which in this case happens to be a wall.
This complicated and difficult to understand. Its presentation here is intended to provide some idea of how an AIM works and how it relates back to user information requirements.

## Slide 30: Mapping Table
Mapping Table ties the information requirements (ARM) to the exchange specification (AIM).
For each ARM object (and attribute) the mapping table specifies:
  what constructs from the IRs represent that object
  constraints and rules on the constructs from the IRs
Mapping tables are complex and difficult to understand, but are a critical component of the Application Protocol
Notes: The “formal” relationship between the ARM and the AIM is specified in the Mapping Table.
The Mapping Table is the part of the AP that really ties the requirements and the exchange specification together.
The MT lists each application object from the ARM (and any attributes/relationships of the Application Object) and specifies:
  what constructs in the AIM (from the IRs) are used to represent that object; and
  constraints and rules on the data population.
The mapping table is complex and a challenge to understand, but is the critical linchpin within the Application Protocol.

## Slide 31: Example: Mapping Table (simplified)
ARM
AIM
property_definition
where the .description attribute is “load_bearing”
structure_enclosure_element <-
product_definition
product_category.name
where the .name attribute is “wall”
mapped_item
structure_enclosure_
element
structure_enclosure_
element_type
load_bearing
component_
location
Notes: In the example above, the MT shows that the ARM object
structure_enclosure_element
maps to the AP-created AIM object
structure_enclosure_element
which is a subtype of
product_definition
from the IRs.
The fact that the structure_enclosure_element is a wall is represented by the name of a product_category.

## Slide 32: AP Development Process Summary
Integrated Resource Schemas
ENTITY product_category;
name : STRING;
. . .
END_ENTITY;
Application Protocol
AAM
design
make
building_elements
building_element
STRING
type
ARM
AIM
ENTITY product_category;
name : STRING;
. . .
WHERE
name = 'wall';
END_ENTITY.
ARM
AIM
property_definition
where the .description attribute
is “load_bearing”
structure_enclosure_element <-
product_definition
product_category.name
where the .name attribute is “wall”
mapped_item
structure_enclosure_element
structure_enclosure_element_
type
load_bearing
component_
location
Mapping Table
Interpretation
Notes: This diagram provides a summary of the AP development process.
The information flows in an AAM lead to information objects in the ARM.
The interpretation process identifies IR objects that correspond to ARM requirements An express AIM is created that includes a subset of the IRs and specializations of those constructs.
The correlation between the ARM and the AIM is documented in a mapping table.
The mapping table provides guidance on the usage of AIM constructs within that application.

## Slide 33: Summary of STEP Architecture Advantages
Provides a unique and innovative solution to data exchange requirements.
Incorporates the rich semantics and constraints of individual application domains.
Maintains a limited, generic, reusable set of data constructs as an exchange mechanism.
Notes: The STEP architecture provides a unique and innovative approach to solving data exchange requirements.
STEP incorporates the rich semantics and constraints of individual application domains while maintaining a limited, generic, reusable set of data constructs as an exchange mechanism.

## Slide 34: Back-up Slides
Part 21 Comparison Details

## Slide 35: How the Data was Generated
Both sets of data were auto-generated starting with a hand-written AP224 ARM physical file describing a block with one feature, a 12.7 millimeter hole in the top.
The ISO 14649 data file was produced by:
  Inputting the ARM224 file to FBICS and having it output an ALPS Part21 workstation-level process plan and associated data.
  Inputting the ALPS plan and associated data to the alps2stepnc translator I wrote and having it output an ISO14649 Part 21 file.
The AP238 data file was produced by:
  Inputting the ARM224 file to FBICS and having it output a Parasolid file.
  Inputting the Parasolid file to the STEP Tools Parasolid-to-AP203 service and having it output an AP203 file.
  Inputting the AP203 file to the STEP Tools ST-Plan system and having it output an AP238 plan file.
Notes: Both sets of data were generated automatically. The generation path of both sets of data starts with an ARM224 Part 21 file I wrote by hand describing a block with a one feature, a 12.7 millimeter hole in the top.
The file containing the ISO14649 data was produced by:
Inputting the ARM224 file to FBICS and having it output an ALPS Part21 workstation-level process plan and associated data.
Inputting the ALPS plan and associated data to the alps2stepnc translator I wrote and having it output an ISO14649 Part 21 file.
The file containing the AP238 data was produced by:
Inputting the ARM224 file to FBICS and having it output a Parasolid file.
Inputting the Parasolid file to the STEP Tools Parasolid-to-AP203 service and having it output an AP203 file.
Inputting the AP203 file to the STEP Tools ST-Plan system and having it output an AP238 plan file. This was done by Martin Hardwick.
The ISO14649 data has not been modified.
The AP238 has data has been modified (1) to compact it by eliminating redundant copies of #58 and #495 and unnecessary newlines so that the two data sets are at roughly the same level of compaction, and (2) to get the drill data to match the ISO14649 data.

## Slide 36: Benefits as measured for AP-238
Build Anywhere using STEP-NC data
  Milling, Turning, Wire EDM, Fabrication, inspection others anticipated
  Any supplier, any machine with the required resources
Other Benefits
  Elimination of 4,500+ post processors
  Safer, more adaptable machine tools
  Out-source quality control
  Reduce costs
Manufacturing
STEP-NC CNC
Design
STEP*
CAD
35% faster
programming
(Lockheed)
50% faster using better machines
(Cincinnati Machine)
CAM
Planning
AP-238
75% fewer drawings
for shop floor
(Raytheon)
Can we get these
benefits if we replace
AP-238 with the
simpler ISO 14649
model?
*STEP can be AP-203 ed1, AP-203 ed2 or AP-224