## Slide 1: JPL and STEP-NC
A Work in Progress
W. Darrol Houser Jr
Group Supervisor
Jet Propulsion Laboratory,
California Institute of Technology
CL#03-0466

## Slide 2: Where We Started
FADAL VMC with a 32MP controller
  486 processor
  Windows 95 operating system
  32 meg ram
  640 x 480 screen resolution
  Gibbs SFP (shop floor programming)

## Slide 3: Where Are We Now
No change in machine hardware
Updated the computer side with;
  AMD K6 2 400mhz
  Windows 98se (Windows XP Pro pending)
  256 meg ram
  800 x 600 screen resolution (new adapter pending)
  Full seat Virtual Gibbs nlo (network license option pending)
  Internet capable

## Slide 4: Costs
Costs to date
  New motherboard (OEM upgrade) $3000
  256meg ram (72 pin 64 meg simm’s 4@ $29.99) $120
  New OS $199
  Network card $39
  CD Rom drive $19
  New Video adapter $?
  Labor 10 hours @ $78.00hr $780

## Slide 5: Machining Process
Traditional multi-axis method
  Program time 105min
  Setup time 90min
  Run time 16.5min
Step-NC multi-axis method
  Program time 12min
  Setup time 90min
  Run time 23min

## Slide 6: Challenges For JPL
Model fidelity #1 issue
ST-Plan, Who and When
Initial origin location from ST-Plan to ST-Machine as viewed from the machine
Incorporating JPL’s machining strategies for consistent and repeatable results
Completing machine upgrades
Continued funding for development