## Slide 1: AP-238 Direct Interface
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
JPL Demonstration
David Loffredo
loffredo@steptools.com

## Slide 2: AP-238 Direct Interface
We are building a library of STEP-NC access and calculation code to simplify programming directly against AP-238.
  Can use from detailed C++ applications or from lightweight COM/VB applications.
  Called STIX, for STEP Index
Advantages
  Start writing applications against AP-238 quickly and from different environments
  Take care of most common access paths and calculations.
  Allows more geometric calculation than possible with EXPX.
  Allows for update path to modify AP-238 data.

## Slide 3: AP-238 Direct Interface
AP-238
Part 21
Tool Kit layer
Index Layer
Application
AP-238
Part 21
Tool Kit layer
Mapping
Layer
Tool Kit layer
Application
XML
Tool Kit layer
Application
ST-Developer
EXPRESS-X
CEB Part 28
DOM
ST-NC Developer
(STIX, ST-Plan,
ST-Machine,
ST-ACIS/Parasolid
ST-Developer)
NEW
OLD
Good for Prototyping
New Method
  Enables Updates
  Smaller footprint
  Easier to maintain
  More sophisticated functions.

## Slide 4: STIX — STEP Index
COM
Shell
  Wrap with COM interface for lightweight applications.
Provide a direct interface to the AP-238 data.
AP-238
Data
Traditional AIM Code
Application
Index
  Read and build in-memory indices and backpointers on the AP-238 data for speed of processing.
STIX
C++ API
  Simplify use of AP-238 data by providing API to common access paths and calculations.

## Slide 5: STIX — Expansion
Continue to add value by expanding services
  Add geometric processing ability via ACIS/Parasolid kernel interfaces.
  Additional validation, creation, update, and other useful application services.
AP-238
Data
STIX
C++ API
Index
COM
Shell
Geometry
Kernel
Validation
Application

## Slide 6: Properties and Relationships
setup info
Feature
Feature
Components
Path, Profile,
Taper, Bottom
placement,
orientation,
face geometry,
and other
parameters
component
parameters
Project
Workpiece
Workplan
Functions to access major concepts, relations, and parameters
  No longer need to be an AIM expert to do something useful.
  Even AIM experts will find this saves time. Already traverses through the property definitions, reps, rep items, etc.
Workstep
machining params
stock, shape,
material, other
parameters
Tools
tool characteristics
setup

## Slide 7: You Avoid Having to Learn This:
The Feature
complex instance
of instanced_feature
and round_hole
shape definition
representation
shape representation
with parameters
product definition
shape
axis_placement_3D
name = “orientation”
The Depth
path_feature_component
description = “linear”
shape definition
representation
shape representation
with parameters
property definition
length_measure_with_unit
name = “distance”
value = 100 mm
feature
component
definition
product
definition
shape
shape defining
relationship
shape
aspect
property definition
representation
direction shape
representation
direction
axis_placement_3D
Round Hole Depth

## Slide 8: STIX Example
Print a simple report
  Test harness during development
STEP-NC Index Contents Report ------—
------------------------------
Projects: 1 present
[0] name = 1 (id #184)
workplan = machining operations (id #75)
------------------------------
Setups: none
------------------------------
Workpieces: 2 present
[0] name = 1 A A (id #171)
shape = advanced_brep_shape_representation (id #633)
shape length unit = millimetre
stock = <no-name> A A (id #173)
stock length unit = millimetre
stock min/max X = 0 / 125 (125)
stock min/max Y = 0 / 75 (75)
stock min/max Z = 0 / 50 (50)
[1] [ . . . the stock . . . ]
#include "stix.h”
main() {
StixNC stepnc;
stepnc.load (argv[1]);
stepnc.dump_report();
}

## Slide 9: STIX Example (continued)
Report writer
------------------------------
Root Workplan: workplan machining operations (id #75)
1 elements
setup = none
[0 - 1] workplan Drill-2 (id #76)
1 elements
setup = none
[0 - 1] workingstep drilling (#46)
parent = Drill-2 (#76)
description = Drill-1-Micro-1-Hole-01
operation type = Drilling (drilling_operation)
property = security plane
property = retract plane
property = cutting depth
tool: type: 12.7000 mm TWIST_DRILL (id #32)
name: TL DRILL-2
diameter: 12.7
edge (flute) length: 21.1845
edge radius: 0
circumference angle: 0
technology (#19)
property = spindle
property = cutspeed
functions (#11)
property = coolant
in-process feature = round hole (#145)
final feature = round hole (#145)

## Slide 10: STIX Example (continued)
Report writer
------------------------------
Features: 2 present
[0] round hole (id #145)
feature faces: #423 #422
sar 0 name=[hole depth] desc=[path feature component usage]
linear path desc=[linear] ed_desc=[hole depth occurrence]
sar 1 name=[diameter] desc=[profile usage]
closed circular profile desc=[boundary] ed_desc=[diameter occurrence]
sar 2 desc=[hole bottom usage]
unrecongized aspect desc=[conical] ed_desc=[bottom condition occurrence]
feature depth: 25
feature orientation:
x-axis: 1 0 0
y-axis: 0 1 0
z-axis: 0 0 1
origin: 100 40 25
------------------------------
Tools: 1 present
[0] type: 12.7000 mm TWIST_DRILL (id #32)
name: TL DRILL-2
diameter: 12.7
edge (flute) length: 21.1845
edge radius: 0
circumference angle: 0

## Slide 11: Advanced Calculations
Can perform geometric calculations more easily.
  Switching axes and applying transforms,
  Calculating geometric bounding boxes and extents
  Providing parameters in preferred units
Calculating
extent of
material
Stock
Workpiece
X  Z
Y  X
Z  Y
Permuting axes
for slots

## Slide 12: Moving Forward
STIX
COM
Application
Indexing
Interface
Concept Library
data
COM API functions for the STEP-Manufacturing Application Protocols
  Foundation for next generation of manufacturing automation
  Necessary as we go for the next level of optimization
  API for machine independent CNC control data
    Milling, Turning
    Inspection, Robotics