## Slide 1: THE PARAMETRIC EVALUATOR & ADVANCED INTEGRATED MATHEMATICAL SYSTEM A Brief Overview & NC Application
Tom Melson
Boeing Technical Fellow
IDS, Information Technology
Copyright Unpublished – 2003
All rights reserved under the copyright laws by The Boeing Company
Notes: 1
1
1

## Slide 2: This Presentation of The Parametric Evaluator (PE) and Advanced Integrated Mathematical System (AIMS) is for Information Purposes. It is Not an Endorsement of Any Specific Effort Regarding Automated-NC. However, it Does Propose the Use of the PE and Other AIMS Operating Concepts in All Automated-NC Efforts.
NOTICE
Notes: 1
1
1

## Slide 3: PROBLEM
Transferring High-Precision Complex Curves and Surfaces from the Defining System to Down-Stream Applications and Using them in those Applications without Change/Approximation
SOLUTION
The PE and AIMS Type Processing of Geometry
  In Major Production Use since 1970s

## Slide 4: PRESENTATION TOPICS
Curve and Surface Types
  Explicitly Defined
  Procedurally Defined
The Parametric Evaluator
  Standardization of Curves and Surfaces without Changing the Mathematical Forms of the Existing Definitions
The Advanced Integrated Mathematical System
  Concepts
  Brief History
AIMS/PE in Down-Stream (After Design) Applications

## Slide 5: CURVE AND SURFACE TYPES
Many Mathematical Ways to Represent Curves and Surfaces
  Analytic
  NURBS/Rational Parametric Polynomials
    Limiting but Mathematically Simple and Explicit (Parametric Formula). One Size Fits All Approach - Can Compromise Purity and Exactness of Shape.
  Procedures
    Not Limiting but Mathematically Complex. Usually Many Systems of Non-Linear Equations all Interrelated to Produce Implicit Definition of Curve or Surface. Captures Purity of Shape; no Approximation. Usually no Explicit Formula or Parameterization.
  Others

## Slide 6: EXPLICIT FORMS - EXAMPLES
Rational Parametric Polynomial Curve - Powers Basis
NURBS Surface
Non-Rational if D=1, Identically

## Slide 7
CONSTANT OFFSET SURFACE
Base Surface
Procedural
Offset Surface

## Slide 8: PROCEDURAL SURFACE EXAMPLE
Constant Offset Surface
Functional Offset Surface
Real Space Functionalization of Offset, e.g.,
Taper n-to-1 in Specified Direction

## Slide 9
AIMS SHADOW SURFACE (PROCEDURAL)
Obstructing Surface
Receiving Surfaces
Shadow Surfaces

## Slide 10
SHADOW SURFACES ON CONSTANT
& FUNCTIONAL OFFSET SURFACES

## Slide 11
SHADOW SURFACES ON CONSTANT
& FUNCTIONAL OFFSET SURFACES

## Slide 12
SPINE CONTROLLED CONIC SURFACE
USING DEPENDENT CURVE AND SURFACE
Three-Point/Two-Slope
Conic Surface
Position and Tangent
Continuos With Surface
Base Surface and
Trim of Base Surface
Slope Control
( Plane)

## Slide 13
CONVENTIONAL CONTROL-LINE LOFT SURFACE
(Procedural Definition)
Conic Elements
Three Point/Two Slope
Control Curve 1
Control Curve 3
Independent
Slope Function 2
Independent
Slope Function 1
Control Curve 2
Conic Surface
Element (Typ.)

## Slide 14: PROCEDURAL SURFACE EXAMPLE
Conventional Control-Line Loft Surface (Simple Form) - Conic Example
Similar for Conventional Loft Cubic, Ruled, Etc.
Conic Curve (Element)
Implicitly (very)
Conic Surface (NOTE - Not Parametric)
(Defined by Simultaneous Solution
of Systems of Non-Linear Equations)
(Identity Matrix System)

## Slide 15: AIMS/PE
Many/Limitless Curve & Surface Definitions (Invent Your Own), but How
to Have this Flexibility and Still Maintain Control?
The Parametric Evaluator
  Method of Standardization Without Change/Approximations
  Provides a Single Generic Mathematical Representation for Curves
  Provides a Single Generic Mathematical Representation for Surfaces
  Trim/Faces/Solids - Topology
The Advanced Integrated Mathematical System. Generic Mathematical Operations System Based on PE Standardization, Plus…
  Surface/Surface Intersection
  Minimum Distance from Point to Surface
  Analysis
  Curve and Surface Creation
  Data Exchange
  Database Functionality
  Etc.

## Slide 16
Generic Curve Representation
Generic Surface Representation
Notes: 10
10

## Slide 17
AIMS PE
AIMS/PE CONFIGURATION
AND DOWN-STREAM APPLICATION SUPPORT
PE Interface
AIMS
Processing
Operations
*
External
PE 1
External
PE 2
External
PE n
AIMS-Based
Down-Stream
Applications
*
AIMS
Model &
Database
*
Metrology
Advanced Curve & Surface Creation
Optics Analysis
Laser Beam Analysis
Computational Fluid Dynamics
Data Exchange
Special CAD Functions
Others

## Slide 18: AIMS - INTERNAL TO MCDONNELL DOUGLAS CORPORATION (MDC) (Brief History)
AIMS/PE Invented and Developed at MDC to Unify MDC’s CAD/CAM Systems Without Laborious and Error-Prone Redefinitions, Changes, Translations, Approximations, Etc. (CADD, CALL, MDCAPT, Etc.)
  Began Development in Early 1970s
  First Production Implementation in 1975 with Basic Functionality
  All Production Curves and Surfaces Operational by 1977
  Implementation Into Corporate-Wide APT Systems in 1978 (CAM)
  Implementation Into All Major MDC CAD/CAM Systems by Early 1980s
  First Publicly Released Presentation; January 1984. Tom Melson, CAM-I, Tucson, AZ

## Slide 19: AIMS - WITH CATIA (Pre V5)
Product Defined External to MDC in CATIA (Mid 1980s)
Bring Product Definition into MDC’s CAD/CAM Systems for Processing (Analysis, Machining, Etc.)
CATIA Geometry not Directly Mappable to MDC Specific Mathematical Definitions. Would Need Approximations.
CATIA Geometry to become Applicable to AIMS/PE Base of MDC’s CAD/CAM Systems
Agreement with Dassault Systemes for Software Development of CATIA PE, Access to CATIA Geometry Model and Specific Utility Procedures, All per MDC/AIMS Developed Specifications.

## Slide 20: AIMS - WITH CATIA (Cont.) (Pre V5)
Dassault Systemes Delivered Software per Specifications
Product Transferred to, and Processed in, MDC’s CAD/CAM Systems using AIMS/PE with Dassault Systemes Software (CATIA PE) Callable Under the AIMS PE; i.e., CATIA Surfaces Viewed as Just Another Subtype in the AIMS PE.
Exact Product Definition Processed in MDC’s CAD/CAM Systems
  Used Exact Mathematical Definition as Defined in CATIA
  No Translations or Approximations
  Used same Software for Evaluation as CATIA. Implies same Mathematical Algorithms and Same Procedures for Executing the Algorithms. Thus, Exact Same Results of Evaluation.
  Continued use of CATIA PE

## Slide 21: AIMS - WITH NORTHROP
Product Defined both Internal and External to MDC (Mid 1980s)
  MDC Systems (CADD/CALL); Unique Curves and Surfaces.
  Northrop Systems (NCAD/NCAL); Unique Curves and Surfaces.
Must Exchange and Process Product Definition between MDC and Northrop
Both MDC and Northrop CAD/CAM systems are PE based
Product Transferred between MDC and Northrop and Processed in each others CAD/CAM Systems using PE Technology; Two way Transfer.
No Translations or Approximations.
Continued use of PE Today between Boeing and Northrop Grumman

## Slide 22: AIMS - WITH PROENGINEER
Visits to Parametric Technology in 1989
  ProEngineer Processed MDC’s Geometry Using PE

## Slide 23: AIMS - WITH UNIGRAPHICS/PARASOLID (EDS)
MDC Transitioning to Commercial Modeler (1989)
Large Amount of Legacy Geometry; Procedural and Parametric
Unigraphics/Parasolid not PE-Based at that Time
Combined Effort between MDC and EDS (Early 1990s)
  Unigraphics and Parasolid to become PE-Based
  Provide Data Structures and Interfaces for Foreign Geometry using AIMS/PE Technology as a Guide
  Foreign Geometry Functionality Released in Unigraphics V9 with AIMS PE Operational
  All MDC Legacy Procedural Surfaces Transferred to and Available in UG/Parasolid Without Translation or Approximation of the Mathematical Forms

## Slide 24: AIMS - WITH UNIGRAPHICS/PARASOLID (Cont.)
Current Unigraphics/Parasolid-AIMS used Extensively on Boeing & Heritage MDC Products at Boeing/St. Louis and with Partners, Suppliers, Etc.
Foreign Surfaces Fully Functional in Unigraphics/Parasolid. Foreign Surfaces and Unigraphics Native Surfaces can be Mixed with no Restrictions in a Parasolid Body Definition.
AIMS/PE Delivered by EDS to Boeing Authorized Users with each Unigraphics Release

## Slide 25
FOREIGN GEOMETRY IN UNIGRAPHICS
(Without Translation or Approximation – AIMS/PE Interface)
Notes: <header>
<date/time>

## Slide 26: AIMS - WITH CATIA V5
Boeing/CATIA/AIMS
  CATIA V5 & AIMS are Extremely Compatible Systems
  CATIA V5/AIMS Interface Workshop; Paris, June, 1999
AIMS Interfaced with CATIA V5 and Working

## Slide 27
AIMS-DEFINED PROCEDURAL SURFACES IN CATIA V5
(CATIA V5/AIMS Interface Workshop - Paris/June 1999)

## Slide 28
AIMS ACCESS TO OTHER SYSTEMS
(Bi-Directional Communication & Functionality)
AIMS PE
External
PE 1
External
PE 2
External
PE n
CAD/Solids
Modeling
Systems
PE API
AP
I
AIMS
Applications
*
AP
I
*
Metrology
Advanced Curve & Surface Creation
Optics Analysis
Laser Beam Analysis
Computational Fluid Dynamics
Data Exchange
Special CAD Functions
Others

## Slide 29: AIMS SUMMARY
In Addition to Standards, Not Instead of Standards
Contains Parametric Evaluator
  Standardization of Curves and Surfaces (Solids)
Generic Mathematical Operations Based on Standardization Provided by Parametric Evaluator
Interfaces to Commercial CAD/Solids Modeling Systems
Database Functionality
Data Exchange Functionality
Modular Components/Plug-and-Play Architecture
Can be Used in CAD Systems Environment and Subsequent Down-Stream Applications. Designed to:
  Eliminate Translation and Approximation of Geometry/Solids Representation when Used in Down-Stream Applications
  Allows Advanced Processes to be Defined in CAD Systems and Transferred to, and Used by, Down Stream Applications Exactly as Defined in CAD System, e.g., Metrology Operations

## Slide 30
FOREIGN PROCEDURAL SURFACES IN CATIA V5
(Without Translation or Approximation - AIMS/PE Interface)

## Slide 31
Procedural Offset Surfaces
Defined by CATIA
OFFSET OF FOREIGN PROCEDURAL SURFACES IN CATIA V5
(AIMS/PE Interface)

## Slide 32
AIMS SHADOW SURFACE IN CATIA V5
(AIMS/PE Interface)

## Slide 33: DOWN-STREAM APPLICATIONS
Some Down-Stream Applications
  Metrology
  CAM
  Analysis
    Optics
    Electromagnetic
    Computational Fluid Dynamics
    Etc.
  Others
AIMS-Based Down-Stream Applications
  Designed for Use of Exact Mathematical Definitions from Defining Systems
  Transfer of All Critical Data from Defining Systems to Down-Stream Applications and New Data Back to Defining Systems and Other Databases
  Generic Mathematical Operations Based on PE. Will use NURBS if Specific PE is not Available.

## Slide 34: PROPOSAL
Demonstrate STEP-NC Prototype Using STEP Tools, Inc., Software with
  AIMS/PE
  AIMS Model Containing a Generic Part with Complex Procedural Surfaces as Defined in CAD System
  AIMS Geometry Kernel and Application Program Interface (API) for Accessing the Model and Providing Parametric Evaluation of the Geometry.

## Slide 35
GENERIC PART WITH PROCEDURAL SURFACES

## Slide 36
Commercial Metrology Software Systems
CATIA V5
UG &
OTHERS
CMMs &
OTHER H/W
LASER
TRACKERS
LASER
SCANNERS
PHOTOGRAMMETRY
SYSTEMS
AIMS METROLOGY KERNEL
CAD / SOLIDS MODEL DATA
DIGITAL MEASUREMENT PLAN
CLOSEST POINT CALCULATION
AIMS MODEL, ETC
Application Program Interface (API)
Enterprise Process Capability Database
METROLOGY & CAD SYSTEMS INTEGRATION
Via AIMS-Metrology
Direct Hardware
Interface
(Same Look & Feel but with Added Functionality)
Statistical Reports
Charts & Graphs
AIMS-CAD
Interfaces