## Slide 1: Build Anywhere using STEP-NC
Martin Hardwick
David Loffredo
Blair Downie
info@steptools.com
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: Build Anywhere Vision
“Enable the same price and quality competition for manufactured/custom parts as currently exists for off-the-shelf/purchased parts.”
Using machine independent CNC control files
3D manufacturing features
Inspection quality tolerances
Product and process data

## Slide 3
Contouring
Milling, Drilling,Turning
EDM

## Slide 4: Problems in current method
Current process is inefficient
  Design sends incomplete data
  Manufacturing makes fixes but does not document them
  End result is a control file that can only run on one machine at one supplier
  RS274D is more than 40 years old
Extensive CMM to check the geometry of as-built parts
Incomplete
Information
Partial
geometry
with “issues”
Undocumented
fixes added
Machine specific control
file that works only if
all conditions correct
Machine specific
translator
Processing information is lost
Design
Manufacturing
Detailing and Path Planning
Post
IGES
CAD
CNC Control
RS274D
CAM
CL File

## Slide 5: Current NC programming using RS274D
%
N05 G54
N10 G00 Z10.000
N15 G91 G0 Z200
N20 T5 D1 WW
N30 G90 M5
N35 G00 X0.000 Y-150.000
N40 G00 Z5.000
N45 M08
N50 S3183.000
N55 M03
N60 F1477.000
N65 G00 X60.000 Y-150.000
N70 G00 Z5.000
N75 G00 X60.000 Y-150.000
N80 G01 Z-0.500
...
machine-specific part program with axis data generated by a postprocessor
vendor-specific extensions of the original standard
only primitive motion and switch commands
no standardized data format for spline processing and sophisticated NC technology
Courtesy WZL RWTH Aachen
STEP-NC replaces this with a
rich, integrated data format
Ideal for Paper Tape!
The standard for 40 years!

## Slide 6: STEP-NC is machine independent
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 7: Key feature of STEP-NC
STEP-NC describes “what” not “how”
  Make this geometry from this stock
  By removing these features
  In this order
  With these tolerances
  And tools that meets these requirements
The old standard described “how”
  Move tool to this location
  Move tool to this location
  And so on for millions of commands

## Slide 8: STEP-NC at NASA JPL
Rapidly manufacture AP-238 models
  Focus on making ordinary parts on multi-axis machines
  Default tolerances and finishes set using Crib sheets
  Allow ordinary machinists with little CAM training to be competitive with experienced machinists with extensive CAM training
ST-Plan
Planning
Fadal CNC with
GibbsCAM and
ST-Machine
STEP-NC Control
Modeling
AP-203
AP-238
Pro/E
Detailing
Complete
Model
Required
Wizard to define
Tolerances
Features
Processes &
Tool Requirements
Machine
Independent CNC Control File
What are
the
benefits?

## Slide 9: Benefits of STEP-NC
Build Anywhere STEP-NC data
  Elimination of 4,500+ post processors
  Safer, more adaptable machine tools
  Out-source quality control
  Process savings as follows
Manufacturing
STEP-NC CNC
Design
STEP*
CAD
35% faster using 3D
feature recognition
(Lockheed)
50% faster using better machines because
no single stepping
required
(Cincinnati Machine)
CAM
Planning
STEP
NC**
http://www.stepnc.com
75% fewer drawings
because electronic
data can be read by
browsers
(Raytheon)
*AP-203 ed1, AP-203 ed2 or AP-224
** Must be AP-238

## Slide 10: Progress since last IRB meeting
Processing Rectilinear parts
  If solid model geometry has no issues
Tools will soon be working on the desktop
  No longer have to use web site to get STEP-NC data
  Extensive suite of viewing and checking tools
  Implementing the STIX access and interface library
Learning about Optimization
  Design Tolerances exported from FB Tol to AP-238
  Manufacturing Tolerances from JPL crib sheet
  Prototyped Integration with JPL Cribmaster
  Beginning to understand how to compile STEP-NC data

## Slide 11: STEP-NC Compilation
Optimization Heuristics
  Fold operations that use the same tool together
  Fold operations that use the same axis together
  Machine steps from shallowest side
  Eliminate unnecessary operations
  Remove material in shallowest first order
  Avoid regions
    Use one face regions only

## Slide 12: STEP-NC Implementation Program
Implementation program participants show STEP-NC can be used to make production parts
  Round 1 2.5D feature milling 6/1/02 to 11/30/02
  Round 2 Surface milling 12/1/02 to 5/31/03
  Round 3 Casting 6/1/03 to 11/30/03
  Round 4 Probing 12/1/03 to 5/31/04
Round 2 goals
Minimize air milling
  Exploit direct geometry access provided by STIX
  Suggest changes to standard as necessary
Continue optimization
  New heuristics
  Exhaustive search
  Integrate tolerances and surface descriptions into algorithms
Start processing surfaces
  Definition in planning system
  Processing on the control
Make more robust
  Test using more models
  Improve user interfaces
  Interoperability

## Slide 13: What next – demonstrate interoperability
Expand range of translators
Divide into A and B
  A = build anywhere AP-238 file (AP-224 features)
  B = machine specific AP-238 file (14649 features)
CATIA
AP-238
Unigraphics
Pro/E
Mastercam
GibbsCAM
Esprit
Actual implementations depend on the Pilot Projects
All are A_In and B_In.
But which are
A_Out or B_Out?

## Slide 14: Conclusion – the ongoing achievement
The next step is CAM and CNC systems
and SIGNIFICANT process savings
There are more than one million STEP enabled CAD stations in the world

## Slide 15: Backup

## Slide 16
Initiative: OPTIMAL &
MATRAS project
Korean
STEP-NC
American
Super Model
European
STEP-NC
IMS STEP-NC
Japanese Digital Master
Interest Group
Standardization
TC184/SC1&4
ISO14649/10303
Milling
Turning
EDM
Contour cutting
Rapid Prototyping
Inspection

## Slide 17: Who we are
Mission: Use STEP to make the development of production processes more time and cost efficient
  35% reduction in process planning time
  50% reduction in system costs
  75% reduction in time to prepare RFQ’s
Forerunners in STEP technology since 1991
  Founders working on product data since 1978
  First commercial software tool kit
  First solid model data exchange using STEP
  Software in >500,000 CAD stations
Contributors to STEP and STEP-NC
  Owner of Parts 14, 21, and 28 of STEP
  Editor of AP 238 (STEP-NC)
  Team leader of ISO TC184/SC4 Wg3/T24 STEP-Manufacturing

## Slide 18: Some Customers
Enterprises
Aerospatial
Boeing
British Aerospace
DaimlerChrysler
EDF
ESA
Ford
General Dynamics
General Electric
General Motors
Hitachi Zosen
IBM
Lockheed Martin
NASA
Newport News
Peugot
Raytheon
Samsung
Toyota
CAD Vendors
  SGI Alias, Bentley, Unigraphics, CADKEY, Cimatron, HZS, Entity Systems (Alibre), Intergraph, Spatial
CAE Vendors
  Tecnomatix, Deneb
PDM Vendors
  IMAN, Boeing DCAC/MRM (Metaphase)
CAM Vendors
  Bridgeport Controls, DelCAM, Licom, Fanuc Robotics, Mastercam, GibbsCAM, Esprit

## Slide 19: Role of STEP-NC
Manufacturing
Design
35% faster
(Lockheed)
50% faster using better machines
(Cincinnati Machine)
Operation
Planning
75% fewer drawings
(Raytheon)
Feed Forward
Intelligent Control
Data
Feed Back
Intelligent Kinematics &
Behavior Data
STEP-NC
HIPPEE

## Slide 20: AP-238 or ISO 14649?
ISO 14649 is an object model for STEP-NC
  Many important associations between the features, geometry and tolerances are not in the 14649 model but are in AP-238.
  Convert AP-238 to 14649 using a two stage post
    1. Compute machine specific setup (axes, origin etc)
    2. Summarize and delete feature and geometry relationships
CAM
Post 1
Post 2
CNC 1
CNC 2
X
Not possible for 14649 controllers
AP-238
AP-238
14649
14649
Reading AP-238 directly into the controller is a better solution

## Slide 21: Simplified illustration
14649 does not contain the solid model geometry
  careful calculation is required to flip the part
AP-238 does contain the solid model geometry
  Point, click and flip to rotate the part
A
B
C
D
H
X’
Y’
A’
B’
H’
#20 = Pocket (H, D, B, A, C)
#20 = Pocket (H’, D’, X’, Y’, C’)

## Slide 22: ST-Plan
ST-Plan creates machine independent CNC control files
  Tolerance definition
  Feature recognition
  Process sequence definition
  Tool requirement definition

## Slide 23: ST-Machine
ST-Machine generates tool path data
  Optimizing compiler for STEP-NC
  Machine independent data converted to machine specific tool paths
  CAM system plug-in
  Use On or Off the CNC
Non-optimizing
version is on
web site
Optimizing
version in process

## Slide 24: ST-NC Implementation Package
STEP-NC for legacy databases
  Translate data to STEP-NC
  Evaluate portability and cost savings
  Test and deploy the new process
Engineer
System
Avail
N/A
Alex Lipatov
GibbsCAM
1
1
Jeff Young
Mastercam
1
1
Blair Downie
CATIA
0
2
David Loffredo
2
Esprit
Unigraphics
Pro/E
Legacy Store
STEP-NC
File
Translate
Evaluate
Quality

## Slide 25: Testing Site
There are about 65,122 small manufacturing enterprises using about 500,000 CNC machines.
Upload STEP or STEP-NC files
Esprit Plug-in soon!
Optimizing compilers will not be free
http://www.stepnc.com
GibbsCAM
ST-MachineTM
Mastercam
ST-MachineTM
ST-PlanTM
On-line
STEP-NC
Compilation
Convert AP-203
to AP-238
STEP-NC
Compilation

## Slide 26: ST-NC Developer
Write manufacturing applications and translators
  Make or use the Machine independent CNC control data
  ST-Plan desktop translator with feature recognition to make data
  STIX Programming API with links to ACIS and Parasolid
  Viewers, checkers and ST-Machine harness
ST-Plan
AP-203
Viewer & checker
ST-Machine
harness
ST-ACIS Library
or ST-Parasolid
AP-238
New Translator
New Translator
Included in package
STIX

## Slide 27: AP-238 Direct Interface
AP-238
Part 21
Tool Kit layer
Index Layer
Application
AP-238
Part 21
Tool Kit layer
Mapping
Layer
Tool Kit layer
Application
XML
Tool Kit layer
Application
ST-Developer
EXPRESS-X
CEB Part 28
DOM
ST-NC
Developer
NEW
OLD
Good for Prototyping
New Method
  Enables Updates
  Smaller footprint
  Easier to maintain
  More sophisticated functions.

## Slide 28: The STEP Index (STIX)
COM API functions for the STEP-Manufacturing Application Protocols
  Foundation layer for next generation of manufacturing automation
  Necessary as we go for the next level of optimization
  API for machine independent CNC control data
    Milling, Turning
    Inspection, Robotics
STIX
COM
Application
Indexing
Interface
Concept Library
data